## Slide 1
e+ target:
Cooling by thermal radiation
Felix Dietrich, Alexander Ignatenko, Sabine Riemann (DESY),
Andriy Ushakov (Hamburg U), Peter Sievers (CERN)
Outline
  Status
  Temperature distribution
  Mechanical issues
  To-Do

## Slide 2: Expected target load in the first ILC years
Running scenario H-20
  1326 bunches per pulse during first years
    start with Ecm=500GeV (500fb-1),
    followed by Ecm=350GeV (200fb-1); and
    Followed by 250GeV (500fb-1);
  Luminosity upgrade
    3.5 ab-1 at Ecm=500GeV
    1.5 ab-1 at Ecm=350GeV
   During first 8 years Edep ≤ 5kW
Ebeam [GeV] | Edep [kW] | DTmax/pulse [K] |  | dpa | Edep [kW] | DTmax/pulse [K] | 
 | Nominal luminosity |  |  |  | High luminosity |  | 
120 | 5.0 | 66 | 0.035 |  | - |  | -
175 (ILC EDMS) | 3.9 | 125 | 0.06 |  | - |  | -
250 (ILC EDMS) | 2.0 | 130 |  |  | 4.1 |  | 195
250 | 2.3 | 85 | 0.05 |  | 4.6 |  | 128
A. Ushakov,
Update 2015/16
A. Ushakov, 2015
Edep ≤ 5kW

## Slide 3
Ti6Al4V
Radiator
Cooler
photons
Radiative cooling model
e+ target located close to FC
Rotating wheel consists of Ti rim (e+ target) and Cu (radiator)
Heat path:
  thermal conduction Ti  Cu
  Thermal radiation from Ti and Cu to stationary water cooled coolers
Target, radiator and cooler are in vacuum
Radiating area can be adjusted by fins
Goal:
keep target temperature
below failure
of Ti6Al4V
vated temperatures?
Felix Dietrich
Sketch, no technical drawing!

## Slide 4: Temperature development in target +radiator
200 400 600 800 1000 1400
T [C]
FEM to calculate temperature evolution in real model; here ‘estimation by hand’
Material parameters c, l, e depend on temperature and long-term load
heating due to
energy deposition
Thermal conduction
through material
Radiation from
surfaces
K.C. Mills, 2002,
Recommended Values of
Thermophysical Properties
For Selected Commercial
Alloys, p. 217,
referenced by J. Yang
Specific heat [J/(kg K)]
Thermal conductivity [W/(m K)]
200 400 600 800 1000 1400
T [C]
Ti6Al4V
c( 20C) = 0.545J/(gK)
c(500C)= 0.650J/(gK)
l( 20C) = 0.065W/(m K)
l(500C)= 0.126W/(m K)
Edep from photons
(depends on Ecm)

## Slide 5: Target wheel heating to equilibrium
Mass of target wheel
  Ti rim (assume height of 4cm)  ~11kg
  Radiator weight depends on # of fins, O(100kg)
      Energy stored in target wheel ~O(MJ)
Temperature evolution in rim and radiator
  Neglecting thermal radiation
    It takes ½ hour to heat 100kg Cu with 5kW to 200C
    It takes few minutes to heat 11kg Ti with 5kW to 300C
  Taking into account thermal radiation and time for heat transfer to radiator, few hours needed to achieve
Heat transfer Ti rim to radiator:
  slow due to low thermal conductivity  accumulation of heat load to Tmax over many pulses
  heat dissipates only 5mm within 6s (after ~6-7seconds the beam hits the same rim area)
   Ti rim remains hot

## Slide 6: Equilibrium temperature in the target
Transient analysis of average temperature, ANSYS
Ecm = 500GeV;
Edep = 2.3 kW
Radiator area ~2.3 m2
After ~3 hours equilibrium temperature distribution reached
Temperature in Cu (near Ti) ≈250°C
Felix Dietrich
Max average temperature in Ti
(area along beam path)
Time (s)

## Slide 7: Radial temperature profile along Ti target to Cu radiator
Sketch,
no technical drawing!
Ti Cu
Felix Dietrich (‘Fork model’)
Ti
Cu
Photon beam
position
Temparature
gradient
Distribution of bunch train
preliminary

## Slide 8: Estimated average temperature in T rim and Cu radiator
Consider thermal radiation from rim and radiator
  Case (1): rim 0.082m2 + radiator 1m2
  Case (2): rim 0.082m2 + radiator 2m2
  Emissivity e=0.6
At relatively low Edep (~2kW) the radiator surface is less decisive
Real temperatures need simulations, they depend on radiator design and Ti-Cu contact
Edep[kW]
Tave[C]
Chart: 
| 1 | 2 | 4 | 6 | 8
Trim (1) | 195 | 292 | 436 | 550 | 644
Tradiator(1) | 157 | 220 | 297 | 344 | 383
Trim (2) | 150 | 235 | 370 | 483 | 580
Tradiator (2) | 111 | 160 | 222 | 262 | 293

## Slide 9: Temperature distribution at the target rim
adjust revolution frequency to distribute energy deposition almost uniformly over rim
for example:
  bunch train occupies angular range qpulse
  frev = 1922rpm instead of 2000rpm
   pattern: 1st second: 0, 144, 288, 72, 216,
  2nd second: 0 + qpulse ….,
  3rd second: 0 + 2qpulse ….
  after ~7s the rim is almost uniformly heated
  unbalances due to non-uniform heating are avoided

## Slide 10: Stress due to heating
Instantaneous heating
  Pulse  DT = 80K … 200K
  Ds ~ 100…260MPa
  ILC e+ target: ~3×106 loads per year (5000h)
  fatigue stress limit for Ti alloy ~510MPa at room temperature but lower at elevated temperature
Average heating
  Heated rim:
    Hoop stress if expansion is prevented: sH = E a DT
     Ti rim @ 500C  sH would be ~420MPa
    Expansion of rim not restricted  increase of rim circumference u,
    Du = 1.3cm (Dr = 2mm)
  Spatial expansion Vrim(heated) = g·V20˚C·DT
    Ti: DV ~ 1.2% for DT=500K (~ 2% for 850K)
    Cu: DV ~ 6.6% for DT=200K (~ 11.5% for 350K)

## Slide 11
 Sliced target
  minimizes stress in (non-uniformly heated) target rim and radiator
  Main stress contribution from cyclic energy deposition by photon beam
Rotation  tangential and radial forces
  thin ring approximation for target rim: st ~ rr2w2 = 50MPa
  sliced target,
    ~40 pieces for nominal lumi),
    height ~3cm  Fc=mrw2 ~ 3.3kN
    With connecting area A~10cm2  s ~ 33MPa stress at Ti-Cu connection
 Ti-Cu contact
  must work well for all temperatures
  Calculation of stress at the contact Ti to radiator needs FEM methods
  Possibilities considered
    bolts + plate springs
    bolts + plate springs + fire-tree connection

## Slide 12: wheel sector considered for ANSYS simulations
target
bolts
radiator
cooler
model 1 target with radiator
Artificial peak stress due to implementation
F. Dietrich

## Slide 13: Target-radiator connection
Model (Edep = 2.3kW) | Tavemax[C] in target | sv.Mises [MPa] at bolts | sv.Mises [MPa] at contact | sv.Mises[MPa] (static) | Height h [mm]
2 bolts M5 | 447 | 51 | 168 | <922 | 20
2 bolts M12 | 283 | 66 | 204 | <1170 | 30
Fire-tree | 301 |  |  | 66 | 
bolts
Fire-tree
Artificial peak stress due to mesh
h
Simulations: F. Dietrich
High values
artificial
preliminary

## Slide 14: Temperature in radiator and cooler
Edep = 2.3kW
Radiating area A=3.5m^2
Average temperature in radiator ~250C
Temperature in cooler is fixed at innermost area (s=28cm) to 20C
cooling efficiency is underestimated
But low radiator T is also less efficient
0cm
15cm
28cm
Simulations: F. Dietrich
preliminary

## Slide 15: Thermal radiation – only rim, no radiator
Perfect solution for Ti-Cu connection has not yet been found
Result from target tests (see Alexandr’s talk): Ti6Al4V stands very high loads
Remember: first ~4 years max Edep ~2.3kW (if no ‘staged ILC’)
 what about simple rim with spokes (but no water cooling)?
Taverage[°C]
e=0.6
Consider radiation off target rim only,
r = 0.5m, h=2cm, d=1.5cm
A ~ 0.17m2, e = 0.6
Average temperatures (nominal lumi)
Ecm = 500GeV
Edep= 2.3kW  Ttarget (ave)~525C
Ecm = 350GeV : 5 kW  Ttarget (ave)~694C
250GeV: 7 kW  Ttarget (ave)~778C

## Slide 16: Consider: only rim with cooler (no radiator)
FC
FC
Sketch,
no technical drawing
No spokes (etc) shown
radiation area of rim: 0.14m^2 ( rim height h = 2cm)
0.18m^2 ( rim height h = 3cm)
0.47m^2 ( rim height h = 10cm)
cooler
target

## Slide 17
A. Ushakov, POSIPOL2014

## Slide 18: Assumption: only rim with cooler, no radiator
Taverage [°C]
Edep [kW]
T^4 cooling estimate (no simulation):
Ti6Al4V rim with h~10cm could work for Ecm = 500GeV, nominal lumi
Tave ~ 350C; to be confirmed by realistic simulation
weight of rim + spokes ~50kg
Stress at spokes?
Deformation due to elevated temperatures and stress from rotation?
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
h = 2cm | 410 | 536 | 621 | 687 | 741 | 788 | 830 | 867 | 901 | 932
h = 3cm | 370 | 488 | 567 | 629 | 680 | 724 | 763 | 798 | 830 | 859
h=10cm | 242.5 | 331 | 392 | 440 | 480 | 514 | 544 | 571 | 596 | 620
Ecm = 500GeV, Edep = 2.3kW
Ecm = 350GeV, Edep = 3.9kW
Ecm = 250GeV, Edep = 5.0kW
e=0.6

## Slide 19: Assumption: only rim with cooler, no radiator
Ti6Al4V
Tensile Yield Strength
  = 830 MPa (RT)
  = 565 MPa (370C)
Fatigue Strength
  = 510 MPa (RT), corresponds to
  cyclic stress amplitude ~450 K
10cm high rim, no radiator:
  Tave ~ 350C
F. Staufenbiel, POSIPOL2013:
Equilibrium temperature with cooling channels inside the wheel and a water flow of 0.1 l/s

## Slide 20
2*1010 e- / bunch
2625 bunch / train (0.97ms)
0.366ms bunch spacing
5 train / s
Dynamic stress and temperature evolution in the ILC target wheel (high lumi)
temperature
stress
Friedrich Staufenbiel

## Slide 21: To be done for the target
Operation temperature of target material?
  Our ‘old’ recommendation: max target temperature should be below 450C
  Material tests at MAMI (see Alexandr’s talk): Ti6Al4V can stand high cyclic load and very high temperatures
  Not included in the MAMI tests:
    Load from rotation
      plastic deformation due to lower stress limits at higher temperatures
    Stress from connection with other material which has different thermal expansion coefficient etc.
    Creep effects etc.
Test of T^4 cooling for thick samples
  Test targets at MAMI had thickness of 1-2mm. ILC target has 15mm. Heat diffusion from central part to surface ~15 seconds
  Does the T^4 cooling work as expected also for thick our temperature profiles in the target?

## Slide 22: To be done for the target wheel
Connection of Ti target rim with radiator
  Optimum design
  Test of long-term stability under realistic conditions (elevated temperature distribution, mechanical load)
Weight of wheel
  Target rim + radiator with fins with current design ~ 120kg
  Weight reduction desired
    Safety reasons
    Design and operation of bearings
  Rim with spokes possible for Edep below ~2 kW ?
Mechanical driving system for the wheel
  Radiative cooling can use the system planned for the sliding contact cooling concept
  Tests up to prototype were planned for the sliding contact cooling concept – but now… ?
  Funding for R&D?

## Slide 23: Summary
Although radiative cooling will work for the e+ target, design details are not so easy and need effort
  Principal design: wheel = target rim + radiator, stationary water-cooled cooler
  T in target mainly determined by heat transport in Ti alloy and radiator size
  May be, during first years simple target wheel with spokes is sufficient (to be checked and taking into account running scenario – H20 or staged approach)
Tests are necessary
  Test the material under irradiation
  Test of temperature distribution and T^4 behavior of ‘real-size’ target samples (thickness!)
  Design and test the contact between target and radiator
Mechanical design for the rotating wheel
  No DESY/Uni HH resources
Further issues:
  Shielding
  protection of source components (e.g. FC)
  Source exchange, target replacement, remote handling,…
e+ will be polarized. PhD thesis planned to study the realistic undulator spectrum
We would be very thankful for strengthened collaboration

## Slide 24: Summary
Candidates for closer collaboration
  Test the material under irradiation
  Test of temperature distribution and T^4 behavior of ‘real-size’ target samples (thickness!)
  Design and test the contact between target and radiator
  Mechanical design for the rotating wheel
  Shielding
  protection of source components