## Slide 1: ECAL Day
New Design for Beam Test Structure
Guillaume FAYOLLE
03/21/2017
ECAL Day - New Design for Beam Test Structure
1/9

## Slide 2
1. Initial Design for Beam Test Structure
2. New Design for Beam Test Structure
SUMMARY
Specifications
Design
Specifications
Design
Slab
Principle of assembly
Alignment and precision
Holding system
Steps of development
ECAL Day - New Design for Beam Test Structure
2/9

## Slide 3
Initial Design for Beam Test Structure
ECAL Day - New Design for Beam Test Structure
Tungsten
Specifications
  10 slabs assembly
  Equal distance between slabs
  Possibility to insert 3 different thicknesses of tungsten between slabs
Slabs
BEAM
Mechanical Structure
200 mm
200 mm
850 mm
Design
Slabs
BEAM
Tungsten
Electronic cables
Electronic cables
Constant gap between slabs : 8 mm
Constant gap between wafers : 15 mm
3/9
Desy beam test (2012)
Detection

## Slide 4
New Design for Beam Test Structure
ECAL Day - New Design for Beam Test Structure
Design
Specifications
  20 slabs assembly
  Possibility to change and minimize the distance between slabs
  Possibility to insert different thicknesses of tungsten between slabs
500 mm
270 mm
Tungsten
Slabs
BEAM
Mechanical Structure
Electronic cables
Detection
1100 mm
Slabs
Lifting ring
4/9

## Slide 5
New Design for Beam Test Structure
ECAL Day - New Design for Beam Test Structure
220 mm
Slab without the frame
680 mm
9,2 mm
16 mm
16 mm
Detection part
Electronic part
Slab with the frame
X wafers positioning +/- 0,1 mm
Y wafers positioning +/- 0,1 mm
X wafers positioning +/- 0,2 mm
Y wafers positioning +/- 0,2 mm
5/9
Origin (X0, Y0)
Origin (X0, Y0)
+
+

## Slide 6
New Design for Beam Test Structure
ECAL Day - New Design for Beam Test Structure
6/9
BEAM
Insertion of Tungsten
Tungsten
Support frame
Slab
Support frame
Elastic support
Insertion of the slab
Insertion of the slab
Slab
Support frame
Elastic support
Principle of assembly

## Slide 7
New Design for Beam Test Structure
ECAL Day - New Design for Beam Test Structure
7/9
Alignment and precision
X slabs positioning +/- 0,2 mm
Stop contact
Stop contact
Y slabs positioning +/- 0,2 mm
Base plate
Stop
Directly linked to the wafers positioning in X and Y directions

## Slide 8
New Design for Beam Test Structure
ECAL Day - New Design for Beam Test Structure
8/9
Screws to compact the assembly
Rods to maintain the slabs
Slab elastic support
Minimum gap between slabs : 2,2 mm
Minimum gap between wafers : 9,2 mm
Holding system
Base plate
Gain of 5,8 mm in comparison to the initial design

## Slide 9
Steps of development
ECAL Day - New Design for Beam Test Structure
9/9
  Build a frame for one slab
  Integrate and test a frame for one slab
  Build and integrate all the frames on the slabs
  Build the test bench
  Integrate and test the whole assembly
  Beam test at CERN
+
=
+
=