The latest result of the start to end simulation of E-driven ILC positron source
26-30, June, 2017, AWLC2017 at SLAC
Masao KURIKI (Hiroshima University)

---
Introduction
- E-Driven Positron source is the bottom line of the ILC positron source with a high reliability as a backup of Undulator.
- The design based on off-the-shelf components has been established with an enough performance.
- Further optimization was made to improve the performance and optimize the cost-effective system.
  - Small beam size on target for better yield. (2.8 → 2.0 mm rms)
  - Lower drive beam energy for less cost. (3.5 → 3.0 GeV)
  - Consider only the nominal parameter.

---
E-driven ILC Positron Source
5.0 GeV
L-band + S-band NC
3.0 GeV
S-band NC
- 20 of 1us pulses are handled with NC linacs operated in 300Hz.
- Optimize for the nominal parameter, 1316 bunches / pulse.

---
The beam handling and format
Damping Ring
Positron Booster
tp=480 ns
197 ns
81.6 ns
33 bunches
Tb = 6.15 n sec

---
Electron Driver
- 3.0 GeV Electron beam in the format with 2.4 nC bunch charge.
- S-band Photo-cathode RF gun for the beam generation.
- 80 MW klystron-modulator drives 2 structures giving 50 MV/3m with 0.4A beam-loading.
- 60 of 3m S-band TW structures
  for the acceleration.
Lattice	# of cell	Cell length(m)	Section length(m)
4Q+2S	6	8.0	48.0
4Q+4S	12	14.4	172.8

---
Target
- W-Re 14mm thick.
- 5 m/s tangential speed rotation (180 rpm, 0.5m radius) in vacuum.
- Water cooling through channel.
- Vacuum seal with ferro-fluid.
- A prototype compatible to vacuum
  in test.
- 2.6x10-6 Pa is kept with 225 rpm rotation
  with 100 l/s Ion pump.
- The vacuum level is same as expected.
- The radiation test was already done.
  It is vital against 1 year ILC
  operation.
Positron
Electron

---
Seal performance
- Leak rate 2x10-7 Pa.m3/s at 1000 RPM.
- 1000 l/s pump capacity is enough to maintain UHV for accelerator.
- 1.5 MGy/year is expected for the seal. Irradiation test was performed at JAEA Takasaki lab..
- F-oil : Dissociation/degradation occurred at low dose, 0.27 MGy. No hope.
- CN-oil: 4.7 M. Gy. Viscosity increased, but NO dissociation degradation occurred. No additional leak was found with the irradiated seal at 0-600 RPM.

---
Flux Concentrator
(P. Martyshkin)
- Flux Concentrator for AMD (Adiabatic Matching Device)
- 16 mm aperture
- 5 Tesla Peak field, 40mT trans.
- 25 kW ohmic loss.

---
Positron Capture Linac
- L-band SW structure designed by J. Wang (SLAC) for the undulator capture section is employed.
- Two structures are driven by one 50 MW klystron.
- The effective accelerating voltage depends on the beam loading current.
- The transient beam loading has to be compensated.

---
Beam Loading in SW Linac
Single Cell Model : Simple, but not realistic
- The field in SW accelerator
- The voltage becomes constant if
{size 24 color green { V(t) = { 2 sqrt{%beta P_0 r L }} over {1+%beta} left( 1 - e^{- {t over T_0}} right) - {rIL} over {1+%beta} left (1-e^{- {{t-t_b} over T_0}} right) }}
{size 24 color green { T_0 = {2Q} over {%omega (1+%beta)}}}
Beam Loading
RF
{size 24 color green { t_b = -T_0 ln left( I over 2 sqrt{rL over {%beta P_0} }right)}}
{size 24 color green { V_0= { 2 sqrt{%beta P_0 r L }} over {1+%beta} left( 1 - I over 2 sqrt{rL over {%beta P_0} } right) }}

---
Multi-Cell Model : More realistic
Time differential of the energy of the center cell,
Power flow to next cells
Input Power
Beam loading
WG loss
Power loss
Power flow from next cells

---
Time differential of the voltage
For the intermediate cells,
For the end cells,

---
11 linear simultaneous differential equations

---
A can be diagonalized with a orthgonal matrix R as
Because B is diagonal, the equation for V' is simply expressed as 11 independent linear differential equations,

---
The solution for V' is
The solution for V is expressed as a linear sum of the solution for V'
Amplitude for each modes and cells; two modes are dominant (beta=9)

---
Acceleration Field
  - L=1.27 m (11 cells, L-band SW)
  - R=34e+6 Ohm/m
  - P0=22.5 MW (50MW at klystron, 5MW wave guide loss)
30.6MV for 0A (b=1)
21.2MV for 0.5A(b=2)
14.7MV for 1.0A(b=3)
10.4MV for 1.5A(b=6)
7.3MV for 2.0A(b=9)

---
Beam Loading Compensation
No big difference on the no-load voltage, but 30 % less on the heavyly loaded voltage,
The beam loading compensation works well.
Flatness is less than 0.1%.

---
Phase dependent Beam Loading
- The phase of the drive RF and the beam loading is different.
- The RF field of the cavity is evaluated by accounting phase.
- The impact on the beam loading compensation is very limited.

---
Capture Simulation
Beam loading current is
dynamically changed,
  - Bunching,
  - Lost particles
- For each cells, the accelerator gradient is calculated with IBL(t)
- 18 RF modules (36 L-band SW) makes the average energy of positron 250 MeV.
{size 24 color green { I_BL= 1 over t_b sum q_i cos left( %omega t_i - k z_i right) }}

---
Booster
- A first half is implemented by L-band acc. and the last half is by S-band.
- 50MW L-band Klystron drives two L-band acc.
- 80MW S-band Klystron drives two S-band acc.

---
Beam-loading in TW Linac
- Positrons are accelerated by quadruplet multi-bunch pulse.
- The triplet pulse is repeated in 300Hz.
- Transient beam-loading should be compensated, otherwise, the beam is not accepted by DR.
RF Voltage
33 bunches
6.15ns spacing
0.55A
33 bunches
6.15ns spacing
0.55A
90 ns
0.55A

---
Beam-loading Compensation by AM
Beamloading term
Acceleration voltage by a flat RF (E0),
AM to compensate the beam loading
For transient component
For steady component
RF Pulse
V(no beam)
loading
V(with beam)
RF Pulse
V(beam loading)

---
Energy Compressor
- DR longitudinal acceptance (±35mm in z, ±0.75% in dE/E).
- Energy compressor makes a good matching to the acceptance.
- Energy Compressor consists from chicane and 5 L-band RF .
- The section length is 75.2 m.
RF tubes
Chicane
V
t
Before ECS
After ECS

---
Cooling Water
- Cooling water capability is estimated according to the power loss in RF cavity and RF load.
- dT<0.1K for RF cavity and dT=11K for RF load (TDR specification).
- By employing counter flows in RF cavity, Tout-Tin=10K is acceptable for dT~0.05 K.
- Because of the heavy beam
  load, dissipated power in RF
  cavity and load depend on
  the beam current.
(per tube)
Input RF
Cavity
Beam Acc.
Reflection
Reflection

---
- L-band SW
  (per tube)
- L-band TW
  (per tube)
- 2m S-band TW
  (per tube)
- 3m S-band TW
  (per tube)

---
Cooling Water Summary

---
RF unit
- High density of power units in the service tunnel is expected. (6.45 m/unit, average)
- Compact unit design with a good accessibility is mandatory.

---
Klystron (S. Fukuda)
- L band (1.3 GHz) with 50 MW‐100MW and S band klystron(2.6 GHz）with 80‐150MW are possible, but so far there are no commercially available klystrons.
- In order to reduce the numbers of RF source, higher output power is desirable, while requirements for minimum R&D lead to limited choice.
- For L‐band, we assume a 50 MW tube, since design of this power level is not difficult.
- For S‐band, we assume a 80 MW tube, since existing 2.856GHz 80 MW klystron is widely used, and frequency scaling from 2.856GHz to 2.6GHz is not so difficult. (Comments from Toshiba engineer)

---
Pulse Modulator (S. Fukuda)
- Solid sate modulator has a large merits
  - compact
  - maintenance ability

---
RF Unit
L-band Unit S-band Unit
1725
2447
1420
1894

---
RF Unit Layout
Positron Capture Linac
(highest density)
S-band Electron Linac
2500 mm
1700 mm

---
Parameter Summary
Parameter	Value	Unit
Drive Beam Energy	3.0	GeV
Target material	W-Re
Target thicknesss	16	mm
Beam Size (rms)	2.0	mm
AMD peak field	5.0	T
RAMD (smallest aperture of AMD, 2a)	16.0	mm
Average gradient (MV/m)	8.4 – 22	MV/m
Accelerator Aperture (2a)	60	mm
Solenoid	0.5	T
Booster	Hybrid (L-band + S-band)

---
Total Length
Electron Driver
220.8 m
Positron Booster
531.2m
ECS
75.2m
Positron Target
Capture Linac
55m
Total : 882.2 m

---
Positron Yield
- Positron Yield = # of positron in DR dynamic aperture per electron.
- Edrive=3.0 GeV, rms=2.0mm gives Yield=2.1.
{size 24 color green { left( z over 0.035 right)^2 + left( %delta over 0.0075 right)^2 < 1 }}
{size 24 color green {%gamma A_x + %gamma A_y < 0.07}}
DR acceptance
Capture Linac
Positron
ECS optimization
Electron

---
Potential Problem : PEDD on FC and RF
47kW
FC
5.8kW
1st Acc.
32kW
RF
Pipe
FC
Electron Driver
3 GeV, 2.4nC
Target
6.6kW
32 kW average loss by particle
would detune the RF strucure.
0.8kW/cm3
3.2 J/g.pulse < 7-12 J/g.pulse
It is managable.

---
RF detuning by particle loss
RF detuning is -38.2kHz
for 3.3kW /iris.
Energy deposition /cm is 0.14 kW/cm or less.
If the power over one cell is concentrated on the iris, the energy deposition on the first iris is less than 1.5 kW/iris.
If we assume the same deposition along all RF, the detuning is 17 kHz.
It is less than bandwidth of the structure, 44 kHz.
Detail simulation for the detuning should be made.
RF loss
Particle loss
RF
Pipe
FC
kW/cm
0 0.5 1.0 1.5 2.0

---
Summary for E-driven
- The conceptual design was improved for better performance with a more cost effective configuration.
- The drive beam energy is now 3.0 GeV with 2.0 mm rms spot.
- The yield is more than 2.0.
- Target prototype is currently very smooth (see Omori-san's talk)
- Potential problems are likely to be not serious,
  - PEDD or heat load to FC,
  - RF detuning by heat load.