## Slide 1: ATF February plans
 | Nominal Optics | High-beta optics
Week 1 | Minimum jitter measurements on waist at IPBPMs as function of attenuation + noise floor measurements. Random jitter source scan to measure real jitter (at 0dB). Noise floor measurements at different charges. | 2 BPM IP feedback (two bunches). 3 BPM resolution (X and Y).
Week 2 | Set-up two-bunch upstream feedback. Measure the feedback jitter correction with the IP BPMs. Introduce random jitter source (or just move off waist) in hope of seeing reduction in jitter. | Repeat 2 BPM IP feedback study, in case there are issues in first week.
1 shift
1 shift
1.5 shifts
Pre-beam IP electronics tests
Output of the 1st stage frequency multiplier using a spectrum analyser.
Outputs of the first stage mixer and limiting amplifier diode.

## Slide 2: Week 1: Shift 1 – Minimum jitter measurements
Nominal optics, 1 bunch.
Waist scan at IPC - set QD0FF current, calibrate at 20dB, then vary QD0FF current, set to central value, reduce attenuation to 0dB, then vary QD0FF current, set to waist.
Take a measurement of the noise floor with 70dB attenuation on the dipole.
Calibrate + jitter run at attenuation settings 0dB – 50dB.
Jitter at 70dB + calibration @ 0dB/10dB for various charges.
Random jitter source scan at 0dB.
Repeat for IPB (and IPA if time)

## Slide 3: Week 1: Shift 2 – 2 BPM IP feedback
High-beta optics, two bunches.
Centre the beam in X and Y in all three BPMs using the IP mover system.
Jitter run + calibrate all three BPMs at (in X and Y) at various attenuations for 3BPM resolution study.
Calibrate again at 10dB + take jitter run.
Calculate bunch-to-bunch correlation as a function of sample number.
Set-up IP feedback using 2-BPM firmware and optimal sampling.
Perform kicker scan to calculate appropriate gains.
Take interleaved feedback runs.
Repeat at 0dB.

## Slide 4: Week 2: Shift 1 – Measuring upstream correction at IP
Nominal optics, 2 bunch.
Set-up upstream feedback.
Waist scan at best resolution BPM (found from Shift 1) - set QD0FF current, calibrate at 20dB, then vary QD0FF current, set to central value, reduce attenuation to 0dB, then vary QD0FF current, set to waist.
Take a measurement of the noise floor with 70dB attenuation on the dipole.
Turn on interleaved upstream feedback.
Calibrate + jitter run at IP.
Random jitter source scan with jitter run at IP with each setting
Try moving off-waist.