## Slide 1: Luminosity Optimization at 250GeV
K. Yokoya
2017.2.1

## Slide 2: Basic Formulas
The luminosity
Can be written in terms of beam power and beastrahlung loss
  C : universal constant
  PB = beam power
  The last factor express the hour-glass effect approximately
  dBS = beamstrahlung energy loss
(1)
(2)
(3)
(4)
  Beam size at IP

## Slide 3: Luminosity Scaling
Naive scaling
  (1) and (4) gives L ~ E (constant bx,y )
However, the form (2) says L can be ~1/E, if
  PB independent of E
  dBS independent of E
(a) is realized in “10 Hz collision” (i.e., same beam power with 10Hz@250GeV and 5Hz@500GeV)
  But this is not realistic in the 250GeV in staging
    Cost saving too small
(b) is possible?
  TDR parameter set says dBS ~ 1% at 250GeV
  If 4% beamstrahlung is acceptable, luminosity can be doubled

## Slide 4: How to Increase Beamstahlung
Increase bunch charge
  N  aN, (nb  nb/a so that PB does not change)
  Then, dBS  a2dBS , L  aL
  But this will
    Make the out-coming angle of pairs sqrt(a) times
    Changes of DR dynamics, alignment tolerance of ML
   unacceptable
Shorter bunch length
  sz  sz/a,
  Then, dBS  adBS , Can make by smaller (hour-glass),
   L increases
  But this will
    Make the out-coming angle of pairs sqrt(a) time
   unacceptabl
Smaller horizontal beam size
  sx  sx/a
  Then, dBS  a2dBS , L  aL

## Slide 5: How to reduce sx ?
The simplest way is to reduce bx
But this will make the beam angle spread at IP larger
(5)
 larger beam size at the final quad QD0
Synchrotron radiation from tail particles hit the quad, causing back ground
These particles must be collimated out upstream
The horizontal collimation depth is already ~ 6 sx

## Slide 6: Collimation Depth with TDR Params
T. Okugi
250GeV 2m QD0
250GeV 1m QD0
The circles shows the betas in TDR

## Slide 7: Horizontal Emittance
sx can be reduced by reducing the horizontal emittance from DR
  Present lattice is presumably conservative
  Circular colliders assumes much more aggressive horizontal emittance
If ex,n  ex,n/a,
Then, sx  sx /sqrt(a), dBS  adBS , L  sqrt(a)L.
This will make horizontal beam angle 1/sqrt(a) smaller.
If we further make bx  bx /a, then L  a2L
Smaller ex,n would also help at other energies
  Luminosity increase may be small but at least FFS tuning would become easier (allow larger bx for same sx )

## Slide 8: Problems
Obvious problems are
  Is it possible to reduce ex,n of DR?
    Technically possible?
    Manpower problem
    Now, Kiyoshi is trying …
    Must include studies of e-cloud, FII, etc.
  Disruption parameter too large
(6)
  Disruption parameter too large
    Dy  aDy
    Present Dy is already ~25
    Feedback tolerance tighter

## Slide 9: An Example Parameter Set
Next page, right-most column
  ex,n  ex,n /2, no change of bx
However, note that Dx ~ 0.5 is not negligible
This will cause effective sx smaller than sx /sqrt(2)
Hence, dBS larger than 2dBS , L larger than sqrt(2)L
Beam-beam simulation being done by Daniel Jeans (the bottom row is to be filled by simulation)
If everything is OK, may try smaller bx