## Slide 1
Undulator based e+ source:
ILC e+ source WG
20th April 2017
Sabine Riemann (DESY)

## Slide 2: Yokoya-san’s list of main topics
R&D plan for the undulator scheme
Possible discussion topics may be
  Define the thin target case as the standard parameter for 250GeV?
  Need corresponding design change of target. (heat conduction, wheel weight ...)
  Further effort of reducing PEDD on FC
  QWT as bottom line

## Slide 3: Thin target as baseline?
Andriy Ushakov:
  With the baseline undulator parameters and Lund = 231m, a thinner target is more efficient for Ecm = 250GeV
  Substantially lower energy deposition:
    Target thickness 1cm instead of 1.5cm  reduction to ~57%
  PEDD decreases only slightly but shouldn't be a problem
  Energy deposition in FC can be reduced by ~25%
 Thinner target is an excellent option for improvement
  To do: Design for the wheel (slim design) with efficient heat removal
    3kW in a 1cm thick, 3cm high target rim cooled by thermal radiation (without radiator!) yields an average temperature of ~600˚C
Further possibilities for optimization ?

## Slide 4: Undulator
With current undulator parameters Lund = 231m are required for Ecm = 250GeV
So far, all optimizations were done with ideal undulator field
  Photon yield (e+ yield) with realistic undulator field?
  Photon polarization (and Pe+) with realistic undulator field?
Studies so far:
  D. Scott, J. Clarke, PRL 107, 174803(2011)  4m undulator module test
  talks of M. Jenkins and A. Alrashdi at POSIPOL’15)
  Prel. Results:
    Photon yield (e+ yield) seems ok with realistic undulator field and assuming Ee- = 150GeV or 250GeV;
    Polarization is more complicated, has to be checked

## Slide 5: OMD
QWT or FC? YQWT ~ 0.6 YFC
  With QWT the gain due to lower load on a thin target is ‘gone’:
    FC, nominal lumi: 3kW deposited in 1cm target
    QWT, nominal lumi: ~5kW deposited in 1cm target
    Radiation cooled target is rotating in the slit between focusing and bucking magnet of the QWT. Heating of the QWT? Cooling??
  Studies are necessary

## Slide 6: My personal conclusion
Optimization of target alone is not sufficient
Must include:
  Optimized undulator parameters?
  more realistic undulator:
    Realistic yield and polarization
    beam induced heating of undulator
      D. Scott (PhD, 2008): total heating of undulator module due to SR and image current must be <1W/m; estimated peak values for SR could reach 20W/m (Jenkins, PhD, 2015),
      SR collimator design for Ee- ≥150GeV and Lund~150m undulator length exists. Check/update it for Ee- ≥120GeV and Lund~231mOMD
Manpower??