Update on ILD models
Vincent Boudry
École polytechnique, Palaiseau
CALICE Meeting
Tokyo University, 26/09/2017
TA support + WP14

---
Outline
Update on dimensions
  refinement from Henri on ECal dimension
  for the Technical Design Document.
1. (Short) needs on R&D
2. Status

---
Redefinition of dimensions
SiW-ECal group should present 2 designs:
  - a model close to the DBD coined “baseline” or “large” with inner ECal radius at RECal =1843 mm
  - a “small” model RECal ~1500 mm (all related quantities adapted ↔ Router[Endcaps] )
  - Plus a model with reduced number of layers
The model should be equally adequate for Si and Sc options but base is Silicon (yielding most constraints)
Early version of ECal Technical Design Document (69 pages) by Henri, Marc and Denis (+ ed. Daniel & Roman) available on https://llrbox.in2p3.fr/owncloud/index.php/s/S0WrOA6CzINiFwZ (⚠ the dimensions in this document are not up to date. Being redone ⚠)
1. Initial presentation done by Henri at the SiW-ECal day in march:
   https://agenda.linearcollider.org/event/7476/contributions/38677/attachments/31312/47232/ECal_models.pdf
  1. Modification requests on ECal thickness
    1. relaxed thickness on chip, increased Si thickness, addition of a 1st layer of W, 2 rails, …
    accepted by ILD but implied changes in return…

---
Dimension constructions (reminder)
1. Barrel length fixed at 4700 mm in all models, same as HCal or TPC
  1. 8 staves ⊃ 5 CF/W modules ⊃ 5 alveoli columns
  2. 1 alvoli width = ~ 2 × wafers width + walls + clearance
2. Endcaps
  1. RINNEREndCaps fixed at 400 mm ⇒ ECal ring & Forward detectors
  2. RouterEndCaps = RouterBarrel + overshoot
  3. ZfrontEndCcaps  = ZouterBarrelL + overlap
1. Baseline
  1. Endcap quadrant
     with 3 modules of
     3 alveoli
2. Reduced
  1. Endcap quadrant
     with 2 modules of
     4 and 3 alveoli
© M.A.
overshoot
overlap
ECal ring

---
ECal thickness
1. DBD thickness: 185 mm, “hopelessly aggressive”
2. More realistic calculations:
  1. 223.2 mm (∆= +38.2 mm) for barrel
  2. 223,6 mm (∆=+38.6 mm) for endcaps
was 320μm
was 0.2mm
was 0.8mm
connexion & capa
For thin layers
(×2 for thick ones)

---
Decision to keep HCAL untouched
1. Keep HCAL untouched and
  1. reduce outer TPC radius ROUTERTPC
  2. reduce the overlap between ECal Barrel & EndCaps
2. For the Baseline design:
  1. RINNERECal, BARREL = RINNERHCAL, BARREL (2058 mm) –30mm (clearance) – 223.2 mm = 1804.8 mm
  2. ZFRONTECal, EndCaps = ZFRONTHCAL, EndCaps (2650 mm) – 15 mm* (clearance) – 223.6 mm = 2411.8 mm
    1. overlap = 61.8 mm (was 100mm in DBD,
       incl. ETD now gone [25mm], so reduction
       is 75mm to 61.8mm)
  3. No changes in R(Endcaps) = 2095.2mm
    1. overshoot = 67mm
3. Tracker dimensions:
  1. ROUTERSET = 1775.3–1790.6 mm and RINNERSET = 1772.8 – 1788.1 mm (24 sym).
  2. ROUTERTPC = 1769.8 mm (was 1808 mm in DBD, ∆ = -38.2 mm)
* gap to have the rails
 and cooling pipes
 (no electronics)
[Speaker Notes: SET 3mm from TPC 2.5mm thickness 24 staves R min = 1769.8+3 (1 – 1/cos(2π/24)) = 1772.8 – 1788.09]

---
Small ILD
Same recommendations as for baseline:
  1. recalculated RINNERHCAL, BARREL as 1500 + 185 + 30 = 1715mm
1. Small ILD ECal dimensions:
  1. RINNERECal, BARREL = RINNERHCAL, BARREL – 30mm – 223.2 mm = 1461.8mm
  2. ZFRONTECal, EndCaps = 2411.8 mm (unchanged from baseline)
  3. ROUTERECal, EndCaps = 1717.2 mm
    1. 2 modules per quadrant of 4 (inner) and 3 (outer) alveoli
    2. The overshoot of the end-cap to the barrel is then 32mm
2. Tracker dimensions:
  1. ROUTERSET = 1775.3–1790.6 mm and RINNERSET = 1772.8 – 1788.1 mm (24 sym).
  2. ROUTERTPC = 1769.8 mm (was 1808 mm in DBD, ∆ = -38.2 mm)
[Speaker Notes: SET 3mm from TPC 2.5mm thickness 24 staves R min = 1769.8+3 (1 – 1/cos(2π/24)) = 1772.8 – 1788.09]

---
Slab plug
The slab plug is identical for both models.
On top of the TDD model an aluminium
plate of 0.7mm has been added (simulation)
Exemple of realistic design (M.A.)

---
Reduced number of Layers
1. Going from 30 to 22 layers
  1. Reduction of cost; (small) reduction of RM ; increase of Energy resolution
    1. “better separation at the expanse of the intrinsic resolution”
2. Increasing the Si thickness to 725μm, if really feasible (next slide)
3. Energy resolution σ(E)/E:
  1. for 22 layers w.r.t. 30: +16.8%
  2. with 725μm w.r.t 500μm : –6.1%
4. ECal thickness = 190.1 mm (close to 185 mm of DBD).
  1. 22 layers = 14 layers with 2.8mm thickness
            + 8 layers with 5.6mm shared between structure and slabs.
5. Study needed on separation, resolution and efficiency performances
   at low energy.
  1. JER : σ(EJ)/EJ +10% for 20 layers (500 μm).
σ(1GeV) in % & Linearity
Impact of the silicon thickness
on the resolution
the resolution goes like
where th. is the Si thickness
in hundreds of microns
Si thickness /100μm

---
Larger / thicker wafers
Use of 8” (200mm), with same alveolus width.
For thin layers
(×2 for thick ones)

---
Needed R&D
1. 3 models: realistic baseline, “small”, reduced layer #
  1. 200mm /150 mm ingots (8” vs 6”); if 200mm design (staggered vs straight);
  2. 725μm wafers
  3. possibility of staggered alveoli
2. What is needed for decision ?
3. ⊗ Feasibility:
  1. ASU + 1st connexion: S/N ratio, Stability, Uniformity between elements. : CALICE technical prototype (7 working ASU as of now)
  2. Long SLAB: readout over long chain: design R&D, power distribution, grounding; connexions between ASU’s
    1. 1st SLAB; later (after ILC confirmation) Module-0 (3–5 alveoli × 22-30 SLABs)
  3. Mechanical models: barrel module, endcap modules: stress tests to be done to assess calculations
  4. DAQ: distribution to SLABs (from concentrator cards → SLAB), redundancy scheme; calculation of occupancy (close to beam pipe)
  5. Wafer production: learn from HGCAL, statistics from current wafer batch ? Other founders (Infineon, LFoundry)
4. No design yet for ECal ring

---
What’s new ?
1. ILD models
  1. Constrains from mechanics	⇒ Marc
  2. Status of implementation in Simulation	⇒ Daniel
2. ILD prototype : Long Slab benches
  1. electronic bench: ongoing	⇒ Frédéric
  2. electro-mechanical:	⇒ Roman
    1. no industrial solution found for inter-connexion
       (rebuttal from Westronic)
    2. LAL electronic service on the work to find a solution
    3. 20 new FEV11 produced and checked
    4. 156 SK2 + 227 SK2a packaged (today, out of 160+240)
1. CALICE Technical prototype:
  1. Existing short slabs 7 + 3 (to be repaired)
  2. Tests in DESY BT	⇒ Adrián & Yu
  3. Production of 10- new slabs w SK2a: delayed to beg of 2018.
    1. new FEV: 15 points of improvement addressed
    2. new wafers received and tested	⇒ Rémi
    3. new flexible stack	⇒ Guillaume
  4. Second production in Japan	⇒ Taikan.
  5. Chip-on-board	⇒ Prof. Chai
  6. DAQ
    1. ECal DIF of code:
      1. review done (with CMS HGCAL)
      2. some modification to be implemented: 40 MHz, muting of fast clock, …
    2. EUDAQ2 to be tested (6h or 6m work ?)