## Slide 1
G. Balik1, B. Aimard, J.-P. Baud1, L. Brunetti1, A. Dominjon, A. Jeremie1, M. Serluca1
B. Caron2
Z. Buchta3
(LAViSta Team: Laboratoires d’Annecy-le-Vieux de Vibration & Stabilization)
1: LAPP-IN2P3-CNRS, Université Savoie-Mont-Blanc, Annecy, France
2: SYMME, POLYTECH Annecy-Chambéry, Université Savoie-Mont-Blanc, Annecy France
3: ISI ASCR, Brno University of Technology, Brno, Czech Republic
CLIC QD0 Stabilization
26th October 2017

## Slide 2
INTRODUCTION
  Context
  CLIC Challenge vs QD0 stabilization
Vibration control for CLIC
  Beam trajectory control (IPFB)
  Mechanical stabilization
  Custom vibration sensor
FuturE prospectS
  Vibration sensor improvement
  ATF2
Conclusion
TABLE OF CONTENTS

## Slide 3
Sub-nanometer beams
Vertical beam offset: 0,2 nm RMS @ 0,1Hz
CLIC detector
QD0 L*
QD0 Cantilever
INTRODUCTION - Context
Final focus CLIC R&D:
Developments of LAViSta team are dedicated to the final focus

## Slide 4
INTRODUCTION - CLIC Challenge vs QD0 stabilization
IPFB : Interaction Point beam based FeedBack is already developed in collaboration with CERN since 2010
Active / passive stabilization : has to be achieved (“Mechanical stabilization”)…
At the IP (mechanical + beam feedback), we aim a vertical beam offset at 0,2nm at 0,1Hz
Final focus : beam stabilization strategy

## Slide 5
Luminosity vs control ON or OFF and vs model of seismic motion (simulation under PLACET)
- Caron B, et al, 2012, “Vibration control of the beam of the future linear collider”, Control Engineering Practice. - Balik G. et al, 2012, “ Integrated simulation of ground motion mitigation, techniques for the future compact linear collider (CLIC) “, Nuclear Instruments and Methods in Physics Research
PLACET a program to simulate drive beams
VIBRATION CONTROL FOR CLIC - Beam trajectory control (IPFB)
IPFB - simulation under PLACET
Controller performances

## Slide 6
Results with commercial sensors : 0,6 nm RMS@4Hz.
- Balik G. et al, “Active control of a sub nanometer isolator“, JIMMSS, 2013.
- Le Breton R. et al, Nanometer scale active ground motion isolator, Sensors and Actuators A: Physical, 2013.
Main limitation : SENSORS (Experimental and theoretical demonstration).
Sensors dedicated to measurement but not to control
Two needed technologies for the selected bandwidth (geophones for low frequencies and accelerometers for high frequencies)
  complexity of the control
Commercial sensors and a developed active foot
Developed active foot with commercial sensors (geophones and accelerometers)
2 sensors used in feedforward and 2 sensors used in feedback
Before 2016 : demonstration at a sub-nanometer scale
VIBRATION CONTROL FOR CLIC - Mechanical stabilization

## Slide 7
Internal development at LAPP
Approach validated → Patent n° FR 13 59336
Prototypes developed since 2011
Development of a new vibrations sensor:
VIBRATION CONTROL FOR CLIC - Custom vibration sensor
Promising results (similar to the best commercial sensors)
Comparison with Güralp and Wilcoxon sensors at CERN (ISR):

## Slide 8
CLIC specification (displacement of the QD0 final focus) : 0,20 nm RMS@4Hz
Previous results with LAPP active foot + 4 commercial sensors : 0,60 nm RMS@4Hz
Results of control (autumn 2016) with LAPP active foot + 1 LAPP vibrations sensor : 0,25 nm RMS@4Hz
Only 1 sensor in feedback -> control less complex and more efficient
Submitted in September 2017, in collaboration with SYMME (approval in progress)
- LAPP active foot + LAPP sensors (one on ground used to monitor ground motion and 1 on top used in feedback) -
- Displacement without control / with control at LAPP -
Active control with the custom sensor
0,25 nm@4Hz ≈ Spec
2016 : CLIC Demonstration of feasibility at reduced scale
VIBRATION CONTROL FOR CLIC - Mechanical stabilization

## Slide 9
Control is not efficient enough in this case (above 100 Hz)
0,78 nm@4Hz > Spec
CMS detector ground motion is taken into account (high level of cultural noise - pessimistic)
Simulation of the system (foot + sensors) with these disturbances
Disturbances don’t reveal the same distribution (more cultural noise)
Control still efficient <100 HZ
More cultural noise >100 HZ
Simulation of the active control with in a collider environment
The Compact Muon Solenoid (CMS)
VIBRATION CONTROL FOR CLIC - Mechanical stabilization

## Slide 10
Necessity to have a passive insulation under the concrete or under the last elements
0,26 nm@4Hz ≈ Spec
Passive isolation ≈ 25 Hz
A passive insulation at about 25 Hz is common to the standard industrial solutions
Example of usable PI (Biltz® B13W- vibration isolation rubber pad).
Poster session at IPAC17: G. Balik et al, “Proof of concept of CLIC final focus quadrupoles stabilization”, in Proceedings of International Particle Accelerator Conference (IPAC 2017), Copenhagen, Denmark.
VIBRATION CONTROL FOR CLIC - Mechanical stabilization
Simulation of the active control with a collider environment

## Slide 11
PACMAN : Particle Accelerator Components’ Metrology and Alignment to the Nanometer scale (Marie Curie program at CERN)
Collaboration with several labs and industries : LAPP academic partner – SYMME co-director of a thesis
Use of the LAPP sensor with dedicated instrumentations
Capacitive sensors : PI & Lion Precision
Optical encoder : Magnescale
Interferometer : Attocube & a developed one (INRiM (It) and ISI Brno (Cz))
P. Novotny et al, “What is the best displacement transducer for a seismic sensor?”, IEEE Inertial Sensors and Systems 2017, Hawaï, USA.
FUTURE PROSPECTS- vibration sensor improvement
Comparison of different technologies for the embedded sensitive part

## Slide 12
FUTURE PROSPECTS- vibration sensor improvement
High reflectivity mirror to increase the signal-to-noise ration in the built-in interferometric sensor
New opto-mechanical components to suppress low frequency noise
Further tests ongoing and comparison with current setup (embedded capacitive sensor)
Multipass interferometer setup test
Integration of a multipass-interferometer
Vibration sensor with different technologies for the embedded sensitive part
Collaboration with ISI (Institute of scientific Instruments , The Czech Academy of Sciences)

## Slide 13
FD : Final Doublet
Shintake monitor : beam size measurement
  Relative motion between shintake monitor and final doublets of 6 nm RMS @ 0,1 Hz in the vertical axis.
  -> Analysis of the upgrades influences and of the drift.
2008 by B. BOLZON | Tolerance | Measurement [SM-QD0] | Measurement [SM-QF1]
Vertical | 7 nm (for QD0) 20 nm (for QF1) | 4.8 nm | 6.3 nm
Perpendicular to the beam | ~ 500 nm | 30.7 nm | 30.6 nm
Parallel to the beam | ~ 10,000 nm | 36.5 nm | 27.1 nm
2013 by A. JEREMIE | Tolerance | Measurement [SM-QD0] | Measurement [SM-QF1]
Vertical | 7 nm (for QD0) 20 nm (for QF1) | 4.8 nm | 30 nm
Parallel to the beam | ~ 10,000 nm | 25 nm | 290 nm
Magnet 450kg
Magnet 1200kg
2012
Responsible of the final doublet relative displacement
2008
FUTURE PROSPECTS- ATF2
ATF2 magnet supports upgrades
feet and T-plate

## Slide 14
Involved in the assessment of the beam feed-forward control vs ground motion
Processing of 14 Geophones (Guralp 6T sensors)
Collaboration with CERN, LAL & KEK
Last campaign of measurements : May 2017
Next campaign in December 2017
Vibration sources identification
Feedforward study: correlation between the ground and the beam motions.
D. Bett et al, “Ground motion compensation using feed-forward control at ATF2, in Proceedings of International Particle Accelerator Conference (IPAC 2016), Busan, Korea.
FUTURE PROSPECTS- ATF2

## Slide 15
Active control
  A sensor dedicated to this vibrations control issue is developed
  Sub-nanometer control is validated by demonstration on a small size prototype
Future prospects
  Improvements of the developed sensor (comparison of different technologies for the embedded sensitive part)
  Improvement of the embedded multipass interferometer and comparison with a original capacitive measurement
  ATF2 beam and ground motions correlation study ongoing, feedforward implication, next campaign planned in December 2017
Conclusion

## Slide 16
Thank you for your attention