## Slide 2: Summary of Staging Consideration
H. Hayano, 07212017
CFS Conditions & cryomodule distribution
ステージングの検討は最終段階。TCMBのレビュー中。８月にLCBに報告する予定

## Slide 3
staging option name （given ｂｙ S. Michizono, 02052017）
125GeV e-
125GeV e+
Option D:
250 GeV e-
250 GeV e+
Option C:
125GeV e-
125GeV e+
125GeV e- sparse linac
125GeV e+ sparse linac
Option F:
Option E:
TDR:
125GeV e-
125GeV e+
Simple tunnel (no center wall, no facilities)
Simple tunnel
(no center wall, no facilities)
350GeV Option E’:
350GeV Option F’:
350GeV option were added
500GeV
250 GeV
less important
for staging,
cost reduction
effect are less.
125GeV e-
125GeV e+
Simple tunnel (no center wall, no facilities)
Simple tunnel
(no center wall, no facilities)
350GeV Option D’:
20.5km tunnel
33.5km tunnel
collision timing considered
33.5km tunnel
27.0km tunnel

## Slide 4
TDR cost
Subtract cost reduction of
2014-2016 TDR cost reduction and design change
Subtract cost reduction of each staging option
Subtract cost reduction by change of 31.5MV/m to 35MV/m, assuming success of 35MV/m Q0=1.6x1010 SRF HG,HQ
Estimation of cost for each staging option
How to estimate the cost of each option
Estimation of cost for each staging option
Decide working assumptions,
and cryomodule configuration,
tunnel configuration.
cost estimation conditions.
in case of 31.5MV/m
in case of 35MV/m
TDR-updated cost
each option cost
each option cost with HG HQ success
WG2
WG3
decrease of RF unit,
Nb material cost reduction,
surface process cost-reduction,
cryogenics cost reduction,
HLRF cost-increase, etc
35MV/m

## Slide 5
Working assumption (1)
(1) Considering collision timing adjustment, condition must keep in any option,
option C = remove length between PM+10 and PM+12,
and remove TDR timing adjustment,
and adjust to n=6
option D = adjust to n=10, it is option C + simple tunnel of 6477m (total).
option D’ =adjust to n=8, it is option C + simple tunnel of 3238m (total).
In TDR(Ecm=500GeV), this equation is not satisfied as follows ( additional 294m exist);
Change Request is to adopt n=10;
with putting 1473m space
in both LINAC (updated TDR)
collision condition
CDR=3238.68m
(L1 + L2 + L3’) - L4 = 10 x CDR
( L1 + L2 + L3 ) – L4 = n x CDR
n=integer
e+

## Slide 6
ダンピングリングへのビーム入射・出射
偏極電子源
5GeV 電子ダンピングリング(3.2km)
ターン部
ターン部
バンチ圧縮部
陽電子生成部
5GeV 陽電子ダンピングリング(3.2km)
バンチ圧縮部
final focus
衝突点
injection with compressed bunch spacing
extraction with long bunch spacing
In damping ring （6ns bunch spacing） : 2.3km length
beam generation （560 ns bunch spacing）
beam acceleration in Linac
（560 ns bunch spacing）
1312 bunch (220km length)
ILCのビーム加速のシーケンス
1312 bunch (220km length)
1msのビームトレインの中は
電子加速部
陽電子加速部
ー＞実に長いバンチトレイン！
バンチトレイン圧縮
バンチトレイン拡張

## Slide 7
In Option-C(Ecm=250GeV), required Linac length become half, then we can adopt n=6
( -1367.74m - 4907.8m - 202.02m) x 2 = -12955.12m = - 4 x CDR
remove L (PM+10 – PM+12) = 4907.8m
remove 1367.74m
at BDS entrance
(timing adjustment)
remove 202.02m at end of Linac area.
L3 is shortened by 4 x CDR , it means LINAC length is shortened by 6477.56m
PM-8
PM-10
PM-12
PM+8
PM+10
PM+12
PM+13
PM-13
4907.8m
4907.8m
TDR
4911.6m
3413.8m
2334.9m
4795.2m
put 1473m
by change Request
put 1473m
by change Request
1375m
1264m
1375m
1264m
n=10
Shortning the e+ LINAC length is possible
as a unit of CDR /2 = 1619.34m.
Keep the same length of e- LINAC
for the symmetric collision energy.

## Slide 8
Working assumption (2)
(2) Keep Energy Reach Margin enough safe to reach target energy (250GeV).
(1) Module margin : margin to reach the target energy of the target experiment (0% in TDR)
(2) Availability margin : margin to compensate cryomodule trip (1.5% in TDR, ~3 RF unit trip )
(3) Space margin : cryomodule space to be installed more cryomodule in future.
*Anytime 0.5% is required in the operation with cavity phase offset.
3 RF unit margin correspond to 3% for Ecm=250GeV
2.5% module margin(3.1GeV each) for Ecm=250GeV
Total margin: 1.5%+ 0.5% = 2% for TDR Ecm=500GeV
2.5% + 3% + 0.5% = 6% for Ecm=250GeV, Option C
(3) In case of HG,HQ R&D success;
HG HQ upgrade :from 31.5MV/m Q0=1E10  35MV/m Q0=1.6E10 by N-infusion.
Same RF unit configuration, but increase of klystron output to 11MW, 1.75ms.
Consider decrease of number of RF unit for 35MV/m.
The length of tunnel is kept the same as 31.5MV/m.
for enough positron production and meaningful energy reach of Higgs physics

## Slide 9
Working assumption (3)
(6) Adopt CR0009 and CR0014 for cryogenics. The access hall is re-considered
with this design change. Angle cross with Linac tunnel and access tunnel
for cryomodule carry in, is considered.
(8) Two Vertical shaft access to detector hall is assumed.
(10) Number of beam dump and power of them proposed by Yokoya are adopted.
(7) Linac central shield wall is 1.5m thick. Total width of Linac tunnel is 9.5m.
(5) Maximum cryo-line length of one cryogenics is 2.5km+/-10%, the same as TDR.
(9) Design change of positron side BDS tunnel and injector-linac position are adopted.
(4) Only 5Hz Linac operation is considered (not 10Hz).
This determines the interval of the access point, such as PM+/-8, PM+/-10, PM+/-12

## Slide 10
Working assumption (4)
(14) Simple tunnel means: normal wall finish, but no central shield wall,
no AC power line, no cooling water line,
however air-condition, lighting and water drain are installed.
(15) Digging tunnel during accelerator operation without serious interference.
(16) Keep the Damping Ring circumference. No design change for DR.
(12) Remove access tunnels at turn-around (PM-13 and PM+13) of TDR tunnel,
not for staging tunnel.
(13) One water-drain-tunnel is considered in the collision point, not at PM-13/PM+13.
(11) TDR-undulator-based positron is kept in this study.
The length of undulator is streched to 231m from 147m with 125GeV beam.
This determines energy sensitivity of positron production
This determines the requirement of collision timing condition.

## Slide 11
PM-8
PM-10
PM-12
PM+8
PM+10
PM+12
PM+13
PM-13
IR
cryomodules
99
189
189
189
189
99
180
189
189
189
E gain (GeV)
28.1
53.6
53.6
53.6
53.6
28.1
51.0
53.6
53.6
53.6
51
51
10.0
10.0
4907.8m
4907.8m
Ecm=500GeV
Ecm = 500GeV
TDR
BC
BC
RF unit
42
42
42
42
22
42
42
42
40
22
17
24
8
24
8
e-inj
e+inj
17
SRF 31.5MV/m
2509.7m
129.3m
129.3m
4911.6m
3413.8m
2334.9m
4795.2m
2509.7m
Cavity active length = 1.0385m
Energy gain by 1 cavity = 31.5*1.0385 = 32.7 MeV
Energy gain by 1 RF unit = 32.7 MeV * 39 =1.2753 GeV
length of 1 RF unit = 58.3m
5.0
5.0
Total length of tunnel = 15872.2m+14676.9m+1473m+1473m=33495m
put 1473m
by change Request
put 1473m
by change Request
1375m
1264m
1375m
1264m
TDR Cryomodule configuration

## Slide 12
Keep BDS tunnel length as TDR, but put verical bend 87.5m on both entrance of BDS
There is no vertical bend in the optics deck.
ML tunnel should be along geoid
ML tunnel should be along geoid

## Slide 13
emit
ML
BC2
BC1
EMIT
SPIN
TURN
LAUNCH
BC2
BC1
spin rotator
LAUNCH
167.6m
818.6m
230.6m
45.1m
77.8m
turn around
~92m
1264m
e+ ML
This is the same length for e- side and e+ side,
We keep this section same in option C,
except EMIT part.
e+ Main Linac end region details
PM+12
1454m
turn-around and bunch compressor
We will touch the ML length for staging.
We will touch this length for staging, too.

## Slide 14
Cavity active length = 1.0385m
Energy gain by 1 cavity = 31.5*1.0385 = 32.7 MeV
Energy gain by 1 RF unit = 32.7 MeV * 39 =1.2753 GeV
length of 1 RF unit = 58.3m
SRF 31.5MV/m
Cavity active length = 1.0385m
Energy gain by 1 cavity = 35.0*1.0385 = 36.3 MeV
Energy gain by 1 RF unit = 36.3 MeV * 39 =1.418 GeV
length of 1 RF unit = 58.3m
SRF 35MV/m
Parameters for staging RF unit count
RF unit
RF unit
58.3m
58.3m
“a Pair of RF units” is the fundamental unit of Main Linac Accelerator

## Slide 15
PM-X
PM-10
PM-12
PM+8
PM+10
PM+12
PM+13
PM-13
IP
4907.6m
4907.8m
Ecm = 500GeV
TDR Recent Optics Deck (M. Woodley)
2639.6m
6318m
3401.5m
3729.2m
4795.1m
2718m
Total length of tunnel = 17266.9m+16149.9m=33417m
1454m
1264m
1375.6m
1264m
(2015 Okugi BDS) + 87.5m = 2361.46m
3401.5m + 87.5m = 3489m
delta-L = -1367.74m
remove this length for option-C
delta-L = -4907.6m
timing path length is matched with n=10
collision condition
CDR=3238.68m
( L1 + L2 + L3 ) – L4 = n x CDR
( L1 + L2 + L3 ) – L4 =(L1’+87.5)+L2+(L3’-1367.74x2-4907.6x2 -X) – (L4’+87.5)
=(L1’+L2+L3’)-L4’ -( 12550.68m +X)
=10 x CDR - 4 x CDR
= 6 x CDR
remove timing adjust
6318m – 1367.74m = 4950.26m
remove this length
for option-C
delta-L = -4907.6m
4 x CDR=4 x 3238.68m = 12550.68m + X
X = 404.04 m
2718m – 404.04m/2
=2516m
Option C with n=6
2639.6m
– 404.04m/2
=2437.48m
manipulation details for option C CFS configuration

## Slide 16
LINAC configurations for each staging option
(number of RF unit, length of tunnel are considered for each option.)

## Slide 17
Option C

## Slide 18
Option C
PM-8
PM-10
PM-12
PM+8
PM+10
PM+12
IR
cryomodules
189
189
180
189
E gain (GeV)
53.5
53.5
51.0
53.5
Ecm=250GeV
12.8
10.0
12.8
10.0
45
45
BC
BC
RF unit
42
42
42
40
10
17
24
8
24
8
e-inj
e+inj
51
51
17
10
= e+ 132.3GeV
e- 134.8GeV =
5.0
5.0
4950.26m
3489.0m
2361.46m
4795.2m
2437.58m
2516m
Total tunnel length = 20549.5m
(PM-0)drain tunnel
(20.5km)
module space
180
189
90
51
189
189
90
24
51
24
583m space
583m space
SRF 31.5MV/m
ECM=250GeV
+5.8%margin
module space margin
for option C, 31.5MV/m
module space margin
for option C, 31.5MV/m

## Slide 19
Option D

## Slide 20
PM-8
PM-10
PM-12
PM+8
PM+10
PM+12
IR
Ecm=250GeV
4950.26m
3489.0m
2361.46m
4795.2m
2437.58m
2516m
Ecm = 250GeV tunnel=500GeV length, accelerator at downstream
Option D
SRF 31.5MV/m
tunnel total length = 17353.8m+16149.7m=33503.5m
6477m
6477m
simple tunnel
Simple tunnel
4085.2m
2391.8m
4907.8m
4907.8m
4006.8m
2470.22m
(33.5km)
simple tunnel length = 6477m+6477m=12954m
(12.9km)
PM+13
PM-13
(n=4 extension on both end)
cryomodules
189
189
180
189
E gain (GeV)
53.5
53.5
51.0
53.5
Ecm=250GeV
12.8
10.0
12.8
10.0
45
45
BC
BC
RF unit
42
42
42
40
10
17
24
8
24
8
e-inj
e+inj
51
51
17
10
= e+ 132.3GeV
e- 134.8GeV =
5.0
5.0
module space
180
189
90
51
189
189
90
24
51
24
+5.8%margin
module space margin
for option C, 31.5MV/m
583m space
583m space
module space margin
for option C, 31.5MV/m

## Slide 21
Option D’ 350GeV tunnel

## Slide 22
PM-8
PM-10
PM-12
PM+8
PM+10
PM+12
IR
Ecm=250GeV
4950.26m
3489.0m
2361.46m
4795.2m
2437.58m
2516m
Ecm = 250GeV tunnel=350GeV length, accelerator at downstream
Option D’
SRF 31.5MV/m
tunnel length = 14114.8m+12910.7m=27025.5m
3238m
3238m
simple tunnel
Simple tunnel
(27.0km)
simple tunnel length = 3238m+3238m=6476m
(6.5km)
4907.8m
4907.8m
(n=2 extension on both end)
cryomodules
189
189
180
189
E gain (GeV)
53.5
53.5
51.0
53.5
Ecm=250GeV
12.8
10.0
12.8
10.0
45
45
BC
BC
RF unit
42
42
42
40
10
17
24
8
24
8
e-inj
e+inj
51
51
17
10
= e+ 132.3GeV
e- 134.8GeV =
5.0
5.0
module space
180
189
90
51
189
189
90
24
51
24
+5.8%margin
module space margin
for option C, 31.5MV/m
module space margin
for option C, 31.5MV/m
583m space
583m space

## Slide 23
Option E
less important
for staging; cost reduction effect is small
TDR updated tunnel & place SC-ML accelerator upstream

## Slide 24
PM-8
PM-10
PM-12
PM+8
PM+10
PM+12
IR
cryomodules
189
189
180
189
E gain (GeV)
53.6
53.6
51.0
53.6
Ecm=250GeV
12.8
10.0
12.8
10.0
45
45
BC
BC
RF unit
42
42
42
40
10
17
24
8
24
8
e-inj
e+inj
51
51
17
10
= e+ 132.4GeV
e- 135.0GeV =
5.0
5.0
4911.6m
3413.8m
2334.9m
4795.2m
Ecm = 250GeV tunnel=500GeV length accelerator upstream
Option E
4907.8m
129.3m
2509.7m
4907.8m
2509.7m
129.3m
932.7m
932.7m
4897.2m
4897.2m
SRF 31.5MV/m
Total length of tunnel = 15872.2m+14676.9m+1473m+1473m=33495m
put 1473m
by change Request
put 1473m
by change Request
place SC-ML accelerator upstream

## Slide 25
Option F
less important
for staging; cost reduction effect is small
TDR updated tunnel & place SC-ML accelerator sparse cut

## Slide 26
PM-8
PM-10
PM-12
PM+8
PM+10
PM+12
PM+13
PM-13
cryomodules
E gain (GeV)
4907.8m
4907.8m
BC
BC
RF unit
20
22
20
22
10
22
20
20
20
10
17
24
8
24
8
e-inj
e+inj
17
SRF 31.5MV/m
2509.7m
129.3m
129.3m
4911.6m
3413.8m
2334.9m
4795.2m
2509.7m
5.0
5.0
Ecm = 250GeV tunnel=500GeV length accelerator sparse
Option F
Ecm=250GeV
12.8
25.5
25.5
10.0
12.8
28.1
25.5
10.0
45
45
51
51
99
90
99
99
90
90
90
25.5
28.1
28.1
25.5
90
Place SC-ML accelerator sparse cut, for 10Hz operation possible
= e+ 132.4GeV
e- 135.0GeV =
IR
Total length of tunnel = 15872.2m+14676.9m+1473m+1473m=33495m
put 1473m
by change Request
put 1473m
by change Request

## Slide 27
ILC staging Cost estimation Conditions

## Slide 28
Conditions
(1) Estimate cost with ILCU unit for;
TDR-updated, staging option each with 31.5MV/m gradient
(2) Estimate cost for accelerator part;
using RF unit cost and other unit cost calculated from TDR,
decrease TDR cost by subtracting decreased number of units.
( ignor mass-production effect
which will be different for number of production.)
(3) Consideration items for accelerator part;
Decrease number of RF unit (cavity&cryomodule, klystron, modulator,
waveguide,LLRF, installation)
Decrease number of cryogenics (cooling power is the same as TDR)
Add simple beam line for open space of cryomodules
Decrease of RTML-return line length
Increase number of positron undulator
Decrease of beam dump power for BDS tune-up

## Slide 29
(4) Estimate cost for CFS part;
Because of TDR estimation method is not relevant to decomposition,
calculate the CFS cost option by option.
ignore the cost difference depending on the length.
(5) Consideration items for CFS part;
Decrease of number of access-hall cavern
Decrease of number of access-tunnel
Decrease of number of surface access-station
Decrease of utility devices in the surface access-station and cavern
Decrease of Main Linac Tunnel length
Decrease of Utility device, AC power cable, water pipes
of cut Main Linac Tunnel
Increase of simple tunnel
(6) Estimate cost for High-Q High-G R&D success;
If the R&D success, consider cost reduction effect
on the change of RF unit cost and decrease number of RF unit.
No change for CFS part.

## Slide 30
ILC staging Unit Cost

## Slide 31
Details of calculations
“TDR_Value_Matrix-ay170119” = cost reference
geometry of RTML beam line = from “geom-pLET-tape.csv”
consider “eLET”, the same as “pLET”
pLET=positron :DR exit - RTML - turn around - BC - Main Linac - BDS
eLET=electron :DR exit - RTML - turn around - BC - Main Linac - BDS
ILC staging Unit Cost

## Slide 32
すみません。コスト情報は開示できません。

## Slide 33
すみません。コスト情報は開示できません。

## Slide 34
すみません。コスト情報は開示できません。

## Slide 35
すみません。コスト情報は開示できません。

## Slide 36
すみません。コスト情報は開示できません。

## Slide 37
すみません。コスト情報は開示できません。

## Slide 38
すみません。コスト情報は開示できません。

## Slide 39
Summary of WG2 : CFS staging

## Slide 40
(1) We examined the conditions to be considered for the staging,
such as, collision timing condition, energy margin,
cryoline length, undulator length, access point intervals,
RF unit arrangement, etc.
(2) CFS configurations for option C, option D and D’ are proposed.
option E and F configurations are also proposed.
(3) Cost estimation conditions are examined.
(4) Unit Cost estimation & cost reductions are examined.
The calculation is under cross-checking.
Reduction of common part is under discussion.

## Slide 41
End of Slide