## Slide 1: Cost Comparison of Undulator and e-Driven Systems
K. Yokoya
2017.10.12. Positron WG.
This is basically the same as my talk in the Cost Review Meeting with LCB and LCC on Sep.26 at KEK

## Slide 2: Contents
Cost of e-driven system
Cost of undulator system: What’s in TDR?
Basic cost comparison
First stage cost
Luminosity upgrade
No technology discussion

## Slide 3: Basic Assumptions for e-Driven Scheme
Number of bunches per pulse 1312
Number of positrons per bunch 3x1010 (incl. margin)
Beam pulse structure
  Repetition 5Hz : 200ms interval
  20 times 0.48ms pulse in 63ms (300Hz)
  Bunch distance 6.15ns
  No pulse in the rest 137ms
  Electron spot size on the target 2mm (RMS)
target
3GeV S-band NC
drive linac
solenoid
AMD (FC)
g and e- dump
chicane
L-band SW NC
capture cavity
5GeV L+S band NC e+ linac
energy compressor
Damping Ring
e+ dump

## Slide 4: Electron Drive Linac
3GeV sufficient owing to nb = 1312 (4.8GeV for nb = 2625)
Bunch charge 2.4nC (peak current 0.39 Ampere)
S-band photo-cathode RF gun
 | unit cost | # in RF unit | # of RF units | cost sum
Electron gun |  |  |  | 6.24
Klystron | 0.285 | 2 | 16 | 9.12
Modulator | 0.3972 | 2 | 16 | 12.71
Circuit | 0.3487 | 1 | 16 | 5.58
Acc. Structure | 0.1806 | 4 | 16 | 11.56
Vacuum | 0.22 | 1 | 16 | 3.52
Sum |  |  |  | 48.76
Include others (magnets, vacuum, construction, etc)
Total cost 58.38 OkuYen
80MW klystron drives two 3m structures
60+4 (spare) 3m TW structure
Total length 255m including RF gun and matching section
Major cost drivers

## Slide 5: Target System
Electron spot size on target 2mm r.m.s.
  Larger spot needed for for nb = 2625
Rough cost estimation
 | note | cost (OkuYen)
Solenoid (incl. PS) | longer by 20% than undul. | 10.00
Flux concentrator (incl. PS) | ~5.2OkuYen for undul. | 3.00
Remote handling | ~1.2OkuYen for undul. | 2.00
target | ~6.4OkuYen for undul. | 1.60
Sum |  | 16.50

## Slide 6: L-band Capture Linac
L-band SW NC
 | unit cost | # of units | cost sum
Klystron | 0.285 | 18 | 5.13
Modulator | 0.3276 | 18 | 5.90
Circuit | 0.088 | 18 | 1.58
Acc. Structure | 0.3224 | 2x16 | 11.61
Vacuum | 0.15 | 18 | 2.70
Sum |  |  | 26.82
Including others (magnets, construction, etc)
Sum is 32.80 OkuYen

## Slide 7: Booster
 | unit cost | # in RF unit | # of RF units | cost sum
L-band section |  |  |  | 
Klystron | 0.285 | 2 | 36 | 20.52
Modulator | 0.3276 | 2 | 36 | 23.59
Circuit | 0.3937 | 1 | 36 | 14.17
Acc. Structure | 0.2621 | 4 | 36 | 37.75
S-band section |  |  |  | 
Klystron | 0.285 | 1 | 23 | 6.56
Modulator | 0.3972 | 1 | 23 | 9.14
Circuit | 0.3424 | 1 | 23 | 7.88
Acc. Structure | 0.1329 | 4 | 23 | 12.23
Magnets incl. chicane) |  |  |  | 7.02
Vacuum | 0.185 |  | 59 | 10.92
Sum |  |  |  | 149.66
Including others, sum is 158.84 OkuYen

## Slide 8: Energy Compressor
 |  | cost sum
Klystron | 3 units | 0.85
Modulator | 3 units | 0.98
Circuit | 18 | 0.67
Acc. Structure | 2m structure x6 | 1.52
Vacuum |  | 0.48
Magnets (incl.PS) |  | 1.18
Sum |  | 5.68
Including others, the sum is 6.27 OkuYen

## Slide 9: Sum of Accelerator System
Electron drive linac (incl. electron gun) | 58.38
Target system (excl. linac) | 16.50
L-band capture linac | 32.80
L+S band booster linac (incl. chicane) | 158.84
Energy compressor | 5.68
others | 
Sum | 272.2
Others should include (but level of a few OkuYen)
  photon&electron dump after capture linac
  positron tuning dump
  Electron dump right after drive linac (perhaps needed)
  Beamline from end of energy compressor to DR

## Slide 10: CFS Cost for e-Driven Source
The required width of tunnel is quite complex. There is no definite design in the positron source region even for the undulator scheme.
The RF source components for NC linac occupy the space in service tunnel more densely than SC components for undulator system, but detailed consideration including the transportation is necessary
For upgrade to 2625 bunches some more space for the mudulators may be reserved due to the longer beam pulse (0.48ms  ~1ms)
For simplicity here we assume a slightly increased cost per longitudinal length due to the larger power consumption and cooling water system.

## Slide 11: Cost Comparison Policy
We estimated the cost of the accelerator components of e-driven system in JYen, as we saw.
It is more convenient to convert the undulator scheme cost in ILCU in TDR into JYen than the other way
We use the same policy which we used when we converted TDR cost in MILCU to JYen for MEXT 1 MILCU = 1.09 OkuYen for tunnel civil engineering 1 MILCU = 1 OkuYen for CFS others and components

## Slide 12: Cost of Undulator System
TDR quotes 228MILCU as the value of accelerator components and 72MILCU for the CFS for the undulator positron source.
However
  There are several design changes since TDR
  We could not reproduce 72 MILCU for CFS from other data. We will not use this number.
  For the purpose of comparison with the e-driven system, numbers of items which are included in other area systems have to be modified

## Slide 13: Change of Undulator System Since TDR
The undulator section must be lengthened 147m231m for positron production at Ee=125GeV
  TDR adopted 10Hz operation with 147m undulator
The beam dump of spent electron after photon production is needed for 10Hz operation. This will not be built in the first stage.
Auxiliary positron source will not be constructed, perhaps (majority of CRWG. It is not useful enough)

## Slide 14: Items that must be included as undulator system cost
In TDR many items needed for undulator system are included in other area systems, because there was no concept of “comparison”
The electron loses 3GeV in the undulator. This must be compensated for in the electron main linac (this is included in the value of ML in TDR). Also, RTML beam line cost should be added, though small.
After the undulator the electron beam is separated from the photon beam by a dogleg. The cost of dogleg is included in BDS in TDR
  The actual dogleg which has been re-designed is much shorter for Ee=125GeV because photon emission angle is larger

## Slide 15: CFS Cost for Undulator Scheme
The tunnel length for the undulator scheme in TDR is 1678m. 40 OkuYen/km x 1678m = 67 OkuYen
  The tunnel extention for the undulator length 147m  231m is already included in the tunnel
ML tunnel cost for the 3GeV compensation
CFS cost for the dogleg is already included in positron source in TDR

## Slide 16: Basic Cost of Undulator Scheme (for comparison with e-driven)
values were converted from MILCU to OkuYen
 | Accelerator | CFS
TDR | 227.5 | 67
Longer undulator | 13.0 | 0
3GeV compensation | 27 | 7.3
Dogleg | 21 | (1)
Beam dump for 10Hz | - 7.7 | 0
Auxiliary positron source | -5.9 | 0
SUM | 273.9 | 74.3
(1) CFS cost for dogleg is already included in TDR

## Slide 17: Comparison of the Basic Cost
 | Undulator | e-Driven
Accelerator | 274 OkuYen | 272 OkuYen
CFS | 74 OkuYen | 44 OkuYen
Sum | 348 OkuYen | 316 OkuYen

## Slide 18: Implementation in Staging
Up to this point we naively estimated the cost difference, which is more or less independent of the scenario
Now, there are several more points that must be considered when we take into account the staging scenario (higher lumi, higher energy).
In particular, what must be estimated is the case when we start with the e-driven source. Depend on the order of upgrade undulator & higher lumi & higher energy

## Slide 19: Questions (1)
The following items might be accounted for the cost comparison.
The 250GeV stage that we are studying now (option C, Option D) includes some empty tunnel for global timing adjustment for undulator scheme, which is not necessary for e-driven case. Should we eliminate it from the beginning?
  Rigorously speaking, the timing constraint is necessary in the positron wing only. The empty tunnel in the electron side is added for future extension to higher CM energy
  The empty space is larger if we assume 35MV/m rather than 31.5MV/m. Can we cut this space? (less margin for 250GeV)

## Slide 20: Questions (2)
Should the space of the undulator (and subsequent photon drift) be reserved for later upgrade?
  The tunnel of this region is laser-straight in TDR. Presumably, we can manage from beam dynamics view point, even if it is bent. (BDS part must still be laser-straight)
  Note: to reserve this space does not immediately mean that we can go to undulator scheme any time
Should the dogleg of electron beam line after undulator be eliminated (different tunnel layout)? This brings about further cost reduction but a pair of doglegs (not a single dogleg) would be needed for later upgrade to undulator source if it is not implemented.

## Slide 21: 250GeV Stage for Undulator Scheme
Option C
Not for timing. Not included in the comparison
Null Module Space
1049m (35MV/m)
583m (31.5MV/m)
e+ ML
e- BDS tunnel 2.85 km
E-drop
compensation
3 GeV, 138 m
e+ BDS tunnel 2.25 km
IP
e- ML tunnel
e+ ML tunnel
undulator
e+ source
1.678 km (TDR)
Null Module Space
1049m (35MV/m)
583m (31.5MV/m)

## Slide 22: Tunnel for e-Driven Scheme
With undulator/dogleg space
Without undulator/dogleg space
e- BDS tunnel 2.85 km
e+ BDS tunnel 2.25 km
IP
e- ML tunnel
e+ ML tunnel
E-driven
e+ source
1.05 km (v8.3)
E-driven
e+ source
1.05 km
IP
e- ML tunnel
e+ ML tunnel
e- BDS tunnel 2.25 km
e+ BDS tunnel 2.25 km

## Slide 23: Final Cost Comparison
(1) components+CFS, including 3GeV compensation, dogleg
(2) Assume the space for undulater+photon drift is eliminated. If reserved, the cost increases by ~23 OkuYen
(3) CFS + RTML beam line + main beam line. Only the positron wing
 | Undulator | e-Driven
Basic cost (1) | 348 | 316 (2)
Empty space for timing (3) for 31.5 MV/m | 26 | 
for 35 MV/m | 46 | 
Sum for 31.5 MV/m | 374 | 316
35 MV/m | 394 | 316

## Slide 24: Luminosity Upgrade (1)
Here, we cannot avoid mentioning the technology
Basic change for upgrade 13122625 bunches
  Reinforce main linac RF system (common to und.&edriven)
  Electron damping ring (common to und.&edriven)
    More RF system
    Faster injection/extraction kicker
  Positron damping ring
    Same as electron DR if the e-cloud instability allows doubled beam current.
      The first stage has factor ~3 margin to the instability. So, high possibility to double the bunches
      We will get sufficient info from superKEKB and 1st stage ILC
    If not, add one more positron DR. The room reserved.

## Slide 25: Luminosity Upgrade (2)
Required change for e-driven source
  Add one more positron DR (independent on electron-cloud)
    Beam-loading compensation difficult with 3ns bunch spacing
    ~166 MILCU
    Might be possible with one e+ DR if not doubling the bunches
  Increase the energy of drive electron 3  4.8GeV
    ~ 31 OkuYen (simple scaling)
    Tunnel length extension unnecessary (determined by BDS length)
  Re-inforce modulators of drive linac and booster
    due to longer beam pulse
    Assume tunnel width is large enough
Required change for undulator source
  Target technology not confirmed yet
    Target wheel would be heavier
  To add positron DR or not depends only on the electron-cloud issue
  Re-inforce RF of booster linac