## Slide 1: Micromegas modules
P. Colas, D. Attié, S. Ganjour
(contribution from M. Zito and S. Suvorov
LCTPC collaboration meeting, Nov. 29,2017

## Slide 2: dE/dx analysis
With MM test beam data from 2015 by S. Suvorov a Russian student (from T2K)

## Slide 3: Micromegas Large Prototype overview
Endplate with 7 modules
each module has 24 rows x 72 columns

## Slide 4: ILC-TPC raw data
Event display

## Slide 5: dE/dx study
Perform the study similar to the one for the T2K TPCs (Claudio TN-001)
Method:
  For each pad take maximum charge from ADC ()
  Sum up pads in a row to make a cluster ()
  For each track sort in increasing order
    (N clusters per track)
  Take first clusters.
  Truncated mean energy per cluster
  First look at the resolution.
  Vary to understand the influence on the results
  Calculate independent from the some calibrations needed

## Slide 6: 2015 LP TPC Micromegas samples
Lots of different configuration tested with beam
For the 1st look use a scan over drift length
plots in this talk are mainly for module 0

## Slide 7: ILC-TPC event selection
For first look PID study need:
  one track per event (per FEM)
  long enough track
Selection:
  Look at maximum gap between pads hit in a row
  Look at track length (number of rows)
FEM 0 selection results: Events in sample: 46000
Not empty fem0: 44224
< 2 tracks : 37151
> 20 rows: 36146

## Slide 8: Charge per row (cluster)
Look at the most probable charge per cluster in a row
Edges of module demonstrate lack of charge (Electric field inhomogeneity)
pads at edges collect ~half of charge compared to center
Exclude 1st and last row for dE/dx estimations
Typically 1-4 pad per cluster
charge per cluster (row 10)
MPV from landau
row number
row number
maximum bin

## Slide 9: Charge cut
Reminder about dE/dx study plan:
  Take first clusters.
  Truncated mean energy per cluster
Need to define
Resolution from Gaussian fit
T2K value is 0.7 Still make sense!

## Slide 10: First results
Applying calculation method to the selected events
gives the best resolution
Truncated charge
Truncated charge per cluster
Gaussian and FWHM calculations give ~same results ~14% for 24 rows FEM (~17 cm)
for T2K TPCs 72 pads (~80 cm) have ~6.5% For ILD TPC track length ~120 cm : ~5.0%

## Slide 11: First results
Drift distance, cm
PID resolution
Charge per pad is calculated as maximum ADC
Maximum ADC can depend on drift distance  can effect PID resolution
No dependence observed  is good enough

## Slide 12: Summary
LC-TPC samples are used for dE/dx resolution estimation
the first estimation of the dE/dx resolution was done : 5.0 %
TODO:
  We still have:
    other module  work started some very preliminary results obtained
    other data samples (voltage, beam position, peaking time)
    other technical details  understand the possible dependence
  Calibration is necessary

## Slide 13: Encapsulated resistive foil Micromegas with reverse polarization
Reserved a test beam period at DESY to test 3 to 4 modules with several improvements:
  Better pad connections (threaded stiffener glued on PCB, under mechanical test, electronic test in 1 or 2 weeks)
  Grounded mesh, anode at +400 V
  (should give less noise and less
  distortions)
  -- DLC delivered (2.5 Mohm/sq)
  -- same test going on for T2K
  upgrade with cosmic rays (2
  modules ordered, one with
  annealing at 210 °C to reach 500 KOhm

## Slide 14: Cosmic-ray setup (Boris Tuchming)
There is a cosmic test permanently going on in Saclay (so-called FCC test)
We hope to be able to test 4 new modules there before going to the test beam.