DAQ status and plans
- DAQ Hardware
- Moving stage (MIP calibration)
- (semi-)Online Software
Jiri Kvasnicka
AHCAL meeting
Tokyo
25.9.2017

---
DAQ hardware: updated TODO list
- CCC (clock and control card)
  - BUG (?): Trigger validation LVDS receiver recovery not working properly, even after a fix.
- LDA (Link Data aggregator)
  - Wing-LDA: 2nd FPGA (to get >24 layers)
  - Improved TCP performance (otherwise LED calibration
    too slow)
  - Data Backpressure mechanism (not enough memory
    to store a complete readoutcycle for more than >5 layers)
- DIF (Detector InterFace):
  - Protocol change: backpressure mechanism
  - 40 MHz clock gating (noise+power reduction)
  - Trigger validation timing
  - Nice-to-have: parameter-controlled number of readout chains
- BIF (Beam Interface, based on AIDA mini-TLU)
  - Need to record closely timed signals from more inputs reliably (Investigated early 2017, not easy)
CCC
Trigger
Spill
…
LDAs
BIF
LDA
PC
...
Up to 96
DIFs
DIF
…
Up to 72
SPIROCs
spiroc
36
SiPMs

---
Moving stage remote control
- Two 20mA TTY/Ethernet devices arrived on Dec5 (Tuesday) from Marcel Stanitzki
- Plug&Play implementation (+ a week of playing in June 2017)
- EUDAQ producer implemented during TB
  - Sets the position according to the configuration file
  - Readback position stored in the EUDAQ event (start + every 10 s)
  - https://github.com/jkvas/eudaq/tree/calice_cosmics_2017
- Precision within 72x72cm2 range: 2-3mm difference between corners
  - Not enough precision to maintain shoot-in-between-tiles position, good enough to shoot at the tile
- 90 seconds per run (includes moving, T readout and 15k evt @DESY TB)
Tile beam hit position

---
Labview readiness issues
- Labview Event display: ChipIDs only 8 bits!
- Labview forwards data without big processing (port# is in the data)
- Module naming and addressing
  - “Module” for production index
  - “Layer” for position in the stack
- Unknown bandwidth performance
  - Might be a surprise for LED calibration
DIF
DIF
DIF
DIF
DIF
DIF
DIF
LDA
Labview
EUDAQ
Slcio
convert
DIF
DIF
DIF
DIF
DIF
When labview is not fast enough

---
EUDAQ
- Working stably with cosmic teststand on windows (for weeks)
- AhcalRunControl custom runcontrol
  - Reimplemented: new run after N triggers / N seconds
  - Reimplemented: automatic reload of new configuration file
- EUDAQ extremely unstable during TB last week
  - EUDAQ 2.1 running on windows
  - Windows & labview running same notebook
  - We pushed the eudaq a bit (new run every 1.5 minutes)
  - Reason unclear (Network? Bug in EUDAQ producers? Bug in Run control auto restarting feature? Wifi?)
- Bandwidth limit not an issue (can reach 40MB/s on ntb)
- TODO
  - fix the stability
  - Chipid definition (chipid is 32-bit int in eudaq raw/slcio, no problem expected)

---
Data Quality Monitoring
- Direct streaming eudaq → DQM4HEP foreseen to be ready
  - Remi pushing strongly to be ready before summer
- We expect to have new noise frequency plots in DQM4HEP
  - Tom was supposed to work on this
  - Other option: eudaq monitor (text output, quick results, noise freq only)
- Trigger threshold monitoring (external trigger event rejection)
thr=260
thr=280(?)

---
Qasi-online monitor & Event display
- Needs modifications for 40 layers
- Speed will be sufficient?
  - Need to be as fast as the data taking
- Volunteers to take over the responsibility?

---
Discussions and ideas
- LED calibration outside a spill
  - Possible solution: a dedicated fast command (would need changes in CCC, LDA & DIF)
  - How to split the physics and calib data in eudaq? Different events → dedicated collectors?
- Run without validation
  - Not a good idea? Depends on the noise levels and trigger thresholds
- PCs: 19’’ rack mounted server?

---
First look at TDC (only 25 ns reference from LDA)

---
Summary
- Essential: backpressure of the data between LDA & DIF
  - Few weeks of work
  - Iff not done → no data for >5 layers
- Essential: 2nd FPGA of the wing-LDA
  - Iff not done → no data for >24 (22) layers
- Few things to be done to get fast LED calibration
- Help with DQM4HEP and quasi-online monitor would be appreciated

---
Backups

---
MIP position vs. preamp settings
600 fF
200 fF

---
EUDAQ2: AHCAL Event building
- Architecture: Producer(s) → Data collector → (lcio converter) → data file
  - Controlled by run control within simple states
- Simple data collectors available in EUDAQ (triggerID sync / Timestamp syn)
- Our event building is more complex → we need a custom data collector
- Slcio compatible with EUDAQ1 → analysis in DQM4HEP unchanged
AHCAL
producer
ASICs
ROC,
BXID
ASICs
ROC,
BXID
AHCAL_same_bxid
ROC
TS_start,
TS_bxid (opt. TS_trig)
triggerID
ASICs
ROC,
BXID
AHCAL_same_bxid
ROC
TS_start,
TS_bxid (opt. TS_trig)
triggerID
ASICs
ROC,
BXID
AHCAL_same_bxid
ROC
TS_start,
TS_bxid (4 us range)
triggerID
EUDAQ_evt
TrigID(Event#)
Timestamp
AHCAL custom
data collector
ROC=ROC,
TS_trig=bxid
TS
overlap
AHCAL_same_bxid
LDA
ROC,
TS_start,
TS_trig,
triggerID
LDA
ROC,
TS_start,
TS_trig,
triggerID
TrigID=
Event#
LDA TS
ROC,
TS_start,
TS_trig,
triggerID
LDA TS
BIF
ROC
TS_start
TS_trigger
BIF
ROC
TS_start
TS_trigger
BIF
ROC
TS_start
TS_trigger
BIF (opt.)
BIF (opt.)
Telescope
producer
Telescope
Mimosa
Event#
BIF
producer
Mimosa
Event#
Telescope
Event#
AHCAL data from Labview

---
BIF (Beam Interface): Timestamping external signals
- Modified firmware of the AIDA mini-TLU
  - Receives AHCAL clock
  - Knows AHCAL fast commands from HDMI
- Records timestamps from 4 inputs (lemo)
  + start&stop of acquisition
  - Estimated time jitter: 1 ns
- acquisition is gated (=records only when AHCAL active)
- Implemented in the “slave mode” - acts like another LDA/DIF
Trigger
Spill
CCC
…
Up to 8
LDAs
LDA
PC
beam
triggers
BIF
DIF