## Slide 1: MDI Planning (What should we do if Project Approval & Funding occur?)
T. Markiewicz/SLAC
ALCW 2018, Fukuoka, Japan
2018-05-31
Marty Breidenbach (SLAC)
Marco Oriunno (SLAC)

## Slide 2: Preparing for the Preparatory Phase of ILC
List the fundamental shared design choices made in the long process of bringing the ILC to a reality
What was chosen and why (briefly)
Which choices, if any, should be re-evaluated
  This partly so that the next generation who will see the project to completion “own” those choices
Which choices have been so “baked-into” the design that they should not be questioned
Documentation for choices made tends to be scattered over time & space
List MDI Engineering Issues and R&D required before construction begins
Estimate resource & time requirements

## Slide 3: Time Scale for Design Changes

## Slide 4: List of Design Choices
Crossing Angle
Extraction line chicane
Incoming line polarimeter
L*
Common L*
QD0 Technology
Muon Walls and Backgrounds
Self-Shielding
Magnetic Fringe Field Requirements
Anti-Detector-Integrated-Dipole
One or Two Detectors
Platform or not
Underground versus Above Ground Assembly

## Slide 5: R&D List
Crab Cavity
QD0
He Distribution
Vibration & Vibration Suppression
SC Cable Design
Feedback (FONT)
Spot Size (ATF2)
Diagnostics
Polarimeters
Energy Spectrometers
Collimators

## Slide 6: Crossing Angle
History
  0 degrees TESLA
  2 degrees
  30 degrees Gamma-Gamma compatible
  20 degrees CLIC compatible
  14 degrees Current ILC
14 degrees chosen for ILC as it is thought to be the smallest crossing angle compatible with a minimum radius (30cm) compact SC Final Focus Cryostat housing both incoming and extraction QD and QF quads
Couples to L* choice
Assumed to minimize risk associated with crab cavity
Assumed that package would be mounted in endcap and of minimal diameter to maximize detector acceptance

## Slide 7: Extraction Line Chicane for Polarimeter & Energy Spectrometer
Pros
Advocated by SLC experience
Measures beam after beam-beam interaction has occurred
Cons
Large aperture dipoles with large power requirements
Radiation shielding required to handle off energy disrupted beam
Increased size of dump window
Superfluous according to advocates of Energy/Polarization in incoming beamline

## Slide 8: Incoming Polarimeter & Energy Spectrometer
Pros
Cleaner measurements made on non-disrupted beam
Advocated by proponents coming from 0 crossing angle TESLA design
Cons
Beam line length
Superfluous if you believe advocates of extraction line solution

## Slide 9: L*
Current compromise value of 4.1m
Naïve assumption that smaller L* maximizes luminosity
  Not necessarily born out by detailed studies where control of higher order optical effects dominate spot size
3.5m was consistent with smallest 14mrad crossing angle and compact SC technology developed by Parker at BNL
4.5m advocated for ILD with TPC
CLIC shows no loss of luminosity at larger L*
Mounting QD0 outside detector simplifies detector swap
Management decision (Walker, ~2014) to have common L*

## Slide 10: QD0 Technology
Direct wind compact SC magnets developed by Brett Parker at BNL
Introduced to LC Community at Snowmass 2005
Used at HERA , KEK and ??
ILC prototype begun but not completed due to funding issues
Concerns about vibration due to fluid
Other technologies researched by CLIC

## Slide 11: Muon Walls and Backgrounds
Historic SLC experience
Gaseous tracking chambers more sensitive
Design & leave space but do not implement at t=0
Expensive

## Slide 12: Self-Shielded Detectors
Probably required in any model where a “garaged” detector is being worked on while 2nd detector is taking data
Baked into design in 2-Detector push/pull model
  Too long to demount
Strong push from SLD people as SLC design had shallow tunnel
May be somewhat similar situation to the “2-tunnel” original ILC design or the Kamaboko tunnel with thick shielding wall
  “No access during beam operation” is current model

## Slide 13: Magnetic Fringe Field Requirements
Almost surely necessary to allow work on garaged detector” while IP-located detector is taking data

## Slide 14: Anti-Detector-Integrated-Dipole
Probably a detector risk/benefit choice

## Slide 15: One or Two Detectors
Much less expensive, simplified IR design if powers that be descope to one detector

## Slide 16: Platform Underground versus Above Ground Assembly
Motivated by CMS experience and CMS-like nature of ILD design
Above vs. Below ground motivated by “timing” arguments that may need to be re-evaluated once funding profiles for ILC construction are known

## Slide 17: Scope of R&D
Crab Cavity
EM design
Warm & Cold prototypes
LLRF system with adequate phase jitter
QD0
Complete QD0 prototype
Prototype with incoming & extraction line quads & all windings
Field measurements
Vibration measurements
Vibration & Vibration Suppression
Design & prototype Mover system with Feedback
SC Cable Design
SiD and ILD based on 25 year old CMS cable design
He Distribution
The He II system from the 4k cold box to the FFS is not trivial and should be identical for the two detectors.
A joint R&D opportunity, which very likely is tied to the one for QD0.

## Slide 18: Scope of R&D
Feedback (FONT)
Spot Size (ATF2)
Diagnostics
Polarimeters
Energy Spectrometers
Collimators & Dumps: Probably beyond scope of MDI