A Status report
of E-driven ILC Positron Source
ALCW2018 at Fukuoka, Japan
Masao KURIKI (Hiroshima University)

---
Introduction
- The design of the ILC positron source based on off-the-shelf components has been established.
- Optimization for 250 GeV parameter as
  - Small beam size on target for better yield. (3.5 → 2.0 mm rms)
  - Lower drive beam energy for less cost. (4.8 → 3.0 GeV)
  - Consider only the nominal parameter.
- A margin for the booster energy is now reserved.

---
E-driven ILC Positron Source
5.0 GeV
L-band + S-band NC
3.0 GeV
S-band NC
- 20 of 0.48us pulses are handled with NC linacs operated in 300Hz.
- 100 of 300 pulses are actually fired.

---
The beam handling and format
Damping Ring
Positron Booster
tp=480 ns
197 ns
81.6 ns
33 bunches
Tb = 6.15 n sec

---
Electron Driver
- 3.0 GeV Electron beam with 2.0 mm RMS beam size at the target.
- 2.4 nC bunch charge is giving 0.39 A beam loading.
- S-band Photo-cathode RF gun for the beam generation.
- 80 MW klystron-modulator drives 2 structures.
- The effective input power for each tube is 36 MW. 50 MV/tube.

---
KEK CONCEPT DESIGN 80MW S-band
RF & Solid State Modulator PARAMETERS
Main Parameters	Value	Unit
RF Frequency	2600	MHz
RF Peak Power	80	MW
RF Average Power	0.2 (12)¹	kW
Mod. Peak Power	143	MW
Mod. Average Power	1.4 (86)¹	kW
Klystron Voltage	382	kV
Klystron Current	375	A
RF Pulse width (top)	0.5	µs
Pulse Repetition Rate	5 (300)	Hz
Pulse-to-Pulse stability	<15	ppm
98x
Fig: K400-platform
¹ Corresponding to 300Hz operation
OPTIONS: Integration of …
Solenoid Power Supply
Ion Pump Power Supply
RF Drive amplifier
Cooling of Klystron (Collector, Body), Solenoid
All diagnostics and interlocks

---
- 60 + 4 (spare) of 3m S-band TW structures for the acceleration. The energy is 3.2 GeV.
- The lattice design was based on ATF linac, 4Q + 2RF(S) up to 600 MeV, 4Q+4RF(S) for other.
- The total length is 235.2 + 20 m (RF gun + matching section).
Lattice	# of cell	Cell length(m)	Section length(m)
4Q+2S	6	8.0	48.0
4Q+4S	13	14.4	172.8

---
Positron Capture Linac
- 36 L-band SW structures designed by J. Wang (SLAC) for the undulator capture section is employed.
- Two structures are driven by one 50 MW klystron.
- Surrounded by 0.5 T solenoid field.

---
Acceleration Field
  - L=1.27 m (11 cells, L-band SW)
  - R=34e+6 Ohm/m
  - P0=22.5 MW (50MW at klystron, 5MW wave guide loss).
  - 10.36 MV/tube with beta=6.0.
Single cell
Multi-cell

---
KEK CONCEPT DESIGN 50MW L-band
RF & Solid State Modulator PARAMETERS
Main Parameters	Value	Unit
RF Frequency	1300	MHz
RF Peak Power	50	MW
RF Average Power	0.125 (7.5)¹	kW
Mod. Peak Power	76	MW
Mod. Average Power	0.7 (42)¹	kW
Klystron Voltage	271.7	kV
Klystron Current	282	A
RF Pulse width (top)	0.5	µs
Pulse Repetition Rate	5 (300)	Hz
Pulse-to-Pulse stability	<20	ppm
74x
Fig: K300-platform
¹ Corresponding to 300Hz operation
OPTIONS: Integration of …
Solenoid Power Supply
Ion Pump Power Supply
RF Drive amplifier
Cooling of Klystron (Collector, Body), Solenoid
All diagnostics and interlocks

---
Capture Simulation
Red : positron
Black : electron
- 1000 electrons on target by GEANT 4.
- The positron is decelerated and bunched at the acceleration phase by phase-slipping.
- Positrons with a large z (longitudinal position) are not captured by the final acceptance, because the energy is determined by booster.
- The energy after the capture have less effect on the capture.
- The beam loading current is typically ~1.5 A, which is much less than the NLC design.
Red : Accepted
Black : not accepted
δ
z

---
At the end
of capture linac
Accelerator Aperture
δ
y
z
x

---
Booster
- A first half is implemented by L-band acc. and the last half is by S-band.
- 50MW L-band Klystron drives two L-band acc. (2a = 34 mm).
- 80MW S-band Klystron drives two S-band acc. (2a = 20 mm).

---
In Booster
Middle
End
δ
y
x
z
δ
y
z
x

---
ECS Section
ECS optimization
- ECS design R56=1.2m and R65=-0.8.
- Required voltage is 122 MeV, 3 tubes are enough.
- We need an additional RF to compensate the beam loading.

---
Limit the current
Removing "rude positrons" by collimation in the capture section (22mm rad.) and in the chicane (100 mm width) was studied.
The rude positrons are decreased 15% with 7% less yield.
Red : Accepted
Black : not accepted
Config.	Iblcap(A)	Iblbstr(A)	Yield
No cut	1.71	0.96	2.06
Cap.	1.56	0.93	2.04
Chic.	1.71	0.93	2.04
Cap. + Chic.	1.56	0.90	2.02
ｙ
ｘ
ｘ

---
2m L-band TW structure (Positron Booster)
2m L-band (1298 MHz) designed for KEKB injector.
Saw modulation:22.5 MW input with 0.78 A BL gives 14.41 MV/tube (2m)
The energy spread is zero (ideal), but the voltage is limited.
22.5 MW

---
Step Modulation
22.5 MW
Step modulation:19.54 ± 0.51 MV.
If P0 is optimized (lowered) for lower energy spread, 17.38 ± 0.17 MV.
The gradient depends on acceptable energy spread and we took 17.38 MV as our working assumption.
19.54 ± 0.51 MV.
17.38 ± 0.17 MV

---
S-band TW accelerator (Positron Booster)
- 2m S-band (2856MHz) accelerator designed for KEKB injector.
- Saw modulation:22.5 MW input with 0.78 A BL gives 23.03 MV/tube (2m)
- Step modulation gives 29.42 ± 0.69 MV.
36 MW

---
Optimization
36 MW
- Step modulation gives 29.42 ± 0.69 MV, the spread is more than 2%.
- P0 optimization does not work, because tf~tp.
- Instead, semi-Step-saw modulation was made with the peak power which is less than that for the perfect compensation.
- An example is 25.49 ± 0.23 MV.
- The accelerator voltage is determined
  by the acceptable energy spread.
25.49 ± 0.23 MV.

---
Yield variation in a pulse
- By employing the quasi-perfect BL compensation, energy for each bunch in a pulse will be varied.
- The positron yield variation by the energy variation was studied.
- The bunch energy is varied 1.2% in a pulse, that corresponds to 0.1 % after ECS.
Energy after booster (GeV)
Energy after ECS(GeV)
Energy after booster (GeV)

---
Total Length
Electron Driver
255.2 m
Positron Booster
684.8 m
 Target
Capture Linac
Chicane
63.0 m
ECS
78.2m
Total : 1081.2 m

---
An Expected Schedule on Pre- and Design Phase
Pre-Design Phase
Design Phase
We are here
Budget req. 2
Budget req. 1
2018	2019	2020	2021	2022	2023	2024
Fund.
RD
Final
Design
Conceptual Design
Const-ruction
Engineering design
Basic design
Basic plan
General drawings
Rough estimation
・const. draw.
・const. schedule
・Estimation
Construction drawings
Estimation
Call for tender, contract
Accelerator
design
Construction
Phase
Bud. Req. 1
Basic plan by consultation
Fix Spec.
Fix Layout
A rough estimation
Documentation by a consultation company to start the detail deign.
By a consultation company to define the baseline schedule and to obtain information required in the initial phase of the design.
Geological survey
Should be finished before the final design. It takes 3 years defined by law.
Environmental assessment

---
An Expected Schedule on Positron Source Design
Conceptual design
Target prototype test
Real Target design
FC driver design
Everything is ready before the Engineering design in the preparation phase.
Remote handling study
RD on joints
Radiation environment
 CFS Layout Design
Exchange Scenario
We are here
Budget req. 2
Budget req. 1
2018	2019	2020	2021	2022	2023	2024
Fund.
RD
Final
Design
Conceptual Design
Const-ruction
Engineering design
Basic design
Basic plan

---
Summary
- E-driven ILC positron source is optimized for 250 GeV ILC.
- Collimation at chicane (after capture linac) and cut by iris in the capture are effective to decrease the beam loading.
- The energy variation by the positron booster is evaluated with the quasi-perfect BL compensation.
- The yield variation due to the energy variation is 6% in full-width.
- The conceptual design should be fixed in this year.
- Everything can be ready before the engineering design in the preparation phase.

---
Beam Loading in SW Linac
Single Cell Model : Simple, but not realistic
- The field in SW accelerator
- The voltage becomes constant if
{size 24 color green { V(t) = { 2 sqrt{%beta P_0 r L }} over {1+%beta} left( 1 - e^{- {t over T_0}} right) - {rIL} over {1+%beta} left (1-e^{- {{t-t_b} over T_0}} right) }}
{size 24 color green { T_0 = {2Q} over {%omega (1+%beta)}}}
Beam Loading
RF
{size 24 color green { t_b = -T_0 ln left( I over 2 sqrt{rL over {%beta P_0} }right)}}
{size 24 color green { V_0= { 2 sqrt{%beta P_0 r L }} over {1+%beta} left( 1 - I over 2 sqrt{rL over {%beta P_0} } right) }}

---
Multi-Cell Model : More realistic
Time differential of the energy of the center cell,
Power flow to next cells
Input Power
Beam loading
WG loss
Power loss
Power flow from next cells

---
Time differential of the voltage
For the intermediate cells,
For the end cells,

---
11 linear simultaneous differential equations

---
A can be diagonalized with a orthgonal matrix R as
Because B is diagonal, the equations for V' are 11 independent linear differential equations,

---
The solution for V' is
The solution for V is expressed as a linear sum of the solution for V'

---
RF Mode and Beam Loading Mode
The total acceleration voltage is given as sum of the RF mode and the Beam-loading mode.
They are not identical, but the dominant mode is common (tau=1.22 us).
The RF mode has the second dominant mode, but nothing for BL. This gives the imperfection on the BL compensation, but the effect is not large.
RF mode
BL mode

---
Beam Loading Compensation
No big difference on the no-load voltage, but 30 % less on the heavyly loaded voltage,
The beam loading compensation works well.
Flatness is less than 0.1%.

---
Beam-loading in TW Linac
- Transient beam-loading is compensated by Amplitude Modulation.
- Acceleration voltage by a flat RF,
RF Pulse
V(no beam)
loading
V(with beam)
RF Pulse
V(beam loading)

---
Beam Loading Compensation with AM
Laplace transformation of TW accelerator voltage V(s) is
where E(s) is the Laplace transformation of applied voltage (power).
E(s) is determined to cancel s (t) dependence of V(s or t).
{size 24 color blue {E(s)}}

---
Step Modulation
Imperfection

---
Saw Modulation
{size 20 color blue {E(t)=E_0 U(t)+E_1U(t-t_f) + E_2 over t_f (t-t_f)U(t-t_f)}}
{size 20 color blue {E(s)=E_0 over s +E_1 over s e^{-st_f} + E_2 over {t_f s^2} e^{-st_f} }}

---
Actual Compensation (Trade off)
- Saw modulation is ideal, but it requires a high peak power.
- Step modulation is a replacement, but it has an imperfection (energy spread).
- If tp << tf, an optimization for P0 gives smaller energy spread.

---
What is the acceptable energy spread?
- z -d phase space distribution after booster has a larger energy spread by RF curvature.
- Imperfection of the compensation gives additional energy spread.
- The effect is not expected large, because the energy spread is compensated by ECS further.
- As our working assumption,
  1% additional energy spread
  does not affect the yield.
- If larger energy spread is acceptable,
  the accelerator voltage is gained.
1%