## Slide 1: SuperKEKB e+ source
Yoshinori. Enomoto
KEK electron positron injector LINAC group

## Slide 2
Positron production target
KEK electron/positron injector LINAC

## Slide 3
Google street view is available

## Slide 5: OUTLINE
Part 1 : status of SuperKEKB positron source
  Introduction
  Setup
  Present status
  Improvement plans
  Preparation for emergency
Part 2 : topics to be considered
  Target
  Degradation of the first ACC structure
  FC discharge
  Tunnel design
  Space for radioactive materials

## Slide 6: OUTLINE
Part 1 : status of SuperKEKB positron source
  Introduction
  Setup
  Present status
  Improvement plans
  Preparation for emergency
Part 2 : topics to be considered
  Target
  Degradation of the first ACC structure
  FC discharge
  Tunnel design
  Space for radioactive materials

## Slide 7: History of positron source in KEK
TRISTAN (1985-1994)
KEKB (1998-2010)
SuperKEKB (2016-)
electron / positron

## Slide 8
1/25
x2.25

## Slide 9
1/25
x2.25
x50 more positron injection is required
→increase bunch charge x4
→increase duty and rep. rate

## Slide 10: Injection requirement
Life | 360 s
Current | 3.6 A
Injection bunch charge | 4 nC
Injection rate | 25* Hz x 2 bunch
Injection efficiency | 50 %
Circulation frequency | 105
Present working assumption
 | SLC | LEP | KEKB | SKEKB | FCC-ee
Primary e- energy | 33 GeV | 200 MeV | 4.3 GeV | 3.5 GeV | 4.46 GeV
e- / bunch | 4.8 - 8 nC | 0.8 - 48 nC | 10 nC | 10 nC | 8.8 nC
Rep. rate | 120 Hz | 100 Hz | 50 Hz x2 | 50 Hz x2 | 200 Hz x2
Beam power | 20 - 30 kW | 1kW (max) | 4.3 kW | 3.5 kW | 15 kW
e+ yield (e+/e-) | 1.1 | 0.003 | 0.1 | 0.4 | 0.7
*total rep. rate is 50 Hz
The other 25 Hz will be used electron injection

## Slide 11: OUTLINE
Part 1 : status of SuperKEKB positron source
  Introduction
  Setup
  Present status
  Improvement plans
  Preparation for emergency
Part 2 : topics to be considered
  Target
  Degradation of the first ACC structure
  FC discharge
  Tunnel design
  Space for radioactive materials

## Slide 12: Positron source setup for Super KEKB 1
Positron target and capture section

## Slide 13: Positron source setup for SuperKEKB 2
target
BC (bridge coil)
FC(flux concentrator) head
LAS (large aperture S-band)
solenoid
FC head + BC + target = FC assembly

## Slide 14: Positron source setup for SuperKEKB 3
Φ2 mm hole for electron
W target
Temp sensor
Cooling water pipe
beam

## Slide 15: Positron source setup for SuperKEKB 4
e+
e-
target
e+
target
Electron hit small point of the target.
Positron comes from small spot.
Angle distribution is large.
Adiabatically expand position distribution.
Angle distribution decrease.
Matched to the aperture of the following LAS.
How the FC works?
Bridge coil
DC magnet
I = 600～750 A
Flux Concentrator
pulsed magnet
I = 6000～12000A
Ratio B @ target / B @ entrance of the LAS is important
stronger field is preferred in the following solenoid section
much stronger field is required @ target
Calculated by T. Kamitani

## Slide 16: Positron source setup for SuperKEKB 5
Flux concentrator method is adopted for positron source of SuperKEKB.
  Developed by SLAC in 1980’s
  In service in KEK and IHEP (china)
  Will be used in FCC-ee.
W amorphous fixed target is used.
  This is a conventional target material.
  Similar one was used in KEKB

## Slide 17: Capture section after the target 1
AC_15_1
AC_15_2
AC_16_1
AC_16_2
AC_16_3
AC_16_4
FC
+
target
AC_17_1
AC_17_2
AC_17_3
AC_17_4
AC_18_1
AC_18_2
AC_18_3
AC_18_4
solenoid
solenoid
Q
Normal
LAS
Solenoid section (15 m)
Quad section (115 m)
Electron / positron separator
 | LAS | Normal S band
Acc. Gradient (MV/m) | 14/10 | 20
Aperture (mm) | 30 | 20

## Slide 18: Capture section after the target 2
To dumping ring
1-5
1-6
1-7
1-8
Normal x 32
LAS x 10
10m
2-6
2-1
2-2
2-3
2-4
2-7
2-8
Target & FC
15m long solenoid
About 100 Quad magnet
1.1 GeV @ DR

## Slide 19: Capture section after the target 3

## Slide 20: Capture section after the target 4

## Slide 21: LAS
S. Matsumoto PASJ2014-SAP045

## Slide 22
input
output
beam

## Slide 23: OUTLINE
Part 1 : status of SuperKEKB positron source
  Introduction
  Setup
  Present status
  Improvement plans
  Preparation for emergency
Part 2 : topics to be considered
  Target
  Degradation of the first ACC structure
  FC discharge
  Tunnel design
  Space for radioactive materials

## Slide 24: Status of SuperKEKB positron source
 | Phase 1 | Phase 2 (now) | Phase 3 (design) | KEKB
year | 2016 | 2018 | 2019- | -2010
Primary electron energy | 3.4 GeV | 3.4 GeV | 3.5 GeV | 4.3 GeV
IFC | 5～6 kA | 5～6 kA | 12 kA | -
①Primary electron @ target | 6.3 nC x 2 | 6.9 nC x 2 | 10 nC x 2 | 10 nC x 2
②Positron @ entrance of DR | 1.9 nC x 2 | 2.0 nC x 2 | >4 nC x 2 | -
③Positron @ LINAC end | 0.75 nC x 2 | 1.4 nC x 2 | >4 nC x 2 | 0.5 nC x 2 1 nC x2 (design)
DR | without | With | With | without
①
②
③
x 2 means two bunch operation

## Slide 25: Charge along the beam line
Positron target
Linac end
Electron gun
Phase 1
LINAC
BT
0.75 nC

## Slide 26: Charge along the beam line
Positron target
Linac end
Electron gun
Phase 1
0.75 nC
Positron target
Linac end
Electron gun
DR
Phase 2
1.4 nC
Loss in the 3 sector decreased thanks to the DR

## Slide 27: OUTLINE
Part 1 : status of SuperKEKB positron source
  Introduction
  Setup
  Present status
  Improvement plans
  Preparation for emergency
Part 2 : topics to be considered
  Target
  Degradation of the first ACC structure
  FC discharge
  Tunnel design
  Space for radioactive materials

## Slide 28: Requirement and Improvements toward phase 3
Provide 4 nC x 2 positron 25 Hz at injection point of the LER.
  Big difference among phase 2 (0.5 nC), phase 3 (4 nC) and present (1.4 nC).
1. Increase primary electron charge and energy @ target
2. Increase positron production efficiency
3. Decrease loss between the target and the DR

## Slide 29: 1. Increase primary electron charge and energy @ target
There are 21 (+1 standby B7) acceleration unit before the target
160 MV/unit
We will re-install 1 unit in 2018
  5 % up in energy
Some units are not in full power operation
  A few % up in energy
Chart: unit # before target
| 20 | 19 | 18 | 17
1st bunch | 2 | 1.8 | 1.6 | 1.5
Positron charge @ downstream of the target
Unfortunately 1 unit was down due to water leak when we took the data
This will be repaired shortly
energy
target

## Slide 30: 1. Increase primary electron charge and energy @ target
charge
Decrease loss in the first section
  We have been trying but not easy…
Increase 2nd bunch charge
  Optimizing timing at the bunching section
Increase charge at gun
  High efficiency cathode has developed recently by the injector group
1st bunch
2nd bunch

## Slide 31: 2. Increase positron production efficiency
Parameter | simulation | Experiment
BC | 600 A | 600 A
SL_15_11 | 650 A | 600 A
SL_16_11 | 650 A | 400 A
SL_16_22 | 650 A | 400 A
SL_16_33 | 650 A | 650 A
ACC_15_1/2 | 10 MV/m | 8.5 MV/m
ACC_16_1/2/3/4 | 12 MV/m | 12 MV/m
FC current (kA) | SP_15_T_Q (nC) | SP_16_5_Q (nC) | Positron Yield
0 | 6.93 | 1.26 | 0.18
6 | 6.93 | 2.50 | 0.36
12 (expectation) | 6.93 | 3.12 | 0.45
Simulation by F. Miyahara
design
Present expectation
Increasing FC current, positron yield of 0.45 (12 kA) is expected from experimental data.
Difference from design is still not clear.
x1.25

## Slide 32: 2. Increase positron production efficiency
1 kV / turn @ 12 kA operation 6 us pulse width
Slit gap = 0.2 mm
6 us
FC current (kA)
FC current waveform measured by CT
5 MV/m

## Slide 33: 3. Decrease loss between the target and the DR
Increase some steering magnets in this section
Beam tuning and study
Better alignment

## Slide 34: OUTLINE
Part 1 : status of SuperKEKB positron source
  Introduction
  Setup
  Present status
  Improvement plans
  Preparation for emergency
Part 2 : topics to be considered
  Target
  Degradation of the first ACC structure
  FC discharge
  Tunnel design
  Space for radioactive materials

## Slide 35: Quick exchange mechanism
Before the installation of the quick exchange mechanism
(phase 1), in case of emergency on the target / FC system,
  Heavy exposure to radiation is inevitable.
  Need long (>1 month) cooling time.
The mechanism is installed
  In March 2017. (8 months after the end of phase 1 operation)
  Old assembly (used in phase 1) was replaced by new one using this mechanism.
  We demonstrated that replacement work can be done within 1 week.
Fortunately this did not happen

## Slide 36: Replacement work (March 2017)
４00uSv/h
800uSv/h
8 month cooling after phase 1 operation

## Slide 37
Water, electrical connection

## Slide 40: Evaluation of radiation
Measured by S. Matsumoto
Measured (1 pps operation)
Expected (25 pps operation)
March 2017
Radiation rate gets 1/10 at 100 hours after stopping operation
Cooling time | Radiation | dose | comment
8 months | 50 uSv/h | < 10 uSv/day | Measured in March 2017
1 hour | 3000 uSv/h | < 600 uSv/day | 
100 hours | 300 uSv/h | < 60 uSv/day | 

## Slide 41: Positron yield vs Acc voltage
 | now | -20%
1-5 | 38 kV | 35 kV (-3 kV)
1-6 | 42 kV | 39 kV (-3 kV)
1-7 | 40 kV | 35 kV (-5 kV)
ACC tube is inserted in magnets in these units.
→difficult to replace
→evaluate impact to help decision making

## Slide 42: OUTLINE
Part 1 : status of SuperKEKB positron source
  Introduction
  Setup
  Present status
  Improvement plans
  Preparation for emergency
Part 2 : topics to be considered
  Target
  Degradation of the first ACC structure
  FC discharge
  Tunnel design
  Space for radioactive materials

## Slide 43: Target consideration 1
S. Ecklund SLAC-CN-128, 1981
10 nC, 3.5 GeV→ σ(radius)=0.186 mm [D=0.37 mm]
Handbook of Accelerator Physics and Engineering 2nd edition p.556
symbol | meaning | Value
N+ | Primary electron number | 6.2x109 Q
r | Beam size (radius) | 1~0.2 mm
Cp | Specific heat | 0.138J/(g・K)
αT | expansion coefficient | 4.5 um/(m・K)
E | Young's modulus | 411 GPa
μ | Poisson ratio | 0.28
σ[kg/mm2] | r[mm] | Q[nC] | Comment
3.4 | 0.5 | 7 | Present
9 | 0.2 | 3 | RF gun (achieved)
30 | 0.2 | 10 | RF gun (initial plan)
37 | 0.18 | 10 | ρmax
Beam profile @ target
RF gun
Thermionic gun

## Slide 44
HER
LER(for e+ production）
PF-AR
PF
Thermionic e- gun
RF e- gun

## Slide 45: Target consideration 2
Calculated from cooling
water temp
5 Hz
12.5 Hz
25 Hz
0 Hz
 | Phase 2 (measured) | Phase 3
Beam power / pulse [W] | 35 | 70
Rep. rate [Hz] | 25 | 50
Beam power [W] | 880 | 3500
⊿T [K] | 30 | 120

## Slide 46: OUTLINE
Part 1 : status of SuperKEKB positron source
  Introduction
  Setup
  Present status
  Improvement plans
  Preparation for emergency
Part 2 : topics to be considered
  Target
  Degradation of the first ACC structure
  FC discharge
  Tunnel design
  Space for radioactive materials

## Slide 47: Degradation of the first ACC structure
 | 2015/12 | 2017/11 | design
KLY PS VOL | 40.1 kV | 38.0 kV | 42.0 kV
Energy gain | 40.1 MeV | 33.9 MeV | 55.8 MeV
gradient | 10.0 MV/m | 8.5 MV/m | 14 MV/m
SLED | detune | detune | tune
Energy gain of 1-5 unit was measured by
Beam position after an analyzing bend
Magnet as a function of RF phase.
1-5 unit suffer from discharge and degradation
Shower from the target might be one of the cause…

## Slide 48: OUTLINE
Part 1 : status of SuperKEKB positron source
  Introduction
  Setup
  Present status
  Improvement plans
  Preparation for emergency
Part 2 : topics to be considered
  Target
  Degradation of the first ACC structure
  FC discharge
  Tunnel design
  Space for radioactive materials

## Slide 49: FC discharge 1
FC head #4
  ～2015/9 test w/o BC @ test stand
    12 kA→OK
  2015/9 Installed into the beamline
    Discharge happened at 9.5 kA after a few days operation.
  2015/9～2016/7
    Reduced current (6 kA) operation during phase 1.
  2017/3
    Replaced by FC head #5 (with assembly #2).
Visit specialist in SLAC.
Work-hardening process is important.
External magnetic field by BC is different.
FC inside

## Slide 50: FC discharge 2
FC head #5
  2016/6
    Work-hardening process
  ～2017/3 test w BC @ test stand
    12 kA→OK
  2017/3 Installed into the beamline
    Discharge after a few days operation
  2017/3～2017/5
    Not in operation
  2017/6～2017/9
    Disassembled from the beamline
    Observed
  2017/9
    Re-installed in the beamline
  2017/10-
    6 kA operation
Reconstruct test stand
Try longer pulse operation

## Slide 51: FC discharge 3
What we plan to do in 2018
  Test with longer pulse but reduced voltage
    A modified pulsed power supply is under preparation
 | FC current | Pulse width | Power supply voltage
Now | 6 kA | 6 us | 9 kV
planned | 12 kA | 12 us | 9 kV
6 us
FC current (kA)
FC current waveform measured by CT

## Slide 52: FC discharge 4
Small discharge observed at the test stand
→no significant damage was observed this time

## Slide 53: FC discharge 5
Chart: time(x40nS)
normal
discharged
discharge→inductance decrease→current pulse width decrese
Current waveform monitor is integrated in the interlock system
→next pulse of the abnormal pulse is stopped
→minimize damage to the FC

## Slide 54: OUTLINE
Part 1 : status of SuperKEKB positron source
  Introduction
  Setup
  Present status
  Improvement plans
  Preparation for emergency
Part 2 : topics to be considered
  Target
  Degradation of the first ACC structure
  FC discharge
  Tunnel design
  Space for radioactive materials

## Slide 55: Tunnel design
Typical section
Around target
Additional radiation shield (Fe 40cm)
Enough height to crane operation
Enough width to deliver new assembly
Enough thickness to avoid additional radiation shield

## Slide 57: OUTLINE
Part 1 : status of SuperKEKB positron source
  Introduction
  Setup
  Present status
  Improvement plans
  Preparation for emergency
Part 2 : topics to be considered
  Target
  Degradation of the first ACC structure
  FC discharge
  Tunnel design
  Space for radioactive materials

## Slide 58: Space for radioactive materials
Used FC assembly is temporary kept inside the LINAC tunnel
→space is limited
→final destination have not yet determined…
→better to prepare enough space before start experiment…
Used FC assembly inside

## Slide 59: Summary
SuperKEKB positron source is in operation
  W target + FC + LAS
  Provide 1.4 nC @ linac end
  Many thing to do to reach 4 nC (design)
Present issues
  Degradation of the first acc structure
  FC discharge
For new design
  Tunnel design
  Space for radioactive materials