## Slide 1: Z resolution and event time
P. Colas, CEA/Irfu, Université Paris Saclay
With contributions from A. Bellerive, S. Ganjour, R. Mehdiyev
(No recent work)
LCTPC 2nd Topical Analysis Meeting
May 18, 2018

## Slide 2: Z coordinate given by drift time * vdrift
Origin : t zero
Every pad is connected to a sampler with a clock (25 MHz, 511 time bins, for tests at DESY with AFTER electronics)
Vdrift can be measured by different methods, or taken from simulation. It slightly depends on the row. It is affected by pressure and temperature variations

## Slide 3: Hit time determination
A hit is a cluster of several pads, each having a charge vs time information.
Multiplicity depends on RC per unit surface of the resistive-capacitive anode.
Here 2015 data, 100 ns shaping
<m>=2.59
<m>=3.61
Carbon-loaded kapton
Diamond-Like Carbon (DLC)

## Slide 4: Hit time determination
Several estimators of the hit time (implemented in Marlin, Rashid Mehdiyev)
Max bin (very crude)
Max bin fitted
Half-max bin
Weighted mean
Gaussian inflexion
Fit an helix through the hits
Calculate z-residuals of the hits to te helix
Sigma of the residuals is your z resolution (geometric mean between inclusive and exclusive residuals)
Example of COSMO data

## Slide 5: Hit time determination
Several estimators of the hit time (implemented in Marlin, Rashid Mehdiyev)
Max bin (very crude)
Max bin fitted
Half-max bin
Weighted mean
Gaussian inflexion

## Slide 6: Results
CLK
BD
z resolution is better for CLK than for DLC (‘Black Diamond’)
(CLK : 200 µm ; BD: 250 µm – at zero drift distance)
This corresponds to a time resolution of 2.9 ns per hit
DLC is found to spread more the charge than CLK, so it has a lower RC.
Effective number of electrons is rather low (9 instead of 35 as obtained from r f resolution vs z). Not clearly understood

## Slide 7: EVENT TIME
Assuming independent hits, the resolution on the time of a track of 200 hits is 0.2 ns : not enough to distinguish various particle, but very useful for matching with silicon hits (SET especially) and thus get a TPC event time.
F. Gaede, calorimetric hit time from MC truth

## Slide 8: Conclusion
Z-coordinate resolution can be as good as 200 µm (much better than requirement)
If the 200 hits on a track are independent, the track time resolution is 3ns/sqrt(200), that is 0.2 ns, offering interesting possibilities