## Slide 1: ATF Operations Meeting Friday 18th May 2018
P. Burrows, C. Perry, D. Bett, R. Ramjiawan
Results from April run

## Slide 2: Contents
IPBPM resolution
IPBPM sensitivity to angle
Measured latency of feedback system

## Slide 3: IPBPM resolution
ss = single sample
ms = multi-sample
(i.e. integration of I and Q)
dr = drift removal
All jitter runs from 1700 Thurs 19 Apr to 0900 Fri 20 Apr
With favourable beam conditions, resolutions in the 20-30 nm range achieved without too much effort

## Slide 4: Angle sensitivity
 | A | B | C
 | 0.64 mrad | 0.816 mrad | 2.053 mrad
 | 0.177 | 0.208 | 0.325
 | A | B | C
 | 0.64 mrad | 0.816 mrad | 2.053 mrad
 | 0.177 | 0.208 | 0.325
 | A | B | C
 | 0.081 /um | 0.080 /um | 0.056 /um
 | 0.277 /mrad | 0.253 /mrad | 0.157 /mrad
ratio | 0.0034 m/rad | 0.0032 m/rad | 0.0028 m/rad
 | A | B | C
 | 0.081 /um | 0.080 /um | 0.056 /um
 | 0.277 /mrad | 0.253 /mrad | 0.157 /mrad
ratio | 0.0034 m/rad | 0.0032 m/rad | 0.0028 m/rad
from R. Ramjiawan
Tilt scan: adjust individual movers by different amounts to maintain a constant vertical offset while changing tilt of BPM with respect to beam
beam
movers
BPM

## Slide 5: Angle sensitivity

## Slide 6: Feedback latency
47.6 ns
Latency = bunch spacing – delay required to reduce kick to 90% max.
from R. Ramjiawan
Bunch spacing: 100 samples (280 ns)
Delay to reduce kick to 90%: 17 samples (47.6 ns)
Latency = 280 ns – 47.6 ns = 232.4 ns.

## Slide 7: Shift request
3 shifts during week of June 11
Study: rework IPBPM electronics setup so we can monitor bunch phase and LO jitter
Also: probe maximum resolution of the new diode processors (for stripline BPMs)