## Slide 1
Previous Studies
of the Unwanted Waveform
Compiled from presentations by:
T. Bromwich, N. Blaskovic Kraljevic
FONT meeting – Monday 4th June 2018

## Slide 2: Outline
Recap from the last meeting with Alexey.
Previous studies on the 63 MHz waveform feature seen in I and Q signals:
Slides from:
  17th Nov 2015 (Neven)
  21st Dec 2015 (Talitha)
  27th Jan 2016 (Talitha)
  12th Feb 2016 (Talitha)
  4th March 2016 (Talitha)
  6th and 8th July 2016 (Talitha)

## Slide 3
Recap: Previous meeting with Alexey (16/06/17)

## Slide 4
Example Waveforms
6th July 2017
T. Bromwich

## Slide 6: Calibration with Unwanted Waveform

## Slide 8
Cable mismatches
Cables re-matched to within 2 mm
and static signal remains

## Slide 9: Cable mismatch
Cable velocity 2.381 x 108 m/s.
100 waveforms averaged on the TDR.
d is phase difference after removing integer wavelength differences.
Cables mismatched inside chamber.
Y: Within 0.38cm (10% of wavelength)
X: Within1.29 cm (31% of wavelength)
Measured cable lengths from IP BPM dipole cavities inside the IP vacuum chamber to the hybrid prior to the processing electronics using TDR.
BPM ports | Cavity to hybrid(ns) | Cavity to hybrid (m) | D Length (cm) | d (cm) | Error (cm)
IPA-X1 | 9.91 | 2.360 | 11.43 | 1.08 | 0.04
IPA-X2 | 10.39 | 2.474 |  |  | 
IPB-X1 | 10.39 | 2.475 | 0.011 | 0.11 | 0.06
IPB-X2 | 10.39 | 2.474 |  |  | 
IPC-X1 | 9.92 | 2.362 | 11.21 | 1.29 | 0.06
IPC-X2 | 10.39 | 2.474 |  |  | 
IPA-Y1 | 9.92 | 2.361 | 11.32 | 0.21 | 0.05
IPA-Y2 | 10.39 | 2.474 |  |  | 
IPB-Y1 | 10.40 | 2.476 | 0.38 | 0.38 | 0.06
IPB-Y2 | 10.39 | 2.473 |  |  | 
IPC-Y1 | 9.91 | 2.361 | 11.32 | 0.21 | 0.04
IPC-Y2 | 10.39 | 2.474 |  |  | 
BPM port | Frequency (GHz) | Wavelength (m)
Y port | 6426 | 0.037
X port | 5712 | 0.042
BPM
HYBRID

## Slide 11
Delay cables
Delay cables between cavity and hybrid
Static signal not seen to shift w.r.t BPM waveform

## Slide 12: Delay cables
Results:
SIS digitiser (4.2 ns per sample), expect delay of 6.5 samples with 5.5 m cables. Signals delayed as expected.
Static feature does not move noticeably within the pulse.
Delay cables
No delay cables
Look for reflections inside the chamber by introducing delay cables outside before the electronics and observing if the static signal moves within the pulse.
Matched 5.5 m (28 ns) delay cables introduced on both ports of IPBY and the reference cavity.

## Slide 13
Splitter study
Replace 180 degree hybrid with splitter
so that symmetric modes remain.
Static signal still present.

## Slide 14: Symmetric mode study
IPB hybrid replaced with a splitter to cancel dipole modes and combine symmetric modes.
Dipole modes (normal set-up)
Symmetric modes (with splitter)

## Slide 15: FFT Power
60 MHz signal seen in symmetric modes.
IPBY dipole modes (normal set-up)
IPBY symmetric modes (with splitter)
FFT Power Peak at 63 MHz
FFT Power Peak at 63 MHz

## Slide 16
Dependence on charge
Amplitude of unwanted waveform
scales linearly with charge

## Slide 17: 63 MHz amplitude with charge
63MHz signal amplitude in dipole waveforms increases with charge.
However, this data is with normal dipole set-up and may be confused by the dominant position-dependence.

## Slide 21
Frequency: X, Y / A, B, C
Similar frequency unwanted waveform seen in
IPA, IPB and IPC for X and Y modes

## Slide 23
Studies on the old IPC cavity
VNA analysis of cavity
Cluster of modes found at 7.5 GHz

## Slide 25
6.7 GHz Low Pass Filter
Should attenuate signal if comes from
higher frequency harmonics.
No change in amplitude of unwanted waveform from LPF

## Slide 26
Replace the hybrid on IBPY with a splitter (so only viewing non‐position­‐dependent monopole mode) followed by a low pass filter VLF-­‐6700 .
The static 60 MHz component should be significantly attenuated on addition of the filter if it was a result of higher frequency LO harmonic mixing.

## Slide 27: I Signal with 6.7 GHz LPF
T. Bromwich (8th July 2017)
It appears that the introduction of the low pass filter has shifted the frequency with the peak amplitude.

## Slide 28
Single Port Studies
Different magnitude and waveform shapes
from the two cavity ports

## Slide 30
Neven’s Studies (17th Nov 2015)

## Slide 31
N. Blaskovic
180° hybrid

## Slide 32
N. Blaskovic
With delay cables

## Slide 33
N. Blaskovic
Single port

## Slide 34
N. Blaskovic
Splitter