## Slide 1: CFS design status (based on Tohoku candidate site)
H. Hayano, KEK
TCMB 07/24/2018

## Slide 2
History of ILC250 Design Discussion
ILC WG2 (Staging Plan) was initiated by S. Michizono
after the discussion at LCWS2016-Morioka
Discussion of WG2 (Staging Plan for CFS) has been done
by domestic(KEK, Tohoku) and international tele-conference.
Discussion of WG2 was held at CFS@ALCW2017-SLAC
Cost review of WG2(derivation from TDR and Tohoku estimation)
at KEK Sep 26, 2017 (Lyn, Nakada, Steinar, J.Brau, Benno, etc)
Discussion of WG2 at CFS@LCWS2017-Strausburg
Discussion of ILC250 at CFS@ALCW2018-Fukuoka
Machine mapping research on Kitakami candidate site, and site-specific CFS
design, in parallel. (by Tohoku, KEK, AAA and expert from univeristies)
(access portal location, IP location are included)

## Slide 3
TDR cost
Subtract cost reduction of
2014-2016 TDR cost reduction and design change
Subtract cost reduction of each staging option
Subtract cost reduction by change of 31.5MV/m to 35MV/m, assuming success of 35MV/m Q0=1.6x1010 SRF HG,HQ
Estimation of cost for each staging option
How to estimate the cost of each option
Estimation of cost for each staging option
Decide working assumptions,
and cryomodule configuration,
tunnel configuration.
cost estimation conditions.
in case of 31.5MV/m
in case of 35MV/m
TDR-updated cost
each option cost
each option cost with HG HQ success
WG2
WG3
decrease of RF unit,
Nb material cost reduction,
surface process cost-reduction,
cryogenics cost reduction,
HLRF cost-increase, etc
35MV/m
Slide at AWLC2017(SLAC)

## Slide 4
Working assumption (1)
(1) Considering collision timing adjustment, condition must keep in any option,
option C = remove length between PM+10 and PM+12,
and remove TDR timing adjustment,
and adjust to n=6
option D = adjust to n=10, it is option C + simple tunnel of 6477m (total).
option D’ =adjust to n=8, it is option C + simple tunnel of 3238m (total).
In TDR(Ecm=500GeV), this equation is not satisfied as follows ( additional 294m exist);
Change Request is to adopt n=10;
with putting 1473m space
in both LINAC (updated TDR)
collision condition
CDR=3238.68m
(L1 + L2 + L3’) - L4 = 10 x CDR
( L1 + L2 + L3 ) – L4 = n x CDR
n=integer
e+
Slide at AWLC2017(SLAC)

## Slide 5
In Option-C(Ecm=250GeV), required Linac length become half, then we can adopt n=6
( -1367.74m - 4907.8m - 202.02m) x 2 = -12955.12m = - 4 x CDR
remove L (PM+10 – PM+12) = 4907.8m
remove 1367.74m
at BDS entrance
(timing adjustment)
remove 202.02m at end of Linac area.
L3 is shortened by 4 x CDR , it means LINAC length is shortened by 6477.56m
PM-8
PM-10
PM-12
PM+8
PM+10
PM+12
PM+13
PM-13
4907.8m
4907.8m
TDR
4911.6m
3413.8m
2334.9m
4795.2m
put 1473m
by change Request
put 1473m
by change Request
1375m
1264m
1375m
1264m
n=10
Shortning the e+ LINAC length is possible
as a unit of CDR /2 = 1619.34m.
Keep the same length of e- LINAC
for the symmetric collision energy.
Slide at AWLC2017(SLAC)

## Slide 6
Working assumption (2)
(2) Keep Energy Reach Margin enough safe to reach target energy (250GeV).
(1) Module margin : margin to reach the target energy of the target experiment (0% in TDR)
(2) Availability margin : margin to compensate cryomodule trip (1.5% in TDR, ~3 RF unit trip )
(3) Space margin : cryomodule space to be installed more cryomodule in future.
*Anytime 0.5% is required in the operation with cavity phase offset.
3 RF unit margin correspond to 3% for Ecm=250GeV
2.5% module margin(3.1GeV each) for Ecm=250GeV
Total margin: 1.5%+ 0.5% = 2% for TDR Ecm=500GeV
2.5% + 3% + 0.5% = 6% for Ecm=250GeV, Option C
(3) In case of HG,HQ R&D success;
HG HQ upgrade :from 31.5MV/m Q0=1E10  35MV/m Q0=1.6E10 by N-infusion.
Same RF unit configuration, but increase of klystron output to 11MW, 1.75ms.
Consider decrease of number of RF unit for 35MV/m.
The length of tunnel is kept the same as 31.5MV/m.
for enough positron production and meaningful energy reach of Higgs physics
Slide at AWLC2017(SLAC)

## Slide 7
Working assumption (3)
(6) Adopt CR0009 and CR0014 for cryogenics. The access hall is re-considered
with this design change. Angle cross with Linac tunnel and access tunnel
for cryomodule carry in, is considered.
(8) Two Vertical shaft access to detector hall is assumed.
(10) Number of beam dump and power of them proposed by Yokoya are adopted.
(7) Linac central shield wall is 1.5m thick. Total width of Linac tunnel is 9.5m.
(5) Maximum cryo-line length of one cryogenics is 2.5km+/-10%, the same as TDR.
(9) Design change of positron side BDS tunnel and injector-linac position are adopted.
(4) Only 5Hz Linac operation is considered (not 10Hz).
This determines the interval of the access point, such as PM+/-8, PM+/-10, PM+/-12
Slide at AWLC2017(SLAC)

## Slide 8
Working assumption (4)
(14) Simple tunnel means: normal wall finish, but no central shield wall,
no AC power line, no cooling water line,
however air-condition, lighting and water drain are installed.
(15) Digging tunnel during accelerator operation without serious interference.
(16) Keep the Damping Ring circumference. No design change for DR.
(12) Remove access tunnels at turn-around (PM-13 and PM+13) of TDR tunnel,
not for staging tunnel.
(13) One water-drain-tunnel is considered in the collision point, not at PM-13/PM+13.
(11) TDR-undulator-based positron is kept in this study.
The length of undulator is streched to 230m from 147m with 125GeV beam.
This determines energy sensitivity of positron production
This determines the requirement of collision timing condition.
Slide at AWLC2017(SLAC)

## Slide 9
Tunnel Optimization Tool development (1)
TOT(Tunnel Optimization Tool): CERN-KEK-ARUP development during 2015-2016
(originally developed for FCC)
Layout of accelerator tunnel into detailed geology & topography map
(1) optimize accelerator layout
(2) search access tunnel portal location
example of accelerator layout
Slide from KEK internal review March2017

## Slide 10
Tunnel Optimization Tool development (2)
Slide from KEK internal review March2017

## Slide 11
Tunnel Optimization Tool development (3)
Slide from KEK internal review March2017

## Slide 12
Most updated ILC250 Design was reported in AWLC2018 Fukuoka

## Slide 13
Option A’
PM-8
PM-10
PM-12
PM+8
PM+10
PM+12
IR
cryomodules
189
189
180
189
E gain (GeV)
59.6
59.6
56.7
59.6
Ecm=250GeV
1.4
10.0
1.4
10.0
4.5
4.5
BC
BC
RF unit
42
42
42
40
1
17
24
8
24
8
e-inj
e+inj
51
51
17
1
= e+ 132.7GeV
e- 135.6GeV =
5.0
5.0
4950.26m
3489.0m
2361.46m
4795.2m
2437.58m
2516m
Total tunnel length = 20549.5m
(20.5km)
module space
180
189
90
51
189
189
90
24
51
24
+6.2%margin
module space margin
for option A’, 35MV/m
module space margin
for option A’, 35MV/m
SRF 35MV/m
ECM=250GeV
1049m space
1049m space
Slide at AWLC2018(Fukuoka)

## Slide 14
PM-X
PM-10
PM-12
PM+8
PM+10
PM+12
PM+13
PM-13
IP
4907.6m
4907.8m
Ecm = 500GeV
Acc. length manipulation from TDR Recent Optics Deck
2639.6m
6318m
3401.5m
3729.2m
4795.1m
2718m
Total length of TDR accelerator = 17266.9m+16149.9m=33417m
1454m
1264m
1375.6m
1264m
(2015 Okugi BDS) + 87.5m = 2361.46m
3401.5m + 87.5m = 3489m
delta-L = -1367.74m
remove this length for option-A
delta-L = -4907.6m
timing path length is matched with n=10
CDR=3238.68m
( L1 + L2 + L3 ) – L4 = n x CDR
( L1 + L2 + L3 ) – L4 =(L1’+87.5)+L2+(L3’-1367.74x2-4907.6x2 -X) – (L4’+87.5)
=(L1’+L2+L3’)-L4’ -( 12550.68m +X)
=10 x CDR - 4 x CDR
= 6 x CDR
remove TDR timing adjust
6318m – 1367.74m = 4950.26m
remove this length
for option-A
delta-L = -4907.6m
4 x CDR=4 x 3238.68m = 12550.68m + X
X = 404.04 m
2718m – 404.04m/2
=2516m
Option A’ with n=6
2639.6m
– 404.04m/2
=2437.48m
collision condition
remove TDR timing adjust
Timing adjust
Timing adjust
Timing adjust
Vertical bend
Vertical bend
Slide at AWLC2018(Fukuoka)

## Slide 15
Keep BDS tunnel length as TDR, but put verical bend 87.5m on both entrance of BDS
There is no vertical bend in the optics deck.
Slide at AWLC2018(Fukuoka)

## Slide 16
emit
ML
BC2
BC1
EMIT
SPIN
TURN
LAUNCH
BC2
BC1
spin rotator
LAUNCH
167.6m
818.6m
230.6m
45.1m
77.8m
turn around
~92m
1264m
e+ ML
This is the same length for e- side and e+ side
e+ Main Linac end region details
PM+12
1454m
emit
BC2
BC1
spin rotator
LAUNCH
turn around
e+ ML
1264m
This is the same length for e- side and e+ side
Open space
PM+10
1252m
1049m
TDR
Option A’
Slide at AWLC2018(Fukuoka)

## Slide 17
Damping Ring
Electron Linac
Positron Linac
North
IP
Total Accelerator tunnel length
= 20,549.5m (20.5km)
Option A, A’
Accelerator
20.5km
Slide at AWLC2018(Fukuoka)

## Slide 18
PM-8
PM-10
PM+8
PM+10
electron linac
positron linac
damping
ring
Interaction Region
Total Accelerator tunnel length
= 20,549.5m (20.5km)
AT-10： 1503m
AT-8： 691m
AT・DR (access point to DR)：763m
AT・DH (branch to detector hall)：693m
AT+8： 283m
AT+10： 943m
access tunnels 5
total length 4876m
Option A, A’
Detector shaft 1
φ18m depth 75m
Utility shaft 1
φ10m depth 75m
Access Tunnels
Site-specific design of
Access tunnels
Slide at AWLC2018(Fukuoka)

## Slide 19
Beam Dump
400kW
400kW
60kW
60kW
60kW
60kW
60kW
60kW
17MW
17MW
60kW
60kW
60kW
300kW
Change Request on beam dump in 2016
was approved.
ILC-CR-0013 (Beam dump)
e-8 electron 10Hz dump
8MW
Slide at AWLC2018(Fukuoka)

## Slide 20
ILC-CR-0013 (Beam dump)
Slide at AWLC2018(Fukuoka)

## Slide 21
DR extraction
DR extraction
Source
tuneup
Source
tuneup
Main dump
Main dump
Photon
dump
BDS tuneup
BDS
tuneup
Fast abort
BC2 tuneup
BC2 tuneup
BC1 tuneup
BC1 tuneup
Kitakami Site-specific design
10Hz
dump
North
South
Slide at AWLC2018(Fukuoka)

## Slide 22
DR e- extraction dump
e+ Main dump
Photon
dump
10Hz e- dump
e- BDS tuneup dump
Fast abort dump
Source tuneup
dump
e+ Target
Position not scale
Slide at AWLC2018(Fukuoka)
We need dump hausing design.

## Slide 23
e- BC2 tuneup dump
e- BC1 tuneup dump
Electron turn around
Position not scale
Slide at AWLC2018(Fukuoka)
We need dump hausing design.

## Slide 24
DR e+ extraction dump
e- Main dump
e- Source tuneup
dump
e+ BDS tuneup dump
Position not scale
Slide at AWLC2018(Fukuoka)
We need dump hausing design.

## Slide 25
e+ BC1 tuneup dump
e+ BC2 tuneup dump
Positron turn around
Position not scale
Slide at AWLC2018(Fukuoka)
We need dump hausing design.

## Slide 26
End of Slide