## Slide 1
ILC Simulations
Rebecca Ramjiawan FONT meeting
Friday, 10th August 2018

## Slide 2: Outline
Basic model of FB system implemented in MATLAB, generate bunch trains and model BPM, kicker and lever-arm effect.
MATLAB model 1312 bunch trains: bunch train structures with constant offsets, offsets between consecutive bunches, harmonics of a range of frequencies.
MATLAB model FB system: BPM with resolution effects, kicker with kicker noise, proportional control, proportional and integral control, averaging over multiple bunches, weighted averaging over two bunches (bunchi and bunchi-1).
Lucretia: generate 1312 bunch train and track through the BDS to the IP, model bunch-bunch interaction at the IP using Guinea-Pig.
Deflection angle curves modelled for various beam parameters showing dependence on: bunch size (x,y), bunch length, charge.

## Slide 3: Feedback Loop Simulation (MATLAB)
Construct uncorrected e+e- bunch trains (1312 bunches), with noise, drifts, harmonics, etc.
True beam offset at IP = Uncorrected offset + correction
True beam-beam deflection (using nominal deflection curve)
True offset at BPM (using IP to BPM distance 4m)
Measured offset at BPM (resolution)
Estimate deflection angle, offset at IP from fit to beam-beam deflection curve
Apply correction (can inc. kicker error 0.1% offset- as Javier)
Run for multiple trains and average results.
Determine luminosity from bunch-bunch offset (using nominal luminosity-offset curve)
Delay loop

## Slide 4: Ideal Situation – Rigid Beam
Constant offset 70 nm throughout 1312 bunch train.
0 um resolution.
Perfect correction maintained correctly with delay loop ✓
Successfully removes bunch-bunch offset by second bunch.
Full luminosity recovery by second bunch.

## Slide 5: Resolution Effects
Rigid bunch trains, with 4 nm offset, with feedback with BPM resolution 1 um operating.

## Slide 6: Luminosity vs. Resolution
Two rigid bunch trains with zero offset (i.e requiring no correction), with a BPM with a range of resolutions (0 to 20 um).
As expected, very little degradation to luminosity from a BPM with up to 1 um resolution.
Fractional luminosity for FB system with 1 um resolution BPM and rigid beam: 0.9985 * L0.

## Slide 7: Gain scan
Rigid bunch trains with 10 nm initial offset and proportional gain feedback. Scaling the feedback gain. (1 is nominal)
Gain:
0.4, 0.6, 0.8, 1, 1.2, 1.4, 1.6, 1.8, 2

## Slide 8
Bunch train structures

## Slide 9: Bunch train structure
Bunch train: 1 nm initial offset with offset of 0.4 nm between consecutive bunches.
Proportional gain feedback, with 0 nm resolution. Would not take out the 0.4 nm difference between consecutive bunches.
Leading to a loss in luminosity.
Feedback off, offset between beams.
Feedback on, offset between bunches.
Δx = 0.4 nm

## Slide 10: Proportional Integral Control
0.4 nm offset between consecutive bunches. The 0.4 nm is not removed by just proportional feedback.
Nominal gains for proportional term,
Gains for integral term: 0, 0.5, 1, 1.5
Proportional term
Integral term

## Slide 11: Harmonic (across train)
Bunch train: Banana shape (half cycle across bunch train).
Proportional gain feedback, with 0 nm resolution. Would not take out the difference between consecutive bunches. (Effectively differential of harmonic)
Leading to a loss in luminosity.
Feedback off, offset between bunches.
Feedback on, offset between bunches.

## Slide 12: Frequencies of harmonic
Dependence of feedback performance on frequency of harmonic structure introduced to bunch train.
Worst performance (peak of curve) occurs when frequency of harmonic =1312*pi, as this corresponds to bunch-to-bunch correlation of -1.
Higher frequencies than 1312*pi when sampled at the bunch frequency are equivalent to lower frequency harmonics and consequently perform better.
Jitter here defined as standard deviations of y-offsets (between beams at the IP) across a bunch train after feedback.

## Slide 13: Proportional Integral Control: Harmonic
Proportional control vs. proportional integral control. For harmonic bunch train shape shown on slide 17.
Integral gain Ki: 0
Integral gain Ki: nominal
Proportional term
Integral term

## Slide 14: Harmonic structure and BPM Resolution
Proportional gain Kp = 1;
Integral gain Ki: shown on x-axis.
BPM resolution: 1 um
Harmonic term (um) = 0.1cos((t)+)
where t = 0:1/1311:1, half period across bunch train.
If resolution is the dominant effect integration makes it worse. If harmonic is the dominant effect integration makes it better.
Integral gain scan

## Slide 15
Averaging Bunches to Improve
Bunch Position Measurement

## Slide 16: Averaging over multiple bunches
If noise added is uncorrelated between consecutive bunches, e.g resolution effects then averaging offers some improvement. Very minor improvement for resolution of 1 um. Initially rigid trains with offset 70 nm.
Would become important for beams with poorer bunch to bunch correlation.
1 um resolution
10 um resolution

## Slide 17: Reduced bunch-to-bunch correlation
10 nm std random noise
5 nm std random noise
1 nm std random noise
Initial offset 70 nm with random noise added to each bunch.
Random noise introduced bunch by bunch to reduce correlation and degrade feedback performance.
Position measurements fed into feedback system are now averaged over some number of bunches (x-axis) and the average luminosity recovered shown (y-axis)

## Slide 18: Weighted averaging over two bunches
1 nm random noise added bunch by bunch AND
1 nm amplitude harmonic – half period across bunch train.
Averaging improves if random noise is the dominant effect but degrades luminosity if harmonic is the dominant effect. If combination of correlated and uncorrelated bunch-to-bunch effects then can use weighted averaging.
Optimum weighting coefficient depends on magnitude of effects which are correlated and uncorrelated between consecutive bunches.
Bunch positioni =
z

## Slide 19
Tracking the bunches through the BDS

## Slide 20: Bunches at IP (Lucretia)
Horizontal beam size = 474 nm
Vertical beam size = 5.9 nm
80000 macroparticles.
I still need to figure out which/if any wakefields are implemented.
MATLAB structure called WF.ZSR, possibly short range wakefields?
First bunch in train shown.

## Slide 21: 1312 bunch train tracked through BDS
y-position of bunches at IP modelled in Lucretia for a train of 1312 bunches tracked through the BDS to the IP.
10000 macroparticles modelled per bunch, mean bunch position shown.

## Slide 22
Deflection Angle Curves

## Slide 23: Nominal Curves
Nominal beam-beam deflection angle curve and luminosity curve vs. beam-beam offset at the IP.
Maximum deflection: 365 urad
Maximum luminosity: 1.81

## Slide 24: Horizontal beam size (sigma_x)
Deflection-angle curves for a range of horizontal beam size values (sigma_x):
[0.8,0.9,0.99,1,1.01,1.1,1.2]*474 nm

## Slide 25: Vertical beam size (sigma_y)
Deflection-angle curves for a range of vertical beam size values:
[0.8,0.9,0.99,1,1.01,1.1,1.2]*5.9 nm

## Slide 26: Bunch length (sigma_z)
Deflection-angle curves for a range of longitudinal beam size values:
[0.8,0.9,0.99,1,1.01,1.1,1.2]*300 um

## Slide 27: Charge (number of particles per bunch)
Deflection-angle curves for a range of bunch charges:
As function of number of particles per bunch
[0.8,0.9,0.99,1,1.01,1.1,1.2]*2e10.

## Slide 28: Energy
Deflection-angle curves for a range of energies:
[248:0.1:252] GeV.
Shows no real variation with bunch energy ✓

## Slide 29: Summary
Basic model of FB system implemented in MATLAB.
Ability to model bunch trains: - bunch structures inc. constant offsets, offsets between consecutive bunches, harmonics of a range of frequencies.
Ability to model FB system: proportional control, proportional and integral control, averaging over multiple bunches, weighted averaging.
Generate 1312 bunch train in Lucretia and track through the BDS to the IP, model bunch-bunch interaction at the IP using Guinea-Pig.
Deflection angle curves modelled for various beam parameters showing dependence on: bunch size (x,y), bunch length, charge.