## Slide 1: Optimization of the track reconstruction algorithm in a pixel based calorimeter for proton computed tomography
Author:
Alba García Santos
April 10, 2019

## Slide 2: Index
Introduction

## Slide 3: Index
Introduction
Proton CT

## Slide 4: Index
Introduction
Proton CT
Research Objective

## Slide 5: Index
Introduction
Proton CT
Research Objective
Current Algorithm

## Slide 6: Index
Introduction
Research Objective
Current Algorithm
New Ideas
Proton CT

## Slide 7: Index
Introduction
Research Objective
Current Algorithm
New Ideas
Proton CT
Conclusions

## Slide 8: Introduction
Cancer is a destructive disease, in which tumor cells grow-out-of-control, halting organ function
Different treatment depending on:
  cancer type, stage, organs at risk adjacent to the tumor…
Increase in the number of patient treated with particle therapy Protons
Introduction
Proton CT
Research Objective
Current Algorithm
New Ideas
Conclusions

## Slide 9: Introduction
Safety margins
  Tumor is fully covered
  Increase irradiation of healthy tissue
Narrow Bragg peak
  Localized treatment possible
  High susceptibility to uncertainty in the treatment planning
Introduction
Proton CT
Research Objective
Current Algorithm
New Ideas
Conclusions

## Slide 10: One of the causes of this uncertainty…
CT Hounsfield Units (HU)
Relative Stopping power (RSP)
RSP
HU
Calibration curve
Treatment planning
Dose calculation
Range uncertainties : 7%
Improvement Dual Energy CT: 2%
However, CT artifact inaccurate RSP map
Proton CT (0.3%)
Direct RSP maps
No artifacts
Reduction of imaging dose compare to CT.
Reduction of treatment margins
Introduction
Proton CT
Research Objective
Current Algorithm
New Ideas
Conclusions

## Slide 11: Proton CT
For RSP maps calculation:
Using a Digital Tracking Calorimeter  many protons’ residual energies can be measured at the same time.
Introduction
Proton CT
Research Objective
Current Algorithm
New Ideas
Conclusions
  40 layers
ALice PIxel Detector (ALPIDE) chip:
  Active area: 15 x 30 mm2 (1024 x 512 pixel array of 28 x 28 m2 pixels).
  Readout rate: 5-10 s.
Used sensors + sensor layer design = ALICE FoCal em calorimeter  Synergy in R&D

## Slide 12: Proton CT
For RSP maps calculation:
Using a Digital Tracking Calorimeter  many proton’s residual energies can be measured at the same time .
Multiple Coulomb scattering  stochastic trajectories
Proton intensities + high level of scatter between layers  track reconstruction algorithm
Aluminum
Introduction
Proton CT
Research Objective
Current Algorithm
New Ideas
Conclusions

## Slide 13: Research objective
A proton track reconstruction algorithm has already been developed.
However, it has some limitations on the track density that can be reconstructed correctly.
A more efficient algorithm will allow a reduction of the scan time.
Optimization of the current method
Introduction
Proton CT
Research Objective
Current Algorithm
New Ideas
Conclusions

## Slide 14: Current Algorithm
Based on the track-following scheme
Search cone size depends on Smax
  Determine the of curvature
  Constant value
Sn is calculated for each candidate
If Sn < Smax  the candidate is added to the track
Introduction
Proton CT
Research Objective
Current Algorithm
New Ideas
Conclusions

## Slide 15
Current Algorithm
+
Geant4
GATE
Introduction
Proton CT
Research Objective
Current Algorithm
New Ideas
Conclusions

## Slide 16: Idea 1: Variable Smax
Calculate expected scatter Highland’s Formula
x: target length (3.5mm Al)
X0: radiation length of the target material (Al)
P1v1: proton’s kinematic properties for momentum and velocity.
Introduction
Proton CT
Research Objective
Current Algorithm
New Ideas
Conclusions

## Slide 17: Efficiency
Using Highland’s formula
Using constant Smax (current algorithm)
Introduction
Proton CT
Research Objective
Current Algorithm
New Ideas
Conclusions
Only marginal improvement of the algorithm by using Highland’s formula

## Slide 18: Idea 1: Variable Smax
Starting point
Starting point
Different starting point = Different efficiency
Tracks with same first/last ID | All clusters same ID | Tracks with close match (0.5mm,1 degree) on first/last cluster
90.09% | 81.08% | 98.2%
Tracks with same first/last ID | All clusters same ID | Tracks with close match (0.5mm,1 degree) on first/last cluster
84.96% | 75.22% | 96.4%
Introduction
Proton CT
Research Objective
Current Algorithm
New Ideas
Conclusions

## Slide 19: Idea 2: Calculate best scenario
P1
P2
P3
P4
P6
P5
p(
Best Option!
*…*
Introduction
Proton CT
Research Objective
Current Algorithm
New Ideas
Conclusions

## Slide 20: Conclusions
Proton therapy treatment can optimize the dose delivery to patient
The use of a proton CT will increase the accuracy of the treatment planning
To this end, protons’ residual energies can be measured using Digital Tracking Calorimeter  many protons can be detected at the same time
However, protons follow stochastic trajectories in the detector track reconstruction algorithm.
The current track reconstruction algorithm has some limitation, especially at higher beam intensities
Optimization of this algorithm  better performance
  Idea 1: Adapt the algorithm to the expected scatter depending on the energy
    Small improvement
    Low robustness
  Idea 2: Calculate the best scenario per layer
    More robust
    More computationally expensive
    Better results???
Introduction
Proton CT
Research Objective
Current Algorithm
New Ideas
Conclusions

## Slide 21: Acknowledgement
Thomas Peitzmann
Dieter Röhrich
Helge Egil Seime Pettersen
Naomi van der Kolk
Rene Barthel
Ton van den Brink

## Slide 22: Thank you for your attention!