## Slide 1: HCAL status
I.Laktineh & F.Sefkow
On behalf of the ILD hadronic calorimeter groups

## Slide 2
SDHCAL technological prototype
R&D for SDHCAL ILD:
Detectors
Readout electronics
Mechanics
Gas recycling
AHCAL technological prototype Design
Construction
Testbeam experience
Large layers
Future plans
Conclusion
Outline

## Slide 3
10500 64-ch ASIC were tested and calibrated using a
dedicated (ASICs layout : 93% ).
SDHCAL prototype construction
310 PCBs were produced, cabled and tested.
They were assembled by sets of six to make 1m2 ASUs
50 detectors were built and assembled with
their electronics into cassettes.
Self-supporting mechanical structure.
Full assembly took place at CERN.
170 DIF, 20 DCC were built and tested.
DAQ system using both USB and HTML protocol
was developed and used.
1 cm x 1 cm pads, 48 layers, power-pulsed, mechanical self-supporting structure
SDHCAL Since 2011
TB: 2012,2015, 2016, 2017 and 2018 with ECAL

## Slide 4
The thresholds weight evolution with the total number
of hits obtained by minimizing a χ2
Χ2 = (Ebeam-Erec)2/Ebeam
Erec = α (Ntot) N1 + β(Ntot) N2 + γ(Ntot) N3
N1,N2 and N3 : exclusive number of hits associated to first,
second and third threshold.
α, β, γ are quadratic functions of the total number of hits (Ntot)
Events of H2 runs corresponding to energies : 5, 10, 30 , 60
and 80 GeV were used to fit the 9 parameters.
Then the energy of hadronic events in
both H2( only pions) and H6 (presence of protons)
Energy estimation

## Slide 5
The density of each hit is the number of hits in the surrounding 3x3 cells (including itself)
It can vary from 1 (lone hit) to 9 (completely surrounded)
  For these 3 formulas, the α parameters are found using a chi2 minimisation :
Energy reconstruction

## Slide 6
SDHCAL Simulation
Linear formula shows bad linearity at low energy
The Density formula seems to improve linearity and resolution compared to Linear/Quadratic formulas
G.Garillot

## Slide 7
SDHCAL is a powerful tool to identify particles: muons, electrons and hadrons
B. Liu

## Slide 8
First common test with the technological SiW ECAL prototype

## Slide 9
First common test with the technological SiW ECAL prototype
Still some work to associate the events of the two prototypes.

## Slide 10
SDHCAL for ILD
We propose the videau structure as a baseline for the SDHCAL

## Slide 11
SDHCAL R&D for ILD
Detectors as large as 3m X 1m need to be built
Electronic readout should be the most robust with
minimal intervention during operation.
DAQ system should be robust and efficient
Mechanical structure to be similar to the final one
Envisage new features such timing, etc..
Goal: to build new prototype with few but large GRPC with the new components
 ILD Module0
SDHCAL
ILD Module
GRPC
Glass Resistive Plate Chambers

## Slide 12
2 m
1 m
inlet
outlet
Prototype circulation system
New circulation system
Detector conception
Construction and operation of large GRPC necessitate some improvement with respect to the present scenario.
Gas distribution : new scheme is proposed
Cassette conception to ensure good contact between the detector and electronics is to be improved

## Slide 13
First 2x1 m2 RPC chamber was successfully built with a new gas circulation system
Detector conception

## Slide 14
DIF #1
DIF #2
DIF #3
144 ASICs= 9216 channels/1m2
USB
HDMI
ASU1
3072 ch
ASU2
DIF
100 cm
33 cm
HADROC chip
(ASIC)
1m2 board  6 ASUs hosting 24 ASICs
Electronics readout for the 1m3 prototipo
1 DIF (detector InterFace) for 2 ASU (Active Sensor Unit.- PCB+ASICs)  3 DIFs for ONE 1m2 GRPC detector
Electronics readout for the final detector
Only 1 DIF per GRPC (any size) with small dimensions to fit in the small space available at the ILD detector
DIF dimensions
New electronics
Uo to 9

## Slide 15
HARDROCR3 main features:
  Independent channels
  Zero suppress
  Extended dynamic range (up to 50 pC)
  I2C link with triple voting for slow control parameters
  packaging in QFP208, die size ~30 mm2
  Consumption increase (internal PLL, I2C)
6,3 mm
4,7 mm
H3B TESTED : 786, Yield : 83.3 %
New electronics: ASIC

## Slide 16: HARDROC3: Analog linearity
FSB0
FSB0: 5σ noise limit= 15 fC
Up to 10 pC
Up to 50 pC
Fast shaper outputs (mV) vs Qinj (fC)
50% trig. Eff. (DAC units) vs Qinj (fC)
Dynamic range: 15fC - 50 pC
FSB1
FSB2

## Slide 17
SDHCAL Simulation
Up to 20% improvment is expected
G. Garillot

## Slide 18: ASU (Active Sensor Unit)
An important challenge is to build a PCB up to 1m length with good planarity to have a homogeneous contact of pads with RPCs in order to guarantee an uniform response along all the detector.
A company was found and 1x0.33 m2 with 13 layer ASUs have been built.
ASU
PCB
HR3
ASICs
The ASU-ASU (= ASU-DIF) connections also produced

## Slide 20
DIF sends DAQ commands (config, clock, trigger) to front-end and transfer their signal data to DAQ. It controls also the ASIC power pulsing
• Only one DIF per plane (instead of three)
• DIF handle up to 432 HR3 chips (vs 48 HR2 in previous DIF)
• HR3 slow control through I2C bus (12 IC2 buses).
Keeps also 2 of the old slow control buses as backup & redundancy.
• Data transmission to/from DAQ by Ethernet
• Clock and synchronization by TTC (already used in LHC)
• 93W Peak power supply with super-capacitors
(vs 8.6 W in previous DIF)
• Spare I/O connectors to the FPGA (i.e. for GBT links)
• Upgrade USB 1.1 to USB 2.0
FPGA XC7A35TFGG484
TEXAS TM4C1294U
POWER
POWER
POWER
New electronics : DIF

## Slide 21
6 cm
100 cm
33 cm
New readout electronics is being tested
New electronics
Firmeware is almost fianlized

## Slide 22
33 cm
Two ASUs are being connected and tested
New electronics

## Slide 23
Mechanical Structure
Industrial production of flat large absorber plates (3 m X 1 m) by roller leveling process
Chart: 
L1 Before | 1.9 | 2.5 | 2.5 | 1 | 2
L1 After | 0.2 | 0.2 | 0.2 | 0.1 | 0.2
mm
before
after

## Slide 24
Mechanical Structure
To assembly the technological SDHCAL prototype, bolts were used on 1 cm width bars were used for this. For larger prototype, bigger bolts and thus wider bars are needed. This represents a “dead” zone.

## Slide 25
Improvement on the present system is being made by using Electron Beam Welding rather than bolts to reduce the deformation and the spacers thickness.
Mechanical Structure

## Slide 26: Welding tests
Two identical small prototypes (PT4): 2x (4 plates 0.4x1 m2)
Welding will be performed following the results of the previous welding tests:
Complete Penetration ~10 mm
Greater strength of the structure.
(Plates for the PT3)
(PT4)
(PT4)
(PT4)
+ 1 mm
- 1 mm
Mechanical Structure

## Slide 27: Next Welding tests
‘Final’ calorimeter prototype : 4 plates 3x1 m2
Complete Penetration ~10 mm
Greater strength of the structure.
(PT3)
Pieces for this prototype produced and the preliminary assembly test & measures are done at CIEMAT.
(PT3)
photogrammetry measure
Mechanical Structure

## Slide 28
Mechanical Structure
EBW@CERN

## Slide 29
Mechanical Structure
< 1 mm

## Slide 31
Gas recycling is necessary to reduce cost :
-Goal: reduce the gas consumption to reduce the cost.
-Gas renewal of 5-10% rather than 100%
-Conceived by the CERN gas group and successfully used.
Gas system

## Slide 32
Summary and plans for SDHCAL
Technological protoype running successfully since 2012
Many results validate the potential of the concept
Large prototype with the new generation of readout electronics is on the rails
Mechanical structure optimized for ILD
We intend to introduce timing since RPC is a fast timing detector we collaborate with CEPC colleagues to achieve this.

## Slide 33: AHCAL
design
construction
testbeam experience
large layers
future plans

## Slide 34: AHCAL Design
highly granular scintillator SiPM-on-tile hadron calorimeter, 3*3 cm² scintillator tiles
fully integrated design
  front-end electronics, readout
  voltage supply, LED system for monitoring
  no cooling within active layers
scalable to full detector (~8 million channels)
HCAL Base Unit: 36*36 cm2, 144 tiles, 4 ASICs
  slabs of 6 HBUs
  up to 3 slabs per layer
HBU
ILD barrel

## Slide 35: AHCAL Technolgical Testbeam Prototype
38 active layers of 72*72 cm²
4 HBUs per module
  16 SPIROC 2E readout ASICs, 576 channels of 3*3 cm² tiles
  in total: 608 ASICs, ~22000 channels
all modules with surface-mount MPPCs
  S13360-1325PE
  2668 pixels (3x physics prototype (PP))
  operated at 5V overvoltage
    50% less temperature sensitivity w.r.t. PP
  nominal operation voltage within 200mV in a module -> use same voltage
    Simplified set-up
    Layer-wise regulation
  About 3 orders of magnitude less noise
steel absorber stack corresponding to ~1% of ILD barrel

## Slide 36: Mass Production
design optimized for mass production
  SMD SiPMs soldered automatically
  injection-moulded polystyrene tiles, no further surface treatment
  automatic wrapping in ESR reflector: 500 tiles / day
  glueing of tiles with screen printer and pick-and-place machine 2HBU / hour

## Slide 37: Testbeam Setup 9. – 23. May 2018 in H2 at SPS
38 active layers of 72*72 cm² in steel absorber with 1.7 cm layer thickness (~4 λ)
mounted on the movable platform (“scissors table”) in H2
beam instrumentation: wire chambers, trigger scintillators, Cherenkov detector

## Slide 38: Testbeam Setup 27. June – 4. July 2018 in H2 at SPS
as in May, plus:
  added one module with 6*6 cm2 tiles (prototype for rear layers)
  added CMS HGCAL “thick stack” (12 layers of 1 HBU, 7.4 cm steel absorber) as tailcatcher
  added single HBU in front of absorber as “pre-shower” detector
AHCAL
main stack
tailcatcher

## Slide 39: Testbeam Operation: Temperature Compensation
gain and photon detection efficiency of SiPMs depend on temperature
  can avoid changes by stabilizing temperature or adapting bias voltage (HV)
temperature compensation: use mean temperature in a layer to adjust HV
used routinely, HV changes as expected, gain stays stable

## Slide 40: Data Taking
very stable running
routinely using temperature compensation
all 38 layers working well, <1‰ dead channels
muons for calibration
  several position scans, with and w/o power pulsing
electrons: energy scan 10 to 100 GeV
  with and without power pulsing
  typically 200,000 to 400,000 ev. per energy
negative pions: energy scan 10 to 200 GeV
  with and without power pulsing
  typically 400,000 to 600,000 ev. per energy
  shifted positions for particle separation studies
additional technical tests
in total collected several 10^7 events

## Slide 41: Event Displays and Online Monitoring
electron
hadron
muons
muon

## Slide 42: Online Monitoring: Energy Sums
10
20
30
40
50 GeV
CALICE
work in progress
Electron Beam

## Slide 43: Scintillator Part of CMS HGCAL
22’000 SiPMs
8’000’000 SiPMs
500’000 SiPMs
CALICE AHCAL prototype
CMS HGCAL
ILD
silicon
SiPM
on tile
-30˚C
design: scintillator with SiPM-on-tile technology where allowed by radiation
Intermediate scale, new challenges: radiation, high data rate, operation -30 °C
Technical Design Report approved in February 2018
Engineering Design Report and start of production for many components in 2021
assembled endcaps need to be ready for lowering in August and Dec. 2024

## Slide 44: Combined Testbeam: CMS HGCAL + CALICE AHCAL
2 weeks of combined testbeam at CERN SPS in October 2018
28 layers HGCAL EE (silicon/lead), 12 layers HGCAL FH (silicon/steel), 39 layers AHCAL (scintillator/steel); common DAQ: EUDAQ2
important test of concept, important information for simulation of showers

## Slide 45: Combined Testbeam: CMS Silicon HGCAL + CALICE AHCAL
2 weeks of combined testbeam at CERN SPS in October 2018
28 layers HGCAL EE (silicon/lead), 12 layers HGCAL FH (silicon/steel), 39 layers AHCAL (scintillator/steel)
important test of concept, important information for simulation of showers

## Slide 46
Test of Large (Full ILD Size) Layers
Length 216 cm ,width up to 108 cm
Test power distribution
  Check for voltage drops
  Check stabilization time in power pulsing mode
  Stable after < 120 μs
Test signal quality
  Clock distribution
  Singe p.e. spectra

## Slide 47
Optimisation of Absorber Structure
Adaptation to current outer dimensions
Actuive gao includes 2.5mm tolerance
Reinforcements near cryostat supports and ECAL fixtures
Full disk at z=0
Maximum displacement 1.4mm
Step file ready for export to LLR for further common optimization with ECAL
Return to dynamical simulations of earhquake response

## Slide 48: Summary and Plans for AHCAL
CALICE SiPM-on-tile HCAL prototype with 22’000 channels built
Successfully commissioned and operated in testbeam
Design and procedures for construction and QA scalable to a full collider detector
3 weeks of testbeam at CERN SPS in 2018
  collected several 10^7 muon, electron and pion events
2 weeks of combined test with CMS HGCAL silicon prototype
Future tests
  Test of full-sized ILD layers (3*6 HBUs)
  Commission fast clock mode with ns time resolution
  Alternative tile design and readout ASIC
  Beam tests with (existing) tungsten absorber structure (2021)
  Combined beam test with EM calo in front highly desirable

## Slide 49
Conclusion
The two HCAL technologies have made a big progress.
The AHCAL technological prototype is now ready and successful
The SDHCAL ILD module0 construction is ongoinf
A full large ILD AHCAL layer is to be finalized and tested soon

## Slide 50: Backup

## Slide 51: Quality assurance and calibration
SiPM sample tests
tile sample tests
test of all ASICs
all individual HBUs tested and calibrated with LEDs and cosmics
all modules (2*2 HBUs) tested with cosmics
all modules calibrated with LEDs and DESY beam (3 GeV electrons as MIPs)
  calibrate 4 modules in parallel, ~1 day per set
  automated scan with automated control of the moving stage (EUDAQ)
  many technical tests: gain switching, ...
result: overall quality very good, <1‰ dead channels

## Slide 52: AHCAL prototype construction: work flow
SiPMs
SiPM sample tests
ASICs
ASIC tests
ASIC test board
PCBs
Tiles
Interfaces
Cassetes
Stack
HBU soldering
HBU tiling
Cosmic tests
LED tests
calibration in DESY beam
HCAL integration
Reflector wrapping
Cassette assembly
Cooling
Uni Heidelberg
Wuppertal
Palaiseau
Moscow
Uni Hamburg
Mainz
MPP Munich
DESY
Distributed
production,
construction
and QC

## Slide 53: AHCAL DAQ Hardware / digital readout
CCC (Clock and Control Card)
  Provides a clock to AHCAL
  Synchronizes all detectors
  Starts and stops the acquisition according to the spill level and readiness of all DIFs
  Distributes trigger validation
LDA (Link Data Aggregator)
  Merges DIF readout packets
  Does gray decoding, adds headers
  Send the packets over TCP
DIF (Detector InterFace)
  Controls ASICs in 1 layer (many HBUs)
  Readout the data from all ASICs
  Sends the data to LDA
SPIROC (SiliconPM Integrated Read Out Chip)
  Reads out 36 SiPMs
  each channel has 16 memory cells
  auto-trigger (beam) & external trigger (calib) mode
BIF (Beam interface)
  Precise trigger timestamping
CCC
LDA
DIF
PC
spiroc
…
LDAs
...
Up to 96 DIFs
…
Up to 72 SPIROCs
36
SiPMs
Trigger
Spill
BIF
DAQ HW
DAQ SW

## Slide 54: EUDAQ2 as central DAQ and run control
BIF
ROC
TS_start
TS_trigger
BIF
ROC
TS_start
TS_trigger
BIF
ROC
BXID
TS_start
AHCAL_same_bxid ROC
TS_start,
TS_bxid (opt. TS_trig)
triggerID
AHCAL_same_bxid ROC
TS_start,
TS_bxid (opt. TS_trig)
triggerID
AHCAL_same_bxid ROC
BXID
TS_start,
triggerID
LDA ROC,
TS_start,
TS_trig,
triggerID
LDA ROC,
TS_start,
TS_trig,
triggerID
bunch-crossing(BXID)-wise event building: not a complete readout cycle(ROC), but just triggered BXIDs
  15~20x more (smaller) events in slcio compared to ROC-based
Auto-restart of run (time, # of evts) implemented in a custom run control
Data quality indicators: # of triggers, # of built events (BIF, ahcal, ahcal+bif)
LDA TS ROC,
BXID
TS_start,
TS_trig,
triggerID
ROC=ROC,
TS_trig=bxid
ROC,BXID
match
EUDAQ_evt
(→ SLCIO)
ASICs
ROC,
BXID
ASICs
ROC,
BXID
ASICs
ROC,
BXID
ASICs
ROC,
BXID
AHCAL_same_bxid
BIF (opt.)
LDA TS
AHCAL producer
AHCAL bxid data collector
AHCAL data from Labview
BIF producer

## Slide 55: Online data quality checks for electrons
May:
  clear tail to smaller number of hits and earlier center-of-gravity
  present for all electron energies
May 2018
June 2018
electrons
tail
June:
  changed beam steering
  tail gone, nice and narrow energy distributions

## Slide 56
A new challenge

## Slide 57: New Tests
Welded pieces for the “qualitatively” smaller tests:
Penetration ~10 mm
Several ways tested.
Option 2 has been chosen
Z-axis deformations close to 2 mm
Insertion test of the cassette:
One cassette was tested on the previous welding test pieces produced.
Two identically prototypes ( plates ~0.4x1 m2) will be welded with those parameter to validate the procedure (PT4).

## Slide 58: Additional tests to minimize the welding deformation
Small test prototype: 2 x PTs1 & 2x PTs2
Contact people for EBW at CERN, Manuel Redondas & Thierry Tardy, propose two method to reduce the distortion produced by EBW:
 Placing a 1-2 mm sheet on the welding zone and welding through it. And to remove the first 1 or 2 mm which contain the beginning of the welding cone, maintaining only the narrowest and parallel welding zone, avoiding local stress.
Producing slots, parallel to the weld, that absorb the stress that is produced by the beginning of the welding cone.
Pieces were produced at Ciemat. Delivered to CERN and assembled during December 2017.
Complete Penetration ~10 mm
Some tests using smaller pieces are foreseen to evaluate “qualitatively” those two options (PTs1 &PTs2).
(PTs2)
(PTs1)
To be welded at CERN during February-March 2018.
If this method works, it could be implemented on the previous prototypes, to validate it.
E.Calvo-Alamillo