## Slide 1: Forward calorimeters
Yan Benhammou
On behalf of the FCAL Collaboration

## Slide 2: Outline
Purposes
FCAL detectors : simulation
FCAL detectors : hardware
Electronics
Conclusion

## Slide 3: Forward region detector purposes
precise luminosity measurement, O(10-3) up 500 GeV
fast luminosity measurement and beam tuning
hermiticity
For these purposes, mainly three detectors : the LumiCal, BeamCal and LHCal

## Slide 4: FCAL detector purposes at ILC
LumiCal :
  Precise integrated luminosity measurements (Bhabha events)
  Extend calorimetric coverage to small polar angles. Important for physics analysis
LHCal :
  Extend the hadronic calorimeter coverage
BeamCal :
  Measure instant luminosity. feedback for beamtuning
  tagging of high energy electrons to suppress backgrounds to potential BSM process
  shielding of the accelerator components from the beam-induced background
  providing supplementary beam diagnostics information extracted from the pattern of incoherent-pair energy depositions

## Slide 5
Purposes
FCAL detectors : simulation
FCAL detectors : hardware
Electronics
conclusion

## Slide 6: FCAL detector designs
LumiCal :
  Electromagnetic sampling calorimeter
  30 layers of 3.5 mm thick tungsten plates with 1 mm gap for silicon sensors
  Cover the angles between 41 mrad to 67 mrad
LHCal :
  Sampling Calorimeter (silicon)
  29 layers of 16mm thickness. Absorber : tungsten or iron
BeamCal:
  Sampling calorimeter based on tungsten plates (30 layers)
  Cover the angles between 6 mrad to 43 mrad
  Due to large dose, rad hard sensors (GaAs, Diamond, Sapphire)

## Slide 7
BeamCal simulation
Simulations within DD4hep environment and validation started
Reconstruction software for LumiCal and BeamCal present (FcalClusterer Marlin module) adopted for DD4HEP
Different methods of background generated and different reconstruction algorithms compared
Results : for example, efficiency and angle resolution with 40 bunch crossing overlaid to the signal

## Slide 8
Polar angular pad size calculated to obtain the given precision of luminosity measurement
Simulation of the
energy resolution
Small Moliere radius
for compactness study
LumiCal simulation
For Iq =0.8 mrad, ΔL/L = 1.6 10-4
ILC
H Abramowicz et al 2010 JINST 5 P12002
Polar angle pad size

## Slide 9
Located between the LumiCal and BeamCal
Total thickness : 463 mm
Simulation of tungsten-Si and iron-Si with different incident particles
LHCal simulation
Tungsten looks to be the best candidate

## Slide 10
The collaboration
FCAL detectors : simulation
FCAL detectors : hardware
Electronics
conclusion

## Slide 11: LumiCal sensor
Silicon senor, 320 mm thickness
64 radial pads, pitch 1.8 mm
4 azimuthal sectors in one tile, each 7.5 degrees
12 tiles make full azimuthal coverage
p+ implants in n-type bulk
DC coupled with read-out electronics
40 modules were produced by Hamamatsu
4 sectors:
L2
L1
R1
R2
channels: 1 - 64
Outer active radius R = 195.2 mm
3 x 100 μm guard rings
Inner active radius R = 80.0 mm

## Slide 12: LumiCal test at CERN in 2014
4 LumiCal modules equipped with dedicated electronics (32 channels) glued on a 2.5 mm PCB
4.5 mm between tungsten plates
Tested in test beam at PS with 5 GeV e-/m
Effective Moliere radius :
24.0 ± 0.6 (stat.) ± 1.5 (syst.) mm
Energy fraction
Nucl. Instrum. Meth. A908 (2018) 198-205

## Slide 13: Thin detector assembly

## Slide 14: LumiCal test at DESY in 2016
14
New LumiCal module design : 750 mm thickness. 1mm between tungsten planes
Eight modules fully equipped with generic read out (256 channels)
Two modules were installed without tungsten planes : test of a tracker in front of LumiCal for electron/photon identification
Six modules formed the LumiCal
Test at DESY with 1 to 6 GeV electrons
Creation of a e-g beam

## Slide 15: Lumical test at DESY in 2016
e/g identification around 90%
Pad number

## Slide 16: lumical test at DESY in 2016
Energy response, longitudinal profile and effective moliere radius
8.1 ± 0.1 (stat) ± 0.3 (syst) mm
Effective Moliere radius :
arXiv:1812.11426

## Slide 17: BeamCal test beam
DESY 2010 :
  GaAs plate with Al metallization: 500 μm thick
  45 deg tiles, segmented into 12 rings, 5x5mm2 pads
  S/N ratio and CCE are good: CCE ~33% at 60V, S/N ~19 for all channels.
  4 independent pad areas show identical charge collection
DESY 2013 :
  Idea to test sapphire sensors parallel to the beam line
  Perfect electrical properties, excellent radiation hardness, but presently low charge collection efficiency
2017 :
  New design of the detector
  Aiming to build and test this new model in 2019
Red : 550V
Black 950V

## Slide 18: Radiation damage in electromagnetic shower
BeamCal maximum dose ~100 MRad/yr
Study is performed at California University of Santa Cruz
Exposition of Si, GaAs, Sapphire, Silicone carbide
300 Mrad Exposure
300 Mrad Exposure
500 m thick Al2O3
Dark current remain low for Sapphire

## Slide 19
Purposes
FCAL detectors : simulation
FCAL detectors : hardware
Electronics
conclusion

## Slide 20: LumiCal readout in 2014
Development of an ASIC for the 2014 test beam
Charge amplifier shaper with different gain (MIP/electron)
8 front end channels
Development of an 8 channel 10 bit ADC
Signal to noise ratio ~19
Cross Talk < 1%

## Slide 21: New readout : FLAME
FLAME: project of 16-channel readout ASIC in CMOS 130nm, front-end&ADC in each channel, fast serialization and data transmission, all functionalities in a single ASIC
FLAME prototype :
  Prototype 8-channel FE+ADC ASIC
  Prototype serializer ASIC
First tests are encouraging : FE ok, ADC ok, basic functionality of serializer are ok
JINST 10 (2015) P11012
JINST 10 (2015) P12015

## Slide 22: BeamCal readout
Firstly, BeamCal is hit by beam halo (muons)
  MIP deposition, low noise electronics
  Clean environment
  Good for calibration
~25ns later, BeamCal is hit by collision scattering
  Large deposit energy
  Physics readout
Dual slope integrator for calibration signal
  Integrate baseline (negative gain)
  Calibration halo signal is deposited and held
  Switch to physics mode, process and digitize Vop
  Then integrate calibration signal and digitize Voc

## Slide 23: Conclusions
The precise and complete geometry of the FCAL detectors has been simulated and showed that :
  above 10 mrad, the BeamCal high energy electron reconstruction efficiency is close to 100%
  Very good energy resolution and luminosity measurements with the LumiCal (stochastic term ~0.2)
  Tungsten seems to be the best candidate for the LHCal
A ultra compact LumiCal, including a tracker allowing electron/photon identification has been tested and the results are good and allow a good angle/position reconstruction
GaAs BeamCal gave relatively good charge collection efficiency and a new sapphire based prototype in under study
LumiCal prototypes of key blocks readout fabricated and first promising results obtained. BeamCal readout chip is under intensive study
2019
LumiCal test beam with :
  Between 18 to 20 thin layers
  Close to final front end electronics + readout and DAQ

## Slide 24: thanks

## Slide 25
Luminosity at e+e- collider
Bhabha scattering at low polar angles is used
e+e- e+e- (g)
L = N / s
Count Bhabha events
From theory
25
31/05/16
ECFA, Linear Collider Workshop 2016

## Slide 26
Luminosity precision details