## Slide 1: Calibration/alignment scenarios for ILD/ILC
Ties Behnke based on a talk by Jan Timmermans at the ILD meeting in Oshu City

## Slide 2: Initial requirements on tracking
Very lightweight, but stiff detectors
Stable to electric and magnetic fields (in particular power pulsing effects)
Robust against temperature and humidity gradients/variations
Precise alignment of (sub)detectors
Particular conditions:
Push-pull of the two detectors

## Slide 3: Initial and track-based alignment
Si tracking sensors positioned inside module ≈5μm
Modules positioned into higher order structures and surveyed/aligned at ≈100 μm
Pad positions inside TPC pad plane at <20 μm
Module positions inside TPC endplate (for current LP) ≈20 μm
Track based alignment precision needed:
  VTX: ≈2 μm
  Si inner: ≈4 μm, Si outer: ≈6 μm
  TPC: ≈20 μm
This ensures degradation of momentum resolution due to alignement errors w.r.t. nominal of less than 5%

## Slide 4: Track samples
Cosmics, but rate limited:
  Underground
  Duty cycle 0.5-1 % due to power pulsing
Beam collision data: tracks with known momentum from Z, J/ψ, ϒ.
Z-peak running @ L = 1032 cm-2s-1:
  30k hadronic and 1.5k μμ per 1 pb-1
  (takes ≈ 3 hours of beam)
LEP experience:
  10 pb-1 Z running for commissiioning (30 hours of beam)
  1 pb-1 per year (depending on “interventions”; 0.5 pb-1 per case
But could need more e.g. TPC has more (smaller) modules than at LEP. Need for alignment simulation study.

## Slide 5: Vertex Detector
Supported by beam pipe, which is supported by the inner support tube
During assembly: micron precise pre-alignment via optical survey
After installation: beam based alignment
  Within a layer using overlap between ladders (of few 100 μm)
  Global alignment of layers

## Slide 6: Si tracker
Internal hardware alignment of microstrip tracker uses infrared lasers passing through consecutive layers: relative resolution (between measurements) of 10 μm within 1 min
Deformations/displacements and temperature/humidity monitoring through in-fiber Bragg grating (FBG) sensors, embedded in composite materials (“smart structures”)
Frequency Scanning Interferometry under investigation
Track-based alignment:
  Total number of degrees-of-freedom: ~105
  For quick re-alignment: if sensor positions within modules known @ 5μm: ndof = ~104-5.104
  If only sub-detectors need to be re-aligned: ndof = 26

## Slide 7: TPC calibration issues
Need:
Good B-field map, 1-2 G precision and sufficient number of points (> 104 locations)
Hall probes mounted around TPC; NMR probes?
UV lasers:
  generating ionising tracks in drift volume
  illuminate the calibration spots on the cathode, which then generate electrons drifting over full length
Cosmics: duty cycle 0.5%, would give ≈10 Hz through hor. cut plane through TPC of 14 m2 at surface; less rate underground
Z-peak running: 10 pb-1 commissioning; 0.5-1 pb-1 for quick re-alignment check after “incidents” (e.g. Push-pull)

## Slide 8: In-situ calibration calorimetry
Absolute calibration ECAL can be checked/adjusted by comparison with tracker or using electrons and photons from Bhabha’s or return-Z + kinematical constraints. No need for running at Z peak
Cosmic rays may not be sufficient for MIP-scale monitoring, but MIP-like segments in hadronic showers can be used
Z-peak running: 1 pb-1 sufficient to have >1000 tracks per layer module AHCAL up to layer 20; To reach out to layer 48 would need 20 pb-1, , but can be reduced to 10 pb-1 by adding the mu-pair tracks.
500 GeV: 3% calibration out to layer 20 can be reach with ~2 fb-1
Beam halo muons: could be useful for endcap detectors; rate depends on shielding

## Slide 9: Conclusions
Z-peak running:
  Are the canonical numbers based on LEP experience (10 pb-1 commissioning, 0.5-1 pb-1 quick re-alignment) sufficient for ILD detector modularity?
  Simulation alignment excercise needed?
Alternatives at nominal beam energy?
  Z return
  Momentum calibration from Z, J/ψ, Υ (e.g. Graham Wilson at AWLC14)
Cosmics, yes (LHC has shown importance), but:
  0.5% duty cycle due to power pulsing
  reduced rate, because of underground location, but maybe not so deep
B-field mapping
  Can we measure it precisely enough?
  (study on use of detailed map in reconstruction ongoing)