Meeting ILD Electronics and Cooling
Roman Pöschl,
LAL Orsay Feb. 2018

---
Purpose of meeting
Coordination of integration of Ecal services (electronics and cooling) is pending since a while
Progress on both sides
Hardware development
Cooling loop and heat exchangers at LPSC
SL-Board at LAL
-> Morning 1: Understand how to bring these devices together
    Which constraints and how to remedy them?
Design
Considerations on power and cabling needs for Ecal
=> Morning 2: Occupation of space between Ecal and Hcal by Electronics Hubs and
     cooling circuitry
Technical drawing for cooling system of barrel and endcaps
=> Afternoon 2: Does the cooling system comply with current constraints of ILD in general and
    the Ecal in particular

---
Integration Heat Exchangers and SL-Board
Heat exchanger:
SL-Board:

---
Heat Exchangers and SL-Board - Comments
Design of heat exchanger exists since several years
Successfully tested with thermal demonstrator already in 2009 and also later
within EUDET Module
SL-Board is recent development within AIDA2020 and first step to compactly Digital
readout at the end of an Ecal slab
Will be thoroughly tested in 2019 including beam test
Observations:
Heat exchanger design assumes “empty space” along ASU front
Though already highly compactified current version of SL-Board extends over entire 18cm
Maybe the consequence when dreams face reality
What needs to be done to synchronise development?
Three options (poor man's view)
Redesign of heat exchanger?
Further compactification of SL-Board in next development cycle?
Integration of services e.g. Buffers and power regulators into last ASU or elsewhere?