Meeting ILD Electronics and Cooling
Roman Pöschl,
LAL Orsay Feb. 2018

---
Purpose of meeting
Coordination of integration of Ecal services (electronics and cooling) is pending since a while
Progress on both sides
Hardware development
Cooling loop and heat exchangers at LPSC
SL-Board at LAL
-> Morning 1: Understand how to bring these devices together
    Which constraints and how to remedy them?
Design
Considerations on power and cabling needs for Ecal
=> Morning 2: Occupation of space between Ecal and Hcal by Electronics Hubs and
     cooling circuitry
Technical drawing for cooling system of barrel and endcaps
=> Afternoon 2: Does the cooling system comply with current constraints of ILD in general and
    the Ecal in particular
Remark: Today concentration (mainly) on Ecal barrel

---
Between Ecal and Hcal
Current “design”
SiEcal Hub 1
(hub to external supplies and DAQ)
SiECal internal components
SiEcal Hub2
(internal hub to be checked whether heat
source)
Rails
Pipes of cooling system
SiECal
Hub 1
SiECal
Hub 2
Columns of slabs

---
Hub 1 – Closer look I
“Old and obsolote drawing by R.P. but hopefully instructive for discussion
Hub1 front side
~1000m
~30
-40 mm
~100
-150mm
Data transmission
and s/c
Ethernet connector
Clock, fast and
slow commands
Standard HDMI
connector (Type A)
LV input
USB type
connector
HV input
Standard HV
connector

---
Hub 1 – Closer look I
“Old and obsolete drawing by R.P. but hopefully still instructive for discussion
Hub1back side
~1000m
~30
-40 mm
~100
-150mm
HV out
Ethernet
Upper two rows:
LV, micro USB
Lower two rows:
Clock etc,
micro HDMI (Type C)
Inside Hub1:
- HV/LV distribution (1-many)
- Ethernet hub
- Clock fan out, fast signal distribution
- In this design Hub1 supplies all 25 columns of a stave
=> Huge number of cables
- May be doable if enough space available but ... Fixation of TPC needs to be taken into account

---
Constraint - TPC Fixation

---
Hub1 Constraints and consequences
Summary of constraints:
1) TPC Fixation will most likely limit space available for Ecal Hub1
2) Huge number of outgoing and incoming cables renders design very difficult
Consequences:
1) Reduce what is now Hub1 to simple patch panel that receive and fan out limited
number of service cables (LV, HV, data transfer)
2) Integrate a very much “slimmed” Hub1 in space between Ecal and Hcal
    that serves Hub2
    Hub1
    In: 48 V LV, 150 V HV, optical fibres for clock and data transfer
    Out: 12 V LV (after DCDC Conversion), 150 V HV, optical fibres for clock and
    data transfer

---
New architecture?
Rails
Pipes of cooling system
SiECal
Hub 1
SiECal
Hub 2
Columns of slabs
New hub sitting beween pipes of cooling system

---
Cooling system in ILD
Latest (?) drawings from AIDA2020 delivery report:
Question: Do cooling pipes for barrel enter only on one side of the barrel

---
Cooling system in ILD
62.8mm
100mm

---
Cooling system in ILD
- Comment: Drawing with cooling pipes found in early version of AIDA2020
  Report (maybe obsolete)
- If not obsolete: No compliance with current ILD Design

---
Backup

---
SiECal – Power supply scheme
D. Breton, H. Videau, D. Zerwas, R.P.
DCDC
Converter
12V/3.6V
In SiECAL Hub 2
Hub consumption ~5 W
Slab column
15x600mA, 36 W
x25
.
.
.
Power cable trailer <->
SiECAL Hub 1
PowerSource
48 V
DCDC
Converter
48V/12V
In SiECAL Hub 1
SiECAL Hub 1
Current ~21A

---
SiECal Power – Some numbers
1) The total power consumption of a stave 41 W (=25 columns) is about
25 x 41W =1000 W
2) These 1000W have to be provided by the main power supply of 48 W
=>current drawn from the power supply is
1000W/48V = 21 A (Note that these are average currents, peak current scale with DCDC conversion)
These 21 A arrive at the SiECAL Hub 1
3) 21 A require a cable with a cross section of about 1.5 mm2 maybe 2.5 mm2 .
Voltage drop:
ΔU = (0.0171/1.5)Ohm x 21A = 0.24 Volt => ~5 Volt after 20m in case of 1.5 mm2
with a thermal dissipation of 0.24Vx21A ~ 5W/m
ΔU = (0.0171/2.5)Ohm x 21A = 0.14 Volt => ~3 Volt after 20m in case of 2.5 mm2
with a thermal dissipation of 0.14Vx21A ~ 3W/m
ΔU = (0.0171/4)Ohm x 21A = 0.09 Volt => ~1.8 Volt after 20m in case of 4 mm2
with a thermal dissipation of 0.09Vx21A ~ 2W/m
Cable thickness subject to compromise between material budget and thermal dissipation
=> Propose to choose 2.5 mm2 (requires coordination with other detector components)
Remark: Numbers agree with the ones provided by C. Clerc and R. Cornat for DBD

---
Utility survey
Distributed by Yasuhiro beginning of September
Example SiEcal Power
Numbers were pre-filled but seem about to be correct
Note that this survey contains all subdetectors

---
SiECal Power – Cables/Fibres arriving at Hub1
HV
Fibres
LV
Data transfer,
clock etc.
SiEcal Hub1
Not to scale!!!
Number of cables include redundancy
LV cables will constitute a block of about 10x2.0 mm2
HV cables can be even thinner since they don't carry current O(10 mA)
Space consumption by optical fibres is also negligible
Professional CAD drawing will be provided by A. Gonnin
     at the beginning of November
SiEcal Hub1 has to be designed

---
SiECAL – Service lines
- Service lines leaving from endcap
- Service lines leaving from barrel
Drawing by Henri

---
ILD Cabling
Drawing as shown by
Karsten in Fukuoka
Coordination of review of
Cable and services by
R.P.
Prefered to do “my”
homework before annoying
others
Take this talk as the first
call to send me “your”
updated cabling schemes

---
The reality !? Belle II Vertex Detector
   Cables!!!!
 Thin but many

---
To do list - Electrical interfaces
Have to assume my charge and coordinate cable and service revision
Started with understanding system requirements for Ecal and to request updated
technical drawings for SiEcal
First step: From trailer to first hub
Power consumption agreed very well with pre-filled number in survey by Yasuhiro
Numbers on cable thicknesses agree with those from DBD (not a miracle but good to know)
Numbers don't look critical
SiEcal power scheme (most likely) requires DCDC Converters
Basis of current considerations but subject of technical decision
(Not today) survey on possible products by D. Breton over summer
DCDC converter is pulsed device that operates in magnetic field
Some negative experience in CMS
Considerations for other detectors not using DCDC Converters exist
Power dissipation and influence on other detectors to be understood
e.g. Ecal -> Hcal <= 5 W/m, can this be cooled away by Hcal cooling?
Subject to discussion
The list is for sure much longer and sorry for being late ...

---
Backup ....

---
Supplies – Naive block scheme
Interface region
On detector devices
External devices
Repeats 8 (barrel)
        + 8 (end cap)
        times
   48V V/21A
power supply for
  ASICs, DIFs
   and hubs
How many cables?
250V/150mA
power supply
for Si Wafers
  SiEcal Hub1
    (SIEH1_sn)
        per
stave, quadrant
SiEcal Hub2
 (SiEH2_sn_m)
        per
   slab column
HV Cable
DAQ computer
     (farm?)
Slow control
Slabs
Optical fibre
In electronic trailer:
LV: One power supply type stave/quadrant
HV: One power supply type stave/quadrant
DAQ farm: 1 computer stave/quadrant for acquisition
Slow control: One slow control computer
One clock source
Clock distribution,
 Fast (and slow?)
 commands
Optical fibre

---
Ecal in trailer
A
I
S
L
E
I
N
T
R
A
I
L
E
R
HV/LV
Services
One aisle should be enough
Add a second as safety margin
Computing
SC

---
Cabling and power
A reminder
Patch panels:
Space
Not far
Easy access
From barrel on barrel
From EC on EC
unlikely
C. Clerc, R. Cornat et al. LLR (Status 2011)
Study for DBD needs regular update!!!!
Use ICD

---
On DCDC Converters
... a poor man's point of view
- The advantage of a DCDC converter is that is realises the step down of the voltage
   without ohmic losses (in contrast to a “simple” linear regulator)
- From a “crash course” on DCDC converters I have learned that energy is stored in
  an inductor during time ton and released during a time toff
  The output of a (Buck) DCDC Converter is Vout = Vin x ton/(ton + toff)
  The duty cycle Vout/Vin determines the average current that is drawn from the power source Vin
- Ay each layer the voltage 4V is available from a 12V/4V DCDC Converter.
  The total current of a layer is 200mA (regard SL-Boards only for simplicity)
- Therefore the average current drawn from the power source is in this case
   (4/12)x200mA = 66mA