## Slide 1: ILC Layout with Positron Source
K. Yokoya
TCMB 2019.4.2

## Slide 2: ILC Layout Group (the name not official)
A small group at KEK started to think about the general layout of ILC
  Michizono, Hayano, Terunuma, Kubo, Okugi, Yokoya
The purpose is to prepare a complete set of optics decks for the entire machine to start CFS design
  There are many possible variations of the machine layout
  We cannot prepare CFS design for all the possible layouts
  Actually, optics itself is not important now. The issue is the geometry
The key is the positron system
We need to choose undulation/e-driven soon but NOT NOW
For now we have to down-select possible layouts within each of undulator/e-driven

## Slide 3: Undulator Case
Relatively simple, based on TDR
But many small changes
  The biggest change is 500GeV  250GeV
  Undulator 147m  231m
  Shorter dogleg after undulator (distance from undulator to target)
  Vertical bends at the ends of main linacs
  The electron injector moved upstream
  Two parallel solenoid lines in positron transport (opposite spin)
  Photon dump at ~2km away
  Exact location of other many small beam-dumps
  etc. etc.
Compilation almost done by Kiyoshi
  Based on 31.5MV/m
  CAD system being prepared by Hitoshi

## Slide 4: Remaining Choices for Undulator Case
5+5Hz
  Beam line for spent electron (after positron production)
  and its beam dump (8MW)
  Are these necessary in the initial construction?
  Voices from physics must be taken into account
    Z-pole, W pair threshold
Vertical layout
  Illustration next page
  Symmetric tunnel with inclined detector
  or, asymmetric tunnel with flat detector
  or, symmetric tunnel with undulator in curved section
  Our group almost chose (b)

## Slide 5: Vertical Layout in Undulator Case
TDR
TDR modified
Undulator in curved section

## Slide 6: e-Driven Case
Much more complex than the undulator case
Start with e-driven but must take into account possible upgrade to undulator scheme later
Possible scenarios (eML: electron main linac)
e-Driven system at downstream of eML, later replace it with Undulator system
e-Driven system at downstream of eML, later add Undulator System
e-Driven system in a different tunnel, later add Undulator System at downstream of eML (This is a variation of B but assign a different name)
e-Driven system at downstream of eML or in a separate tunnel, add undulate system in the new tunnel at the time of energy upgrade
e-Driven e+ source tunnel (L=1.1 km, w =9 m)

## Slide 7: Key Questions (1)
Can we remove e-driven system later on?
  Must take out and store radio-active devices on surface
Can we modify the tunnel later on?
  e.g.,
    Widen the tunnel
    Extend the tunnel a bit
    Add heavy shielding (top/bottom at positron target region)
  Can we introduce tunnel boring machine into the tunnel where the accelerator is already sitting?
Should the global timing constraint for the undulator scheme be satisfied in e-driven stage?

## Slide 8: Key Questions (2)
In TDR a dogleg is placed after the undulate to separate the electrons and photons
Should the tunnel dogleg be constructed in the e-driven stage ?
Or, no tunnel dogleg in the e-driven stage ? (cheapest e-driven stage but 2 doglegs needed later on)

## Slide 9: Key Questions (3)
Some of the questions are related to the order of the 3 possible upgrades
  Energy
  Luminosity (doubled number of bunches)
  Positron polarization
Can we assume something now?

## Slide 10: Example A1
Minimum at the e-driven stage
At the transition to undulator scheme
  Remove e-Driven, add two doglegs, move the modules near the end of eML to upstream
Do not change the positron target location

## Slide 11: Example A2
A dogleg in e-Driven stage
  The space for undulator may also reserved
At transition to Undulator, remove e-Driven scheme
Do not change the positron target location

## Slide 12: Example B2
Reserve a space for Undulator system
  (The figure below does not reserve a space for undulator itself
In this case the dogleg should be constructed from the beginning (i.e., B1 is not reasonable)
e-Driven system is located downstream
  presumably not at upstream (because of the undulator location)
At transition to Undulator scheme, add Undulator system
  The shield wall for the target for the Undulator scheme must be prepared from the beginning

## Slide 13: Example C1
Separate tunnel
Minimum tunnel. 2 doglegs at upgrade to Undulator

## Slide 14: Example C2
Separate tunnel
Prepare the space for Undulator/dogleg

## Slide 15: Case D
If the Polarization upgrade is at the energy upgrade time or later, undulator system may be constructed in the area of the new extended tunnel
Construct the Undulator system in the middle of extended eML (as in the design right after Snowmass 2005)
In this case, target shield wall need not be decided in the e-driven stgae
However, the electron energy at the undulation position must be more than 125GeV (ideally 150GeV)
Remove the BC (Bunch compressor) of the 1st stage and fill the pace by modules of eML, the length corresponds to 23GeV (Hayano)
  Total length of BC 230.6 (BC1) + 818.6 (BC2) = 1049.2m
  RF unit (39cavities) length = 58.3m
  1049.2/58.3 = 18 unit
  1.2753GeV/unit x 18 unit = 23GeV
Therefore in the case of 500GeV CM, the electron beam energy at this point is 250 – (125-15+23) = 117GeV This is not sufficient for positron production. This will be 142GeV, if upgrade to ECM=550GeV.

## Slide 16: Example D

## Slide 17: Vertical Layout
TDR tunnel is laser straight from the end of eML to the end of pML, including undulator/dogleg
If optimized for e-Driven only, no undulator/dogleg and the tunnel is symmetric from eML end to pML end.
Even in that case, at upgrade to undulator, tunnel bending in undulatorBDS still possible
  But an additional space for vertical bend would be needed （~200m?）

## Slide 18: Vertical Layout: e-Driven  Undulator

## Slide 19: Vertical Layout : e-Driven
Shortest layout
Follow the geoid up to VB
e-ML fills space down to VB

## Slide 20: Vertical Layout : Undulator after eDriven
Distances only tentative
VB can be inserted at B,C,D,E. Here select only B,D
  2 constraints: Line AB must the same as in eDriven stage
  Should not insert VB inside HDL (avoid complex spin motion)
Line ED does not follow the geoid  Point D is 11.5mm above the geoid
In the positron line there must be 0.421mrad VB somewhere (around 400MeV?)

## Slide 21: Today’s Question
Many of the choices can be made by the layout group
But I believe we need a general consensus for some of the choices
Do we need a face-to-face meeting (1-2 days) ?
Or, a long (many hours) phone meeting enough?
Or, everything can be decided by the layout group?
Layout group must prepare
  Table of pros and cons
  Rough estimation of the cost (or cost delta)