## Slide 1: Summary of the Accelerator Sessions
International Workshop on Future Linear Collider 2019
2019/11/01
Mathieu Omet (KEK)

## Slide 2: Disclaimer
The summary is (by nature) incomplete and is a personal view
  Several excellent and interesting results, which were presented during the sessions are not mentioned
I invite everyone to take a look at the contributions uploaded

## Slide 3: Accelerator Session Overview
Session name | Session count | Talk count | Discussion count
CFS | 3 | 9 | 2
Green Accelerator | 1 | 5 | -
Sources | 3 | 14 | -
Warm RF | 2 | 9 | 2
SCRF | 4 | 20 | -
ATF/DR/BDS | 2 | 8 | -
Total | 15 | 65 | 4

## Slide 4: Accelerator Session Conveners
CFS
  John Osborne (CERN), Nobuhiro Terunuma (KEK)
Green Accelerator
  Takayuki Saeki (KEK), Steinar Stapnes (CERN)
Sources
  Steffen Doebert (CERN), Joe Grames (JLab), Masao Kuriki (U. Hiroshima)
Warm RF
  Toshi Higo (KEK), Emilio Nanni (SLAC), Walter Wuensch (CERN)
SCRF
  Matthia Checchin (FNAL), Marc Wenskat (DESY), Yasuchika Yamamoto (KEK)
ATF/DR/BDS
  Philip Burrows (Oxford), Toshiyuki Okugi (KEK), Rogelio Tomas (CERN), Renjun Yang (CERN)

## Slide 5: Accelerator Session Conveners
CFS
  John Osborne (CERN), Nobuhiro Terunuma (KEK)
Green Accelerator
  Takayuki Saeki (KEK), Steinar Stapnes (CERN)
Sources
  Steffen Doebert (CERN), Joe Grames (JLab), Masao Kuriki (U. Hiroshima)
Warm RF
  Toshi Higo (KEK), Emilio Nanni (SLAC), Walter Wuensch (CERN)
SCRF
  Matthia Checchin (FNAL), Marc Wenskat (DESY), Yasuchika Yamamoto (KEK)
ATF/DR/BDS
  Philip Burrows (Oxford), Toshiyuki Okugi (KEK), Rogelio Tomas (CERN), Renjun Yang (CERN)
A big thank you to all accelerator session conveners!

## Slide 6
CFS
Notes: Conventional Facility and Siting

## Slide 7: Siting and facility layout considertaions
Themes
2 campus model
Collection of CFS basic plan
Volume optimization
Layout considerations

## Slide 8: HL-LHC civil works & ILC upgrade studies
Themes
Diesel powered hydraulic hammer
… the LHC’s worst vibration nightmare …

## Slide 9: Dump shielding & Muon radiation
Themes

## Slide 10: Infrastructure planning for FCC and CLIC / Planning of green ILC community
Themes

## Slide 11
Green Accelerator

## Slide 12: Renewable energy and waste heat usage
Solar heat utilization project in Iwate Prefectural University based on existing technology in Denmark
Waste heat recovery and offline transport is part of the concept (HAS-Clay)
Unused biomass will be used in surrounding industry (e.g. wood and wood chip drying, etc.)

## Slide 13: Electrical power situation in Tohoku

## Slide 14: Further possibilities of energy saving
Proposal of solid-state amplifier for ILC in terms of Green Accelerator by R&K Company Limited
  Cost per watt constantly decreasing, performance constantly increasing
  Maybe worth to reevaluate SSAs for ILC
Would have impact on e.g. waveguide design, LLRF systems, tunnel layout, etc.

## Slide 15: Increase klystron and modulator efficiency
Efforts at CERN in scope of CLIC
Klystron prototypes tested together with Thales and Toshiba (Canon)
S-band
Industry
X-CERN
50 MW
X-CERN
6 MW
industrial empirical limit
X-KEK
PPM, 50 MW
L-MBK ILC,10 MW
L-MBK CLIC, 20 MW
UHF-LHC
0.3 MW
Klystrons for science
L-ESS,1.5 MW
UHF-B-factory
1.25 MW
(µA/V1.5)
ITT 2960
33 MW
L-SNS, 0.55 MW
S-SLAC
65 MW

## Slide 16: Development of new klystrons at CERN
New bunching methods and simulation tools
S-band
Industry
X-CPI
50 MW
X-Canon
6 MW
X-Toshiba
PPM, 50 MW
L-MBK ILC, 10 MW
L-MBK CLIC, 20 MW
UHF-LHC
0.3 MW
Klystrons for science
L-ESS,1.5 MW
UHF-B-factory
1.25 MW
(µA/V1.5)
ITT 2960
33 MW
L-SNS, 0.55 MW
S-SLAC
65 MW
S-SLAC
150 MW
UHF-LHC
0.35 MW
X-BVERI
50 MW
X-CERN,50 MW
X-CERN, 8 MW
L-FCC, 1.5 MW
HE industrial prototype ; off shelf
S-Canon
7.5 MW
L-MBK/2S
CLIC, 24 MW
HE design, CERN (PIC simulations)

## Slide 17: Increase klystron efficiency
Common themes

## Slide 18: Reduction of operation cost studies for CLIC
Usage of permanent magnets (also being considered for ILC)
Operations schedule following energy prices
Study by Fraunhofer

## Slide 19
Sources

## Slide 20: Simulation of e- driven scheme
Results from previous simulations confirmed
Parameter scan (L-band Vacc, z offset, chicane angle, etc.)
Notes: flux concentrator

## Slide 21: Simulation of radiation environment of e- driven positron source
Realistic geometries, but not actual ones yet
  Gives an idea for following engineering design
Developed tools can be used for final design

## Slide 22: Thermal radiation cooled conventional target
Themes

## Slide 23: Polarized Electron Source R&D at JLab
Themes

## Slide 24: SuperKEKB positron source
Old material
New material for FC (flux concentrator) head

## Slide 25: Positron source optimization studies at CERN and Shandong University

## Slide 26: Plasma Lens as possible alternative Optical Matching Device (OMD)

## Slide 27: Energy and temperature simulations in photon masks at ILC undulators

## Slide 28: Flux Concentrator Opera Model
Themes

## Slide 29
Warm RF

## Slide 30: Different production approaches
  Round disk*
  Square disk
  Half structure
  Quarter structure**
  * Mature, but still
  ** has to be studied more

## Slide 31: Fabrication
Always trade off
between these two

## Slide 32: High precision manufacturing
Excellent performance even before tuning

## Slide 33: R&D for large frequency range at SLAC
S-band C-band X-band
108 GHz 300 GHz

## Slide 34: Assembly R&D at SLAC

## Slide 35: State of the art milling
Further discussions
  Milling technique
    Time consumption has to be reduced (quarter CLIC multicell structure at KEK took one week to be manufactured)
  Turning vs milling

## Slide 36: High power RF tests at CERN
Themes

## Slide 37: Simulations at Los Alamos
Atomistic modeling of surface evolution under strong electric fields
Simulations to understand breakdown mechanisms on atomic scale on clean flat Cu surface

## Slide 38
SCRF

## Slide 39: ILC cost reduction
Average accelerating gradient of main SRF LINAC is the largest cost driver
Higher gradients = fewer cryomodules  less $$
Higher Q0 = lower cryogenic costs

## Slide 40: Large grain

## Slide 41: SRF cavities with Nb3Sn film
Efforts at Cornell, Fermilab and KEK
Nb3Sn more efficient at 4 K instead of pure Nb at 2 K
  Lower dynamic load, lower static load, simpler cryo system
  2.6 GHz cavities smaller, thus cheaper
Technology maybe ready for ILC upgrade

## Slide 42: Nitrogen infusion
First N infusion at IPN Orsay, France on single cell cavity
They think they suffer from N contamination from the N vessel to the injector valve
Production and development of N infused cavities has started in at IHEP China

## Slide 43: Nitrogen infusion

## Slide 44: Nitrogen doping for LCLS-II HE cavities

## Slide 45: Trapped-flux Surface Resistance at High Gradients
Themes

## Slide 46: Plasma processing R&D
Themes

## Slide 47: Alternative Cavity Shapes for High Gradient Low-Surface-Field (LSF) Shape Cavity R&D
Jlab, KEK & SLAC

## Slide 48: ILC Prototypes (actual & planned)
Themes

## Slide 49
ATF/DR/BDS

## Slide 50: Beam instrumentation studies for future LCs
Goal: non-invasive way to measure beam size
Tests ongoing at ATF, CLEAR and Diamond light source
ODR: Sensitivity to 4 μm achieved at 250 nm @ATF2
ChDR: measured 63±2 μm, 30 μm not verified yet
  If requirements are all met, it would be a nicely simple and this easy scalable beam instrumentation tool for linear colliders

## Slide 51: Status of ultra-low βy* optics tuning at ATF / Nonlinear optimization of the Ultra-low (25β∗x×0.25β∗Y) optics
50 nm IP beam size achieved with ultra-low betay* optics @ATF2
Swapping octupoles for further beam size reduction at ATF2

## Slide 52: Completion of two-beam lumi tuning for CLIC
Simulation with realistic signal for CLIC BDS

## Slide 53: Wakefield effects in the CLIC BDS
Copper coated pipe is favorable for CLIC BDS
44% increase of aperture can mitigate the wakefield impact

## Slide 54: Intensity-dependent effects in ATF2 and ILC
ILC BDS long-range wakefields induce mainly IP position
3.6% luminosity loss at 2x1010 e- with an incoming position offset of 1 σy

## Slide 55: FONT beam stabilization results at ATF
Feedback On Nanosecond Timescale (FONT)
Study for ILC and CLIC at the ATF extraction line and the IP
BPM resolution improvement by integration -> better FB performance
  Jitter reduction from 96 nm to 41 nm with 2-BPM IP FONT feedback

## Slide 56
A big thank you to all the speakers for the excellent talks!

## Slide 57
Takeaways

## Slide 58: Takeaways
We have an excellent and strong world-wide accelerator community
We keep optimizing and advancing already mature technologies
We are well prepared and ready for all upcoming large-scale LC projects

## Slide 59: Takeaways
We have an excellent and strong world-wide accelerator community
We keep optimizing and advancing already mature technologies
We are well prepared and ready for all upcoming large-scale LC projects
Thank you very much for your attention!