## Slide 1: Muon Pair Production
Koichiro Shimomura (KEK IMSS)*
T. Yamazaki (KEK IMSS)
N. Kawamura (KEK IMSS)
D. Nomua (KEK IPNS)
Y. Kawashima (RCNP)
* Koichiro.shimomura@kek.jp

## Slide 2: Possible way from ILC to muon collider
Need efficient muon pair production
45GeV positron beam on fix target
Use Laser Compton gamma

## Slide 3: Possible way from ILC to muon collider
Need efficient muon pair production
45GeV positron beam on fix target
Although emittance is good O(10-4)
Intensity is not so large 2×107/s
Use Laser Compton gamma

## Slide 5: Muon pair production
e-
Laser
γ線
μ±
Target
Study Items
Electron beam energy from ILC 5GeV and 125GeV
Laser choice
Muon pair production target

## Slide 6: Laser Compton
Eγ [eV] γ energey Fγ [/s] Flux
Assume pulsed laser simultaneously excited ILCに同期したパP [W], Laser power λ [m], laser wave length
γ：electron γ factor
EL [eV]：Laser photon energy
θ [rad]：scattering angle（～1/γ）
me [eV]：electron mas
f [/s]：collision frequency
σ [m2]：Thomas sc. Cross section
A [m2]：Area size of larger beam
※ normally laser size
Ne：number of electron per pulse
NL：number of photon per pulse
→ High power, Shor wave length

## Slide 7: About Laser Exmaple
ILC 1 pluse structure 1312 bunch of 0.3mm length, 554ns interval
Repetition rate5Hz
Laser developed by AMPHOS Co.
  1μm wavelength
  200W power
  20J macro pulse（ width 1ms）with10Hz
  20mJ micro pulse ~1MHz in macro pulse
  Pulse width ~500ps
  compression with grating
  →1ps=0.3mm (94% efficiency)
  M2<1.25（focusing factor
  focusing size ~1.25 times of wavelength）
  Assume every laser pulse interacts with
  electron beam.
1ms

## Slide 8: Beam Dump Specification
From Yokoya

## Slide 9: Case1 5GeV Dump（E-1）
Beam Power at Dump max=100kW
Dump W=60kW
→ Assume 50kW（10μA）→1.25×1013 e-/pulse（1010 e-/bunch）
M2<1.25 hoever we assume w0=10μm.
  Because electron beam bunch length 0.3mm
  λ=1μm
  w0=10μm Layleigh length zR=πw02/λ=0.3mm
Use P. 3 formula
  Eγ = 450MeV (max)
  F = 8.4×1012 photons/s
  Divergence 0.1mrad

## Slide 10: Case2 125GeV Dump（E-5)
Beam Power at Dump max= PB max=2500kW
Dump W=17000kW
Asuume 2500kW（20μA）2.5×1013 e-/pulse（2×1010 e-/bunch）
w0=10μm
Use P. 3 formula、
  Eγ = 90GeV (Max)
  F = 1.7×1013 photons/s
  Divegence 4μrad
γ→∞でEγ→Ee
→、Better than 5GeV dump

## Slide 11: muon pair production via. γA→μ+μ-A
Dotted line is appoximate
c.f. Phys. Rev. ST Accel. Beams 12, 111301 (2009)
γA→μ+μ-A Total cosssection
r0μ：classical muon adisu
μ：muon mass
Au (Z=79, ρ=19g/cc) thickness 1cm
  5GeV dump、Eγ = 450MeV
  σ ~ 30μb
  125GeV dump、Eγ = 90GeV σ ~ 1300μb

## Slide 12: Muon Beam Intensity
125GeV dump
5.7×108 μ+μ-/s
5GeV dump
4.4×106 μ+μ-/s
125GeV dump θ~2mμ/Eγ=O(1) mrad
Beam size
5GeV dump 1mm
125GeV dump 40μm
Au（Z=79, A=197, ρ=19.3g/cm3）

## Slide 13: Comparison
Production method | ~1GeV p | 45GeV e+ | 5GeV e- | 125GeV e-
K.E (GeV) | 10-3～10-2 | 22 | 0.1 | 45
Energy width (%) | 10 | 20 | 20 | 10
emittance (mm*mrad) | O(103) | O(10-4) | O(103) | O(0.1)
Instensity (/s) | O(108) | 2×107 | 4×107 | 6×108
 |  | μ+μ- | μ+μ | μ+μ-
Suitable for muon collider !

## Slide 14: Improvement
How about 500GeV, 1TeV case ?
Oher particle pair production（π, K, B, τ etc.）
Any other photon source ?
Cavity enhancement ?（c.f. H. Shimizu, et al., NIMA 745 (2014) 63-72）