## Slide 1: SuperKEKB e+ source
Yoshinori Enomoto
KEK electron positron injector LINAC group

## Slide 2: Today’s topic
3 major findings since ALCW2018 (May 2018)
  New material for FC head
  Magnetic field correction in solenoid section
  Improvement of pulsed power supply and circuit
General lesson from specific topics in SupreKEKB

## Slide 3: OUTLINE
Introduction of SuperKEKB positron source
lesson 1 : avoid deformation of FC head
  Solution 1 : new material for FC head
lesson 2 : compensate deformation of magnetic field
  Solution 2 : BPM and steering coils inside solenoid
lesson 3 : decrease voltage on FC head
  Solution 3 : LCR measurement and control
upgrade plan

## Slide 4: OUTLINE
Introduction of SuperKEKB positron source
lesson 1 : avoid deformation of FC head
  Solution 1 : new material for FC head
lesson 2 : compensate deformation of magnetic field
  Solution 2 : BPM and steering coils inside solenoid
lesson 3 : decrease voltage on FC head
  Solution 3 : LCR measurement and control
upgrade plan

## Slide 5: Positron source setup 1
Positron target and capture section

## Slide 6: Positron source setup 2
target
BC (bridge coil)
FC(flux concentrator) head
LAS (large aperture S-band)
solenoid
FC head + BC + target = FC assembly

## Slide 7: Positron source setup 3
Φ2 mm hole for electron
W target
Temp sensor
Cooling water pipe
beam

## Slide 8: Positron source setup for SuperKEKB 4
Bridge coil
DC magnet
I = 600～750 A
Flux Concentrator
pulsed magnet
I = 6000～12000A
Ratio B @ target / B @ entrance of the LAS is important
stronger field is preferred in the following solenoid section
much stronger field is required @ target
Calculated by T. Kamitani

## Slide 9: Capture section after the target 1
AC_15_1
AC_15_2
AC_16_1
AC_16_2
AC_16_3
AC_16_4
FC
+
target
AC_17_1
AC_17_2
AC_17_3
AC_17_4
AC_18_1
AC_18_2
AC_18_3
AC_18_4
solenoid
solenoid
Q
Normal
LAS
Solenoid section (15 m)
Quad section (115 m)
Electron / positron separator
 | LAS | Normal S band
Acc. Gradient (MV/m) | 14/10 | 20
Aperture (mm) | 30 | 20

## Slide 10: Capture section after the target 2
To dumping ring
1-5
1-6
1-7
1-8
Normal x 32
LAS x 10
10m
2-6
2-1
2-2
2-3
2-4
2-7
2-8
Target & FC
15m long solenoid
About 100 Quad magnet
1.1 GeV @ DR

## Slide 11
1/25
x2.25

## Slide 12: Injection requirement
Life | 360 s
Current | 3.6 A
Injection bunch charge | 4 nC
Injection rate | 25* Hz x 2 bunch
Injection efficiency | 50 %
Circulation frequency | 105
Present working assumption (final)

## Slide 13: Injection requirement
Life | 360 s
Current | 3.6 A
Injection bunch charge | 4 nC
Injection rate | 25* Hz x 2 bunch
Injection efficiency | 50 %
Circulation frequency | 105
Present working assumption (final)
Life | 2500 s
Current | 0.5 A
Injection bunch charge | 0.6 nC
Injection rate | 6.2 Hz x 1 bunch
Injection efficiency | 50 %
Circulation frequency | 105
Typical Phase 3 operation
*total rep. rate is 50 Hz
The other 25 Hz will be used electron injection
Due to limitation by Belle2 detector and SuperKEKB ring
Required injection amount is still low.

## Slide 14: Positron charge and injection efficiency
9 hours
Primary e- 10 nC@e-gun
Primary e- 7 nC@target
Positron 1.5 nC@first BPM
Positron 1 nC@DR
Positron 0.55 nC@BT end dump
Positron current in the ring (LER)
Injection efficiency

## Slide 15: Simulation and experiment
Increase FC current
lesson 1 and 3
Increase efficiency
lesson 2

## Slide 16: OUTLINE
Introduction of SuperKEKB positron source
lesson 1 : avoid deformation of FC head
  Solution 1 : new material for FC head
lesson 2 : compensate deformation of magnetic field
  Solution 2 : BPM and steering coils inside solenoid
lesson 3 : decrease voltage on FC head
  Solution 3 : LCR measurement and control
upgrade plan

## Slide 19: After large discharge…
Slit gap got narrow.
Not possible to apply high voltage unless the gap will be expanded.

## Slide 20: New material for FC head
Increase yield strength of the material
Work hardening process was tested
  Result was not clear
Another approach using Cu-alloy
Avoid discharge
→Reduce electric field between gap
→manage slit distance
→avoid deformation
Requirements for material of the FC head are
Good brazing characteristic
High yield strength even after brazing
High electric and thermal conductivity

## Slide 21: Cu alloys
Cu
Cu-Zr
Cu-Cr
Cu-Ni-Si
were tested

## Slide 22: Evaluation of brazing characteristic
Cu-Zr(SH-2)
C1020
Cu-Cr(SH-1)
Cu-Ni-Si(NC50)
P:Palladium
A:Silver

## Slide 23: Measured properties of materials
Material | Cu (C1020) |  | Cu-Cr (SH-1) |  | Cu-Zr (SH-2) |  | Cu-Si-Ni (NC50) |  | 
Thermal cycle |  | After brazing |  | After blazing |  | After blazing |  | After blazing | After aging
conductivity %IACS | 102.2 | 102.1 | 90.8 | 76.0 | 81.1 | 68.5 | 50.3 | 25.1 | 48.8
Hardness | 87.4 | 30.4 | 71.6 | 60.0 | 45.9 | 55.8 | 95.3 | 61.2 | 95.4
Tensile strength Mpa | 327.4 | 232.1 | 402.6 | 237.2 | 443.1 | 238.3 | 648.7 | 323.7 | 658.8
Elongation % | 21.6 | 54.4 | 36.8 | 56.8 | 32.6 | 51.4 | 14.8 | 46.6 | 10.6
Yield strength Mpa | 322.3 | 12.9 | 293.6 | 57.9 | 348.2 | 40.8 | 551.8 | 109.7 | 513.1

## Slide 24: Strain-stress curve for C1020 and NC50
C1020
NC50

## Slide 25: Strain-stress curve for C1020 and NC50
C1020 after brazing
NC50 after brazing

## Slide 26: Strain-stress curve for C1020 and NC50
NC50 after aging
(precipitation hardening)

## Slide 27: Strain-stress curve for C1020 and NC50
C1020
C1020 after brazing
NC50 after brazing
NC50
NC50 after aging
(precipitation hardening)

## Slide 28: Yield strength
Chart: Yield strength (Mpa)
| C1020 | SH-1 | SH-2 | NC50
before brazing | 322.3 | 293.6 | 348.2 | 551.8
after brazing | 12.9 | 57.9 | 40.8 | 109.7
brazing + aging | 513.1
x40

## Slide 29: Production and simulation
After 6 months of manufacturing, new FC head using NC 50 was delivered on 18th Oct.
Evaluation at our test bench has started.
  Shows very good result now.
  Already reached 12.5 kA without discharge.
To evaluate mechanical stress, combined electromagnetic and mechanical simulation by ANSYS-Maxwell is in progress by Y. Morikawa.

## Slide 30: Insertion of insulator plates in the slits
20mm x 25mm x 0.2mm or 0.3 mm Zirconia (ZrO2) plates are inserted from 3 direction
It works well but not perfect
→discharge decreased but happened
→further investigation is needed

## Slide 31: Short summary 1
Be care about yield strength after brazing
New Cu alloy NC 50 has promising properties
Preliminary test shows very good result
Insertion of ceramic plate works well
  Further investigation is needed

## Slide 32: OUTLINE
Introduction of SuperKEKB positron source
lesson 1 : avoid deformation of FC head
  Solution 1 : new material for FC head
lesson 2 : compensate deformation of magnetic field
  Solution 2 : BPM and steering coils inside solenoid
lesson 3 : decrease voltage on FC head
  Solution 3 : LCR measurement and control
upgrade plan

## Slide 33: Solenoid field issue
600 A
600 A
650 A
600 A
650 A
400 A
650 A
400 A
650 A
650 A
Design
present
Solenoid section consists of 30 solenoid coils.
They are connected in 5 groups.
Each group is energized by independent power supply.
Design value and present value tuned to maximize positron yield is different

## Slide 34: Solenoid field issue
Measured by T. Kamitani
1,Prepare ballistic beam between SP_15_T and SP_16_5
2,Energize a part of solenoid by
1/10* max. value step.
3, Monitor beam position at SP_16_5
Measurement of deflection amount of 3 GeV electron beam
by asymmetric field in solenoid section

## Slide 35: Present layout
target
BPM and 1st steering

## Slide 36: BPM and steering coils inside solenoid
Steering coils
BPM
Install steering coils and BPM in solenoid section.
Detailed simulation of magnetic field by CST is also in progress
Bx
By
●It is not possible to use BPM for positron beam before separation.
●Use electron beam as a probe for magnetic field
●Development of a Fast BPM which can dissolve λ/2 @ S-band is under cosideration
Inner diameter of solenoid changes
Steel radiation shield end

## Slide 37: Asymmetry of magnetic connection
Iron yoke to connect flux of solenoid
need space for waveguide and support

## Slide 38: BPM and steering coils inside solenoid
K. Yokoyama
Very limited space
Design is in progress
In max. plan, between Acc. structures
Install 3 horizontal, 2 vertical steering coils
Install 5 BPM
BPM
Steering coil
support

## Slide 39: Short summary 2
Asymmetry of iron yoke might affect magnetic field.
3 GeV electron beam is deflected in solenoid section.
No direct measurement for positron but expected to be deflected.
Correction and monitor in the solenoid section is important
Fast BPM to measure positron directly is under consideration
  Such monitor will be useful for future positron source

## Slide 40: OUTLINE
Introduction of SuperKEKB positron source
lesson 1 : avoid deformation of FC head
  Solution 1 : new material for FC head
lesson 2 : compensate deformation of magnetic field
  Solution 2 : BPM and steering coils inside solenoid
lesson 3 : decrease voltage on FC head
  Solution 3 : LCR measurement and control
upgrade plan

## Slide 41
I[kA]
Vsupply[kV]
Vreturn[kV]
Vsupply-Vreturn[kV]
dI/dt]
～3MHz
Due to resonance by capacitance of the cable and inductance of the load
CT
High voltage probe
High voltage probe

## Slide 42: Snubber circuit
Load(FC)
snubber
Pulsed power supply
solid : C1 = 2 uF
dashed : C1 = 1 fF
Avoid discharge
→Reduce electric field between gap
→Reduce voltage keeping current
→suppress rapid current change

## Slide 43: Current and voltage waveform w or w/o snubber circuit
w/o snubber circuit
w snubber circuit

## Slide 44: Frequency response of capacitors
previous
new

## Slide 45: Optimization of the snubber circuit
Es = 5 kV
IFC = 3.5 kA

## Slide 46: Insertion of series inductance
Inductance of FC is about 1 uH
Inserted inductance has similar value

## Slide 47: Insertion position of inductance
L=H : insert L in return side
L=0 : without L
L=L : insert L in supply side

## Slide 48: Insertion position of inductance
L=H : insert L in return side
L=0 : without L
L=L : insert L in supply side
Without L and C
FC voltage | FC current | Snubber current | I/V (FC) | V/Es
1148 | 2245 | 356 | 1.96 | 0.230
1217 | 2800 | 375 | 1.41 | 0.398
2083 | 2631 | 394 | 2.47 | 0.213
2561 | 2792 | / | 1.090 | 0.512

## Slide 49: Optimization of the snubber circuit
Simulation by T. Natsui
Circuit simulation

## Slide 50: Optimization of the snubber circuit
LCR measurement

## Slide 51: Short summary 3
Load (FC) and power supply, transmission line, external circuit (snubber) should be designed as a system.
Circuit simulation, LCR measurement and voltage current monitor is important to reduce voltage across the FC.

## Slide 52: OUTLINE
Introduction of SuperKEKB positron source
lesson 1 : avoid deformation of FC head
  Solution 1 : new material for FC head
lesson 2 : compensate deformation of magnetic field
  Solution 2 : BPM and steering coils inside solenoid
lesson 3 : decrease voltage on FC head
  Solution 3 : LCR measurement and control
upgrade plan

## Slide 53: Upgrade plan
 | 2019 |  |  |  |  |  |  |  |  |  |  |  | 2020 |  |  |  |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
FC (present) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
FC (new material) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
FC (optimized design) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Snubber circuit |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Longer pulse operation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Steering coils |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
BPM |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Magnetic field measurement |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Operation
Design
Test
Biding
Manufacturing
Installation
We are planning big upgrade of positron source in 2020 summer shutdown.
budget is one of the concern…..

## Slide 54: Other topics
Deformation of magnetic field by return yoke before target
  Material consideration
  Simulation and beam measurement
Vibration measurement and resonance frequency
Temperature distribution simulation and measurement of the FC head