Extension of the e-Long Slab
CALICE Meeting
“everywhere”
28/09/2020
V. Boudry, J.C. Brient, F. Jimenez, R. Guillaumat,
M. Louzir, J. Nanni, Th. Dos Santos , H. Videau
Institut Polytechnique de Paris

---
1st ‘electric long slab’ (2018)
1. Support of interface boards + 12 ASUs (DBD)
  1. 2+6+4 ASUs = ~3.2 m
  2. Rotatably along long axis (for beam test)
    Rigidity : ≤ ~1 mm per ASU
  3. Total access to upper and lower parts
    1. 320μm Baby wafers (4×4 pixels) on the bottom

---
Signal over Noise ratios
1. The signal-to-noise ratio is defined as the most-probable-value (mpv) of a mip* divided by the pedestal width.
  1. in highly granular (self-triggering) calorimeters,
     a noise cut above 5–6 σ is mandatory,
     while a cut at ½ mip will ensure a good efficiency,
     resulting in S/N>10–12.
  2. A constant S/N ~ 19 is observed in the readout branch unaffected by the variations of the gain along the slab.
  mip* = [punch-through electron]

---
DESY-2018 beam test
1. 2 weeks beg of July: full test of all prototypes:
  1. Electric long slab: 8 FEV11 + baby-wafers
  2. Very clean response to “mip” (punch through e-)
  3. 1/2h beam on each ASU @ 0, 45, 60°
O. Korostyshevskiy
beam
DIF
Noise, cosmics &
readout errors

---
Electronics adjustments
1. Path length induced reflexions on clock line
  1. Fluctuation over logical level
  2. Extra clock tick → bad ASIC configuration
  3. RC filter adaptation (Sigrity simulation)
2. Impedance adaptation required depending on length
  1. Limited to 8 FEV12 + baby-wafers
3. Noise in the signal
  1. High frequency perturbation in the HV line
  2. Solved by RC filters on the HV line
    1. Possible back-propagation of ASICs noisy channel
       through HV ?
‘1’
‘0’
Also issues on the data routing...

---
ASU: 11 years of R&D
Milestone	Date	Object	Details	REM
1st ASIC proto	2007	SK1 on FEV4	36 ch, 5 SCA	proto, lim @ 2000 mips
1st ASIC	2009	SK2	64ch, 15 SCA	3000 mips
1st prototype of a PCB	2010	FEV7	8 SK2	COB
1st working PCB	2011	FEV8	16 SK2 (1024 ch)	CIP (QGFP)
1st working ASU in BT	2012	FEV8	4 SK2 readout (256ch)	best S/N ~ 14 (HG), no PP retriggers 50–75%
1st run in PP	2013	FEV8-CIP		BGA, PP
1st full ASU	2015	FEV10	4 units on test board 1024 channel	S/N ~ 17–18 (High Gain) retrigger ~ 50%
1st SLABs	2016	FEV11	7 units
pre-calo	2017	FEV 11	7 units	S/N ~ 20 (12)Trig, 6–8 % masked
1st technological ECAL	2018	SLABvFEV11 & FEV13 SK2a+ Compact stack Long Slab	SK2 & SK2a (⊃timing) 8 ASUs	Improved S/N Timing...
1st working COB	2019	FEV-COB	2×1/4 ASUs
1. Most complex element: electro-mechanical integration
  1. Distrib / Collect signals from VFE (ASICs),
     Analog & Digital with dyn. range ≥ 7500
  2. Mechanical placer & holder for Wafers → precision
  3. Thickness constraints
FEV11-COB
FEV11
FEV13

---
Potential FEV14 (2021 ?)
HPK  « No 8’’ wafer
bef. end 2021 »
1. FEV14: Design PCB just started
  1. Compatible 8’’ et 6’’ wafers ; → dimensions×1.5 (18×27 cm²)
    1. 6 Matrices 6’’ OR 2 × 1,5 Matrices 8’’
  2. 24 ASICs vs 16 ASICs
    1. Less cards ⇒ Less connections
  3. Improved scalability & maintenance
    1. 1 HV per card ⇒ independent test, exchangeability
    2. Bloc diagrams ⇔ Sharing BGA / COP ?
  4. LV Regulation on board with LDO ?
    1. + monitoring ? T°, V, ID (⇔ DB)
  5. Corrected data & clock distributions
    1. Must be OK for 2,1 m (EndCaps) = 8 FEV14 (12 FEV12)
    2. Timing ≤ 0,1 ns ? → for SK3 ?
  6. Compatibility new DAQ (≠ FEV13)
Artist view, non-contractual !
2
FEV13b?
1

---
A Long Slab with “FEV13b”
1. Adaptative design wrt FEV12
  1. Integration of new DAQ with Power Scheme
    1. (see Jihane presentation)
  2. Possibility to include FEV13b-COBs in LS
2. Modular design :
  1. Incremental length
3. Full equipped ends of SLAB
  1. 1st and Last ASU
  2. Regulators / Decoupling on each ASU
    1. Shower response at end of SLAB
  3. Possible integration new ASU’s in stack
2
4
4
8
⋮
12
?
?

---
First steps (2020):
1. Test LDO’s scheme in situation
  1. Several implementation on small insert mezzanine
     between ASU’s
  2. Measure stability and behaviour in PP
2. Implement the interface with SLBoard (v2)
  1. for Power Pulsing testing
    1. remove / raise current limitations
4. Package additionnal SK2a’s
  1. Test them
Compatible
with GradConn

---
Implication of HL schemes
1. HL-CLIC:
  1. ℒ × 2
  2. Nbunches →  : τTrain : 176 ns
  3. ƒrep ×2 : 50 → 100 Hz
Dominated by Set-up &
Conversion time:	P (~82μW/ch) ×2
1. HL-ILC:
  1. ℒ × 4 (6)
  2. Nbunches × 2 : τTrain : 1 → 2 ms
  3. ƒrep ×2 (3): 5 → 15 Hz
2. Dominated by ACQ time:
           P(~25μW/ch) × 6
1. Higher ℒ ⇒
  1. Occupation / bunch train ➚
    1. More memory for events
      1. But large margins
  Higher repetition rates × longer bunch
  1. Power = ƒrep × ∑ PASIC_part × τspill_part
    1. τspill	= τRamp-up	+ τTrain + τConv
       = 𝒪(μs) + { ... } + 𝒪(100’s μs)
      1. τTrain = ∆Tbunches × Nbunches
      2. τConv ∝ (occupancy + Noise ≥ thr.)
  ⇒ Full ZERO suppr. needed
290mW
SK2 chips
90mW
64 ch full conversion
26mW
Critical also for Power budget

---
Perspertive: Just In Time ?
1. Start of production of calorimeters in	2026 ?	⇐ achievable with LHC φ2 ?
   ➥ Preparation of production in	2025
   ➥ Pilote ECAL Module in	2024
   ➥ Pilote of SLABs in	2023
   ➥ 1st SLAB in	2022	⊃ all mechanical constraints
   ➥ 1st ASU in	2021
3. Power & Thermal simulation to be reviewed
  1. HL scheme
1. Final ASIC ≥ 2022
  1. Consumption & Timing
We are standing here

---
Back-up

---
Passive cooling
ECAL barrel
   3.0mm Det
+ 2.1mm W
ECAL end cap
First tests results in line with simulations
AIDA report 08/18
http://cds.cern.ch/record/2624680
ILC Case, standard ℒ
EUDET module (carbon structure) equipped with it’s heat exchanger 15 slab in EUDET module
 30 mm

---
Active cooling → ‘Continuous colliders’
R&D using CMS studies (Courtesy of Th. Pierre-Emile from CMS-LLR group)
Pipe insertion on a cooling prototype for FEA correlation
Copper plate prototype dimensions information
Pipe insertion process introduces some efficiency loss due to the thermal contact resistance.
The benefit remains significant with regard to a passive cooling
+3mm of Copper/Layer
Thermal static CFD analysis thermal field example using Fluent with 100W extracted and water mass flow rate of 7g/s through 1,5mm ID pipe
Pipe insertion on a cooling prototype
 = 2× cont. operation of a SLAB
∆T = 2.5°C

---
MIP fluctuation
1. 2 systematic effects has been identified
  1. Bandgap discrepancy (over 128 ASICs).
    1. σ=19.2 mV peak to peak=200mV
  2. Voltage linear decrease over slab length
2. Curve shape can be fitted by weighted sum of these two effects
3. Solutions
  1. Reduce bandgap in ASIC design (already reduced in Skiroc2a version)
  2. Compensate bandgap by software
  3. Select ASICs to mitigate fluctuation
  4. Use fixed length power supply to avoid discrepancy
MIP(\mathrm{ASU})=a*\mathrm{ASU}+b-c*\mathrm{bandgap(ASU)

---
POWER PULSING in SK2
Requirement:
25 µW/ch with 0.5% duty cycle
500 µA for the entire chip
Power pulsing:
Bandgap + ref Voltages + master I: switched ON/OFF
Shut down bias currents with vdd always ON
SK2 power consumption measurement:
123 mA x 3.3V ≈ 40 mW => 0.6 mW/ch
4 Power pulsing lines : analog, conversion, dac, digital
Each chip can be forced on/off by slow control
Measurements
Acquisition	88 mA , 290 mW	Duty Cycle =0.5%, 1.45 mW
Conversion	27.3 mA, 90 mW	Duty Cycle =0.25%, 0.225 mW
Readout	8.0 mA, 26.4 mW	Duty Cycle =0.25%, 0.066 mW
Skiroc2 power consumption with Power pulsing: 1.7 mW ie 27 µW/ch
[Speaker Notes: 2,7 kW pour 100 millions de voies vs 10kW le Lar d’atlas pour 10 000 voies]

---
Power estimations

---
Mip analysis
Convolution
fonction
𝑥
Simple Geant4 simulation for
5.5mm x 5.5mm, 325 um Si detector
Uniformly bombarded by 3 GeV
electrons beam with 60 degree angle
ƒ

---
MIP response vs position
1. mip MPV *cos(θ) vs ASU#
  1. OK for 4 1st ASU’s
  2. Small drop ~of signal ~2%/ASU for ≥ ASU#5
  3. Also hints similar drop on σped
     ⇒ Voltage & Gain drop ?
     Power pulsed mode with ballast et end of slab
     (or just random build-up effect from chip variability ?)