## Slide 1: BDS Design Issues with Short-Bunch LC Configurations
Glen White, SLAC

## Slide 2: Overview
Recent interest in collider options with short-bunch configurations -> long-term vision of ILC…
  Conventional and advanced (e.g. PWFA) acceleration technology
  arXiv:2010.00680 (3 TeV γγ collider with σz=5μm)
  Snowmass LOI’s
    SNOWMASS21-EF0_EF0-CF7_CF0-TF6_TF0-AF6_AF0-CompF2_CompF0-037(2).pdf Particle Colliders with Ultra-Short Bunches LoI to Energy Frontier
    SNOWMASS21-AF1-008.pdf Beam Physics of Extreme Bunch Compression
    SNOWMASS21-EF1-AF1-015.pdf Short-Bunch Paradigm Laserless γγ Collider
    SNOWMASS21-CF1-001.pdf Probing QED Cascades and Pair Plasmas in Laboratory Experiments
    SNOWMASS21-TF1-001.pdf Understanding the Fully Non-Perturbative Strong-Field Regime of QED
Implications for BDS design to maintain beam quality and provide clean environment to detectors
  Large energy spread, CSR, space-charge, backgrounds
Recently proposed short-bunch collider parameters raise challenges for BDS design

## Slide 3: 3 TeV PWFA LC γγ beam parameter study
arXiv:2010.00680: J.Chen, D.Schulte, E.Adli
PWFA requires large energy spread ~>1%
  Increased chromaticity of FFS
  Complicated high-order aberration control & tight tolerances
γγ options, large (100%) energy distribution of beam post-collision
  MDI design for detector backgrounds
Coherent SR in BDS bends
  e.g. emittance degradataion at LCLS for Ipk ~> 1 kA
19.1 kA

## Slide 4: The primary goal of FACET-II is to develop new technologies for next-generation research facilities
Counter-streaming beam and plasma electrons result in instability and form self-generated beam filaments and strong EM fields.
Convert joule-level electron-beam energy into gamma-rays via plasma instabilities
High intensity γ rays
A. Benedetti et al. Nature Photon. 12, 319 (2018)
Acceleration in plasmas created from crystals and nanostructures facilitate extreme gradients, continuous focusing – the properties needed for producing high-quality, high-energy beams
TV/m in Crystals and Nanostructures
  T. Tajima, et.al. PRL 59,1440 (1987)
X-ray pulse has single spike when radiation emitted by the electrons in beam tail, travels to beam head in time shorter than few gain times
Single spike FEL
R. Bonifacio et al. PRL 73, 70 (1994)
Future HEP collider
Alternative beamstrahlung mitigation strategy based on short, round beams: 100x reduction in beam power and thus costs
R. Blankenbecler, S. Drell, PRD 36, 277 (1987)
Beam Physics Advancement
Disruptive progress in accelerator technology is required in order to advance high energy physics
Ultra-short, high-intensity beams promise to facilitate seminal research opportunities far beyond HEP
The benefit of these opportunities outweigh the greater uncertainties associated with handling beams with such extreme parameters
Beam-beam collisions of short bunches can create the largest EM fields in the universe
Access the regime where dynamical mass generation becomes dominant over the Higgs mechanism
  V. Yakimenko, et.al. PRL 122, 190404 (2019)
Fully non-perturbative QED regime
Ultra-Short Bunches to Enable Qualitatively New Physics

## Slide 5: FACET-II : 3-stage bunch compressor S10 – S20
FACET-II will use LCLS-style photo-injector
  designed for @ 2nC with εx,y < 3 μm-rad
Three-stage compression with reverse-sign chirp in BC20
Existing “W-chicane” compressor limited to Ipk ~ 70 kA, with Δεx = 40 μm-rad due to CSR effects
FACET-II can operate with significantly higher compression than FACET-I In this mode, significant emittance degradation due to CSR is expected
6D Particle tracking to IP with 2D CSR

## Slide 6: New BC20 configuration
Proposed upgrade : “double-dogleg” style BC20 compressor
Reduced integrated bending & optimized optics mitigates CSR degradation
  Ipk ~200 kA with Δεx = 23 μm-rad (low espread)
  Ipk ~300 kA with Δεx = 40 μm-rad (high espread)
6D Particle tracking to IP with 2D CSR
δE/E = 0.9%
δE/E = 0.4%
Proposed upgrades to BC20 partially mitigates CSR emittance growth and generates high peak current electron beams

## Slide 7: Benchmarking simulation tools against FACET-II experiments important
Updated 2D CSR Model implemented in Lucretia
  Y. Cai, Phys. Rev. Accel. Beams 23, 014402
Discrepancy with 1d model seen for Ipk > 10 kA
Important to benchmark in experiment @ FACET-II
ML surrogate-modeling opportunity for improved simulation speed
  addressed in recent grant approval, work ongoing
Adjust Bunch Length with Laser Heater (Upgrade)
Going beyond 1-d CSR models important when compressing beyond 10 kA
R&D on efficient 2D CSR code implementations in tracking models ongoing

## Slide 8: Definition of design targets for emittance compensated CSR bunch compressor: FACET-III in ESA @ 30 GeV
1 μm-rad level emittance at <μm rms bunch length at a meaningful charge (Ipk>100kA)
70 – 125 GeV for HEP collider
10 – 30 GeV for extreme power FEL applications ()
Assumptions:
  Join FACET-II & LCLS Cu LINAC for 30 GeV in ESA to study limits of CSR emittance-compensated bunch compression
  for electron injector: εn = 0.5 μm-rad @ Q = 2 nC
    (TOPGUN) – Injector R&D not discussed here
Conduct feasibility study for CSR emittance-compensated bunch compressor

## Slide 9: Emittance degradation by CSR
δPz,CSR momentum kicks as CSR “Wake” catches up to beam in bends
  Correlated with longitudinal position along bunch
Projected emittance degraded due to misalignment of longitudinal slices along z axis in bending plane
  Can be analytically estimated for Gaussian profiles
Slice emittance also affected by CSR if sufficient mixing in z
  “phase mixing” ⇒ incoherent “sum” of C-S invariants.
  Particle tracking simulation required
At FACET-II
  Δεx ~ 40 μm @ max compression
  Effect severe enough to also limit max compression for W-chicane optics: Ipk <70 kA for “W”, 300 kA for upgraded optics
Dipole
P P+δP
z
x
Interaction of Coherent SR wake with bunch through and beyond bend magnets leads to degradation of emittances

## Slide 10: 30 GeV wiggler compressor with distributed CSR compensation using linear-kick interpretation for CSR
14X dogleg cells, triplet focusing lattice
ISR emittance growth <10%
Lbend = 2.5m, ρ = 667 m, B0 = 0.15 T, δE/E=0.25%, R56= 18mm
Sextuple correction fully compensates for CSR kicks using simplified linear-kick model
Notes: \

## Slide 11: Wiggler simulation: optical non-linearities + CSR
Does emittance compensation idea still work in fully 6D coupled case?
CSR compensation using sextupoles & quadrupole families
  Quads adjust dispersion between cells modified by CSR wakes & tailor compression profile for optimal CSR cancelation
εn = 0.5 μm-rad : σx,y* = 1 μm
  Pushed goal is to further increase focused bunch density
    Further challenges chromatic aberration control of magnetic optics
6D start-to-end tracking model built to test compressor design

## Slide 12: Optimization of 3D bunch density @ 2 nC
εn,x = 0.55 μm-rad σx,y,x = 0.9 x 0.9 x 0.5 μm
Ipk = 431 kA
εn,x = 24.5 μm-rad σx,y,x = 6.7 x 1.0 x 0.5 μm
Ipk = 394 kA
εn,x = 2.4 μm-rad σx,y,x = 1.9 x 0.9 x 0.9 μm
Ipk = 258 kA
No CSR
Sextupoles Optimized to cancel T566 & T166
Add 1D CSR Simulation
CSR with Sext + Quad corrections
Results from 6D tracking simulation in Lucretia with 1D CSR model + corrections
Emittance = 0.5 -> 2.4 μm-rad with σz < 1 μm
Optimization with full 6D tracking look promising

## Slide 13: Arc compressor option
Triplet bending lattice (9 cells)
  θtotal = 67 mrad @ 30 GeV
Second-order achromatic (without CSR)
Similar CSR-canceling performance as wiggler so far:
  ε = 2.5 μm-rad @ σz = 1 μm, Q=2 nC (Ipk = 250 kA)
Flexibility: relax compression (initial chirp):
  No re-optimization performed
  εx,n < 1μm-rad @ Ipk > 100 kA (Q=2nC)
  dE/E ~ 0.4% without removing chirp
Relaxed chirp: <μm slice emittance @ Ipk>100 kA
Design with net-bending (as part of ESA bend system) with similar performance

## Slide 14: Status summary & compressor design next steps
FACET-II expectations (E=10 GeV, L ~50m):
  Existing W-chicane
    Ipk < 100 kA, Δεn,x ~ 40 μm-rad
  Upgraded “double-dogleg” chicane (CSR minimized, not compensated)
    Ipk 200 - 300 kA, Δεn,x ~ 20 - 40 μm-rad
FACET-III expectations (E=30 GeV, L ~150m):
  Multi-cell wiggler or bending triplet lattice compressor (CSR compensated)
  Ipk ~ 250 kA with Δεn,x < 2 μm-rad, or
  Ipk ~ 100 kA with Δεn,x < 0.5 μm-rad
FACET-II(a) (E=10 GeV, L ~50m, 40-60 magnets) ? :
  Experimentally verify CSR compensation in multi-cell wiggler or bending triplet lattice compressor
Experimental confirmation of CSR models required to improve confidence in CSR compensation design

## Slide 15: FBCFS – 6 km Compressor
Final Bunch Compressor and Focus System
BC : R56 = 30mm
  10 x 900 FODO cells x 2
  2nd order achromatic
  large T566 & U5666
    16 sextupoles & octupoles
FFS: doublet + triplet (β* = 0.8 mm)
  V. compact: L*=0.5m, LB=10cm

## Slide 16: BC FODO Cell & CSR Shielding Possibility
μ = π/2, Nc=10, NBC=2
Lbend = 140m
θbend = 3 mrad
ρ = 46.2 km
B0 = 9 mT
Large bend radius provides possibility to shield CSR radiation
Transverse formation size: ~
  Shielding plates from 3.5 cm -> 0.8 mm required (tapered along BC for σz = 30 -> 0.1 μm)

## Slide 17: Next steps: Collective effects modeling R&D
1D CSR model implemented within Lucretia tracking code (similar to Elegant simulation)
  Extending to deal with changing geometries & shielding (a la BMAD)
2D/3D CSR solutions being studied, benchmark at FACET-II & apply to these designs
  e.g. currently deployed 2D model omits transient effects: developing theory to address this
    expected to be small perturbations in results
Improve tracking speed to allow more sophisticated optimization algorithms
  GPU algorithm implemented
  R&D ongoing in conjunction with ML group on surrogate modeling
Compression work (longitudinal space charge) effects expected to be important
  adding to tracking simulations.
CSR modeling based on existing 1D models
R&D ongoing to improve 2/3D, optimize execution speed & benchmark

## Slide 18: Next steps: Employ Machine Learning to speed up simulations
Machine Leaning based surrogate modeling (SM) is becoming a common tool in the accelerator community to speed up tracking operations with time-intensive collective physics effects
Application of ML tools are well suited for CSR tracking simulations
  CSR generates highly non-linear correlations in longitudinal and bend-plane dimensions
  SM can be trained to replicate these correlations
  SM is faster than physics simulation & parallelizable
Further development needed
  Understand which & how many beam parameters are required for accurate bunch compressor design & optimization
  Close collaboration with AD/ML group to explore alternative ML algorithms
Initial feasibility tests for fast, neural network-based surrogate modeling of CSR has demonstrated > 2 x N x (CPU/GPU) cores speedup
Particle tracking through bend
physics-based model vs. SM

## Slide 19: Backup Slides

## Slide 20: Survey Coordinates of FBCFS

## Slide 21: RF Phase Jitter
Fix final bunch length at 29μm
Vary C1/C2 ratio by adjusting φL1 & φL2
Optimum at BC1 σz~75μm
  Δσz/σz ~ 0.2% (Δz/σz ~ 1.7%)
Apply random jitter to each cavity
  Δφ +/- 0.1o
Track 105 MP * 100 random seeds
rms Bunch length jitter: Δσz
rms Bunch arrival jitter: Δz
Monte Carlo Simulation
Linear Contribution from 2-stage rf compression (LCLS CDR Ch.7):
2nd order from non-linear rf & T566 (Acc. Handbook 4.5):
For Gaussian:

## Slide 22: FACET-II 2-Stage Compression Configuration
BC14 OFF
BC11 E=135 MeV
BC20 E=8.2 GeV
: C1=6.5 C2=1.6
σz=300μm
σz=46μm
σz=28μm
L2 - φ=54o
L3 - φ=54o
L1 - φ=-90o
Q=10pC
R56 = 5mm
R56 = -46mm

## Slide 23: FACET-II Particle Tracking & Monte Carlo Simulation
Q=10pC
Q=150pC
γεx=0.3μm
γεx=2.6μm
RMS Jitter | Q=10pC | Q=150pC | Q=2nC (3-stage Compression)
Δσz/σz (%) | 2.9 | 3.3 | 48.4
Δz (μm) | 16.1 | 10.1 | 30.0
100-seed MC Sim
Start-to-end Tracking + ISR, CSR, Wakes & LSC

## Slide 24: ML Surrogate Model Development
2-d CSR (or 1-d model with >>10k macro particles) model slow for use with optimization engine
ML surrogate model helps if general enough
First test: feed-forward NN model using Matlab Deep Learning Toolbox to generate surrogate element model in Lucretia:
  Train on any element (or group of elements)
  Training parameters are input 6D coordinates & bulk properties of beam
  Example here trained on 20k data set with example bend+drift, 1-d CSR, consider 20% σz variability
Need to investigate how many bulk parameters can be included & input ranges
Liaising with ML group
Tracking time for 1M macro particles:
CPU = 5.8 s
ML = 2.4 s (per core), can be sped up many times via multi-core or GPU
Initial feasibility tests for fast, NN-based surrogate modeling of CSR look promising
Collaborate with ML group to develop further

## Slide 25: Linear Collider Luminosity @ Low Power
Parameter | Symbol [Unit] | ILC (TDR) | Collider with short bunches
Center mass Energy | ECM [GeV] | 250 GeV | 
Beam Energy | E [GeV] | 125 | 
Bunch Charge | Q [nC] | 3.2 | 1.4
Peak Current | Ipk [kA] | 0.4 | 1700
rms Bunch Length | σz [μm] | 300 | 0.1
rms Bunch Size | σ*x,y [μm] | 0.73, 0.008 | 0.01, 0.01
Pulse rate x # Bunches/pulse | frep [Hz] x Nbunch | 5 x 1312 | 700
Beamstrahlung Parameter | χ av , χ max | 0.06, 0.15 | 969, 1721
Beam Power | P [MW] | 2.6 | 0.12
Geometric Luminosity | L [cm-2s-1] | 3E+33 | 
HEP LC with round bunches: 20 times reduction of required beam power for equivalent geometric luminosity

## Slide 26: BC + FFS Performance (CSR OFF)
Δγεx = 30% from ISR
Sextupoles & octupoles tuned to reduce T566 & U5666 terms, cancel FF chromaticity @ resultant geometric & chromo-geometric errors introduced by correction
Momentum bandwidth ~0.1%
4th+ order vertical aberrations dominate after correction
  Need to investigate adding decupoles to mix of correction magnets
σz (min) ~ 100nm (limit from ISR energy spread)
σx,y (min) ~ 14 nm (core) (limit from residual aberrations)
Wakefields from shielding plates not simulated

## Slide 27: Start-to-End Tracking
All physics effects enabled – 1d CSR model
18 x 15 x 108 nm @ Q=10pC
Higher charges degrade longitudinal emittance due to Linac wake fields & CSR in BC1 & BC2

## Slide 28: Effect of Linac Wakes and CSR (1-d unshielded CSR model)
In each case, adjust L1 and L2 phases to maintain σz= 30 μm @ BC1 and minimize bunch length at IP
Longitudinal emittance grows vs. Q initially due to non-linear wake shape in L2, then additionally due to CSR in BC1
  Limits final bunch length for Q > 0.05 nC
CSR Horizontal emittance growth in BC1 > 0.1 nC and in BC2 >0.01 nC
  Emittance growth in BC2 exacerbated by non-linear magnets, without sextupoles and octupoles & for mono-energetic beam: Δεx ~ 10 μm-rad

## Slide 29: FFS Longitudinal Space-Charge
FFS longitudinal space-charge in converging beam (Tor, Frank NLC paper) NIM 390 (3), 11 May 1997, Pages 279-285 https://doi.org/10.1016/S0168-9002(97)00406-3
LC FFS sensitive to ppm energy deviations due to high chromaticity
Longitudinal space force due to converging beam (not 1/γ2 dependent)
From energy conservation: p.e. of bunch increases as focus -> comes from k.e. of beam and induces additional energy spread not compensated by sextupoles
NLC: OK for N<1011
  Scales as N/σz
  Small-z collider 1000X shorter bunches
  Imposes N or focusing limit?
MC simulation required to check

## Slide 30: Material Effects Considerations: Image Current Heating
For FACET-II at max compression: Single bunch T>melting for single pulse for apertures R<2-3 mm
For short-bunch collider, R exceeds desirable magnet apertures
Effects?
  Ablate um-thickness of metal from vacuum chamber surface each bunch?
Mitigation?
  Non-conductive vacuum chambers
  “Consumable” vacuum chambers
FACET-II Sector 20 @ E=10 GeV