## Slide 1
ILC accelerator R&D proposal for the PreLab phase
Benno List, DESY
ILC Europe Meeting
27.1.2021

## Slide 4: Proposal Document
All proposals in one document
83 pages
Open version available at https://agenda.linearcollider.org/event/9047/ (Technical_preparation_Ver3B.pdf)
Contains estimates for necessary resources -> basis for possible funding requests, neither commitment nor obligation

## Slide 5: Area 1: Main Linac and SRF
Resources: 41.7 MILCU*, 282 FTE-yr

## Slide 6: WP1: Cavity Industrial Production Readiness
Goals:
  Prepare cavity mass production
  Produce 3x40 cavities (40 / region), 3 x 16 for cryomodule installatioon (WP2)
  Decide tuner design
  Establish plug-compatible interface
  Develop recipe for cavity treatment
  (Try to) Establish improved cavity gradient / Q0

## Slide 7: WP2: Cryomodule Global Transfer and Performance Assurance
Goals:
  Produce 3x2 ILC type cryomodules (2 / region)
  Develop and prototype all parts: cold mass, coupler, magnet package
  Develop transport container / cage
  ”CM Global Transfer Program”: ship 1 CM/region to Japan,
  Demonstrate performance in Japan

## Slide 8: WP3: Crab-Cavity System
Goals
  Design, produce and test prototype cryomodule: cavity, coupler, tuner, cryomodule

## Slide 9: Area 2 = WP4: Electron Source
Goals
  Re-evaluate the drive laser design and cost, build a prototype to demonstrate the beam pattern,
  Design a higher voltage gun 350 kV with greater reliability/headroom, and build it,
  Evaluate if higher gun voltage and shorter laser pulse length relaxes harmonic bunching,
  Produce GaAs/GaAsP photocathodes with P>90%, QE>1%, work with vendor to commercialize
Resources
  2,6 MILCU + 6 FTE-y

## Slide 10: Area System 3: Positron Source
2 Concepts:
  Undulator source (baseline)
  Electron driven source (backup)
Downselect during prelab phase -> now planned for mid-24

## Slide 11: Area System 3.1: Undulator Positron Source
3 Work Packages
Resources: 0.9 MILCU, 10 FTE-yr
Main Goals:
  Undulator: improve parameters (simulation)
  Target and capture device: Build prototypes
    Demonstrate cooling concept and vacuum
    Demonstrate field strength and pulse length of matching device

## Slide 12: Area System 3.2: Electron-Driven Positron Source
4 Work Packages
  3 electron driven specific
  1 for target handling: both concepts
Resources:
  4.4 MILCU, 5 FTE-yr
Goals:
  Stable operation of (existing) target prototype
  Build flux concentrator prototype
  Design capture linac
  Scaled model of remote target handling concept

## Slide 13: Area System 4: Damping Ring
3 Work Packages
Resources:
  2.5 MILCU, 29 FTE-yr
Goals:
  Lattice and system design of damping rings, investigate permanent magnet option -> fixes beam polarity, no e-e- running
  Investigate & mitigate instabilities from collective effects (electron cloud, fast ion)
  Design fast kickers for injection & extraction

## Slide 14: Area System 5: Beam Delivery System
2 Work packages
Resources:
  2.2 MILCU, 14 FTE-yr
Goals:
  Further develop Final Focus System -> ATF3
  Prototype of final focus magnet package

## Slide 15: WP15: System design of ILC final focus beamline
Goals
  Further develop Final Focus System
  Test the concepts at ATF-3
    ATF3 ILC-FFS assessment system design
    Hardware optimization: vacuum chambers, magnets, IP-BSM laser, CBPMs, IP-BPMs
    Realistic S2E “beam-dynamics-driven” design and IP optimization
    ATF3 ILC-FFS oriented beam tests
    Long-term stability: nominal (10βx*×βy*) routine operation assessment
    High-order aberrations
    Other ILC R&D complementary studies: ILC collimation issues, ILC type CPBMs, new instrumentation

## Slide 16: Area System 6: Beam Dumps
2 Work packages
Resources:
  3.2 MILCU, 12 FTE-yr
Goals:
  Engineering design of main dump system -> impact on civil engineering design
  Engineering design of photon dump for undulator positron source

## Slide 17: Review Process
Technical Preparation Plan will be reviewed
3x3 Reviewers
  Regionally balanced
  External
Target: late February / March
2-3 hours each for SRF, DR/BDS/dump, sources
Review criteria:
  Is the R&D plan complete
  Are the Work Packages appropriate
  Less emphasis on cost estimates and list of possibly participating labs

## Slide 18: Towards the Engineering Design Reports EDR
Extend the work package structure: accelerator design -> EDR

## Slide 19: Summary and Conclusions
R&D Program for the Prelab Phase has been formulated -> Review in preparation
Money-wise, focus is on SRF, especially high gradient cavities and cryomodule transport
New activity on electron source
Positron source in focus, technology decision schedule provides time for (re)formation of R&D efforts
Damping ring design continues, permanent magnet option of interest -> would fix beam polarity (no e-e-)
BDS R&D continues – boosts ATF-3 programme, synergies with CLIC
Dumps are a critical R&D item
Next step: From R&D to design: Take up the overall accelerator design again – formulate plan for prelab
  Design complete accelerator systems
  Value engineering of important (in terms of volume or value) components and subsystems
  Provide input to management (cost and schedule) and civil engineering (power, cooling)

## Slide 20: Reserve

## Slide 21: WP5: Undulator Technology
Undulator regarded as mature
Goals:
  Simulation of heating by the photons
  Simulation with field errors and misalignment
  Optimization study of undulator parameters (pitch, K, aperture)

## Slide 22: WP6: Target Technology
Goals
  Design finalization of the rotating wheel with radiative cooling design and laboratory test of a stationary sector model. This is labelled as “priority” item.
  Magnetic bearings, feasibility study
  Fabrication of full model

## Slide 23: WP7: Magnetic Focussing System
Goals:
  Final design choice among the possible focusing devices with yield calculation
  Construction of the prototype of OMD and the rotating wheel

## Slide 24: WP8: Target
Goals:
  More accurate calculation of the target stress and fatigue effect to improve the design
  The required high vacuum (in the order of e−6 Pa at the accelerator) should be maintained for a long time.
  Stable target prototype operation; the test operation of the target prototype is set to start in the Spring of 2021.

## Slide 25: WP9: Flux Concentrator
Goals:
  The electrical, thermal, and mechanical properties of the FC conductor should be verified through simulations
  Transmission line design
  Power source design
  FC system (FC conductor, transmission line, and power source) prototyping and test operation

## Slide 26: WP10: Capture Linac
Goals:
  RF design of APS cavity
  Establish beam loading compensation and linac tuning method
  Power unit design and prototyping (L-band klystron + modulator)
  Solenoid magnet design
  Test operation of APS cavity with developed power source

## Slide 27: WP11: Target Maintenance (both source concepts)
Goals
  Complete the technical design
  Fabricate a mock-up to confirm the function
  Develop a fail-safe system

## Slide 28: WP12: System Design of ILC Damping Ring
Goals
  Optimize beam optics
  Evaluate effect of magnet field errors
  Investigate Potential to use permanent magnets: build prototypes

## Slide 29: WP13: Evaluation of collective effects in ILC damping ring
Goals
  Investigate (simulate) electron cloud (EC) and Fast Ion Instabilities (FII)
  Develop high-resolution fast feedback system

## Slide 30: WP14: System design of ILC DR injection/extraction kickers
Goals
  Perform long-term stability test of fast kicker system at ATF
  Develop injection kicker system for electron driven source

## Slide 31: WP16: Final Doublet Design Optimization
Goals
  Design final focus magnets for 250GeV
  Build prototype

## Slide 32: WP17: System design of the main dump
Goal:
  Establish the engineering design of the whole dump system.

## Slide 33: WP18: Design of photon dump for the undulator positron source
Goal:
  The system design of the photon dump is established at an engineering level, including the photon absorption structure, infrastructures for cooling, and the maintenance of the activated equipment