## Slide 1: ILCX2021 Machine-Source session summary
Masao KURIKI (Hiroshima U.)

## Slide 2: Machine Source Session
Discussion about ILC injector (electron and positron) development.
All 8 contributions for positron source development. No contributions for electron.
2 of 2 hours sessions.

## Slide 3
Day 1 (Oct. 27)
Power Incident on the ILC helical undulator vacuum chamber : K. Alharbi
ILC Positron Target : Material Analysis : T. Lengler
A tapered pulsed solenoid as optical matching device for the undulator based ILC positron source: C. Tenholt
Update on the development of the active plasma lens as an Alternative Optical Matching Device : M. Formela

## Slide 4
Day 2 (Oct. 28)
E-Driven positron source R&D by industry-government-academia collaboration : T. Takahashi (Hiroshima U.)
Target R&D of E-Driven positron source : T. Omori (KEK)
Beam-loading compensation on Capture linac of E-Driven positron source : S. Konno (Hiroshima U. )
System integration of E-Driven positron source: M. Kuriki (Hiroshima U. )

## Slide 5: Power Incident on the ILC helical undulator vacuum chamber
5
Unnnndulator!!!
Helical Undulator Prototype
D.Scott et al.,
https://link.aps.org/pdf/10.1103/PhysRevLett.107.174803
1st module
2nd module
× 22
Some photons are absorbed in Undulator leading thermal loss and quenching.
These photons should be collimated.
Khaled Alharbi

## Slide 6: Photon Mask Design
Mask Design depends on:
The average incident photon energy (Ideal and Realistic)
The available area reserved for helical undulator (319.66m)
A possible mask design:
Cylinder with tapered opening
Masks must mainly stop photons of few MeV energy.
Material: High Z-materials, large density and small radiation length are needed:
Material | Atomic number | Radiation Length (cm) | Melting point (K)
Copper (Cu) | 29 | 1.44 | 1358
Tungsten (W) | 74 | 0.35 | 3695

## Slide 7: Secondary Particles Density along Cu and W masks (Realistic Undulator)
Cu Mask
W Mask
Photons
Electrons
Positrons

## Slide 8: Results:
Undulator | Average incident photon energy (MeV) at Mask-21 | (W) at Mask-21 | Mask Material | PEDD (J/g/Pulse) | (K/Pulse) | (W/m) at Wall |  | Photon Polarization (%)
Ideal | 1.77 | 270 | Cu | 1.4 | 4.0 | 0.22 | 98.3 | 41.3
 |  |  | W | 2.1 | 15.0 | 0.03 | 99.6 | 
Realistic | 2.00 | 320 | Cu | 1.6 | 4.1 | 0.26 | 97.6 | 38.7
 |  |  | W | 2.3 | 17.0 | 0.04 | 98.4 | 
Undulator | Average incident photon energy (MeV) at Mask-21 |  | Mask Material | PEDD (J/g/Pulse) |  |  |  | Photon Polarization (%)
Ideal | 1.77 | 270 | Cu | 1.4 | 4.0 | 0.22 | 98.3 | 41.3
 |  |  | W | 2.1 | 15.0 | 0.03 | 99.6 | 
Realistic | 2.00 | 320 | Cu | 1.6 | 4.1 | 0.26 | 97.6 | 38.7
 |  |  | W | 2.3 | 17.0 | 0.04 | 98.4 | 

## Slide 9: Table of irradiation
positions: top 
middle 
bottom 
 | Spot | Irradiation Duration [min] | Repetition rate [Hz] | Pulse length [ms] | DT per pulse [K] | Duty factor | Tave at spot [C]
Oct18-1 | Top | 90 | 10 | 1.5 | 335 | 0.03 | 155
200μm | Middle | 40 | 20 | 1.5 | 350 | 0.015 | 98
 | Bottom | 40 | 100 | 1.0 | 240 | 0.10 | 365
Oct18-2 | Top |  |  |  |  |  | 
250μm | Middle | 45 | 120 | 1.0 | 230 | 0.12 | 425
 | Bottom | 40 | 140 | 0.5 | 170 | 0.07 | 300
Oct18-3 | Top | 40 | 100 | 0.5 | 170 | 0.05 | 280
500μm | Middle | 40 | 100 | 1.0 | 230 | 0.10 | 435
 | Bottom | 40 | 140 | 0.5 | 160 | 0.07 | 345
Electron beam diameter: 0.12 mm
Continuous irradiation of the middle spot for Sample 1
 Much heavier load than expected at the ILC
3.5 MeV Electrons
ILC Positron Target: Material Analyses
T. Lengler (U. of Hamburg)

## Slide 10: Diffraction analysis
Polycrystalline Ti-6Al-4V
wavelength: 0.14236 Å
α-phase: 95%
β-phase: 5%
β-phase
α-phase
www.tf.uni-kiel.de/matwis/amat/mw1_ge/kap_3/backbone/r3_3_1.html
hcp
bcc

## Slide 11: Analysis
no major changes caused by intended irradiation
α- and β-peaks stable
no indication of major radiation damage

## Slide 12: A tapered pulsed solenoid as optical matching device for the undulator based ILC positron source: C. Tenholt

## Slide 15: Update on the Development of the Active Plasma Lens as an Alternative Optical Matching Device M. Formela

## Slide 18: E-Driven Positron Source R&D by Industry-Government-Academia collaboration
T. Takahashi

## Slide 21
ILC E-Driven e+ Source
Rotation Target R&D
28-Octorber-2021
ILCX 2021, Tsukuba, Fully Remote
presented by T. Omori (KEK)
Works by Rigaku, Hiroshima U., and KEK

## Slide 22
Ferrofluid Seal
ferrofluid
= base oil + iron powders (~10 nm) + surfactant
(oxide iron powders) (界面活性剤)
Vacuum seal
+
Rotating shaft
Air
Vacuum

## Slide 23
No sub-pumping
（intermediate point: atmospheric pressure）
sub-pumping
Turbopump
~5x10-4 Pa
sub-pumping
Ion Pump
~ 3x10-6 Pa
rotating at 225 rpm (design value)
1.1x10-6 Pa
Pressure of Main Chamber (Pa)
10-6
10-5
9-Sep-2020
6-Nov-2020
3-Dec-2020
8-Jan-2021
We started the experiment at the beginning of September 2020.
Spikes
Spikes disappear
Result: Spikes disappear.
Conclusion: Two-stage seal is effective
It seemed vacuum still went better and better, but we are forced to stopped the experiment on 8-Jan-2021 to go next step.
10-4
Prototype #2: Two-stage Vacuum Seal
One stage
Two stage

## Slide 24
We added the dummy target disk.
Fabrication at RIGAKU workshop
Jan. 2021
Assembling at KEK
Feb.-Mar. 2021

## Slide 25
Spike
~ 1.2E-6 Pa
x 1.5
Prototype #2 with Dummy Disk
Vacuum Data, Enlarged Plot : From 24th July to 29th July, 2021
Rotation at 225 rpm (design value)
Pressure of Main Chamber
Pressure of Intermediate Point
7.4x10-7 Pa
29th July
We achieved 7x10-7 Pa with dummy disk
with small spikes
2x10-6 Pa
1x10-6 Pa
6x10-7 Pa

## Slide 26: Beam-loading Compensation on Capture Linac of E-Driven Positron Source
S. Konno, M. Kuriki, Z. Liptak ,
T. Takahashi, H. Nagoshi (Hiroshima University)
K. Yokoya, J. Urakawa, M. Fukuda,
Y. Seimiya, T. Ohmori (KEK)
S. Kashiwagi (Tohoku University)
28-October-2021

## Slide 27
Beam loading compensation
  A deceleration field is generated by beam (beam loading).
  Therefore, cavity voltage varies giving energy fluctuation in a pulse.
  Because the positron is not on crest of RF curve, not only the real component, but also imaginary component is induced.
  Beam loading can’t be compensated by adjusting RF amplitude.
Beam voltage
RF voltage
Cavity voltage

## Slide 28
Phase plot
: Steady-state RF voltage
: Transient-state cavity voltage
: Transient-state beam voltage
(Don’t change the input power.)
: Steady-state beam voltage
Off crest beam loading compensation
  In the case of off crest, the above method cannot compensate for complex components.
  By applying phase modulation, compensation is possible.
Change the RF phase
Phase plot
: Transient-state RF voltage
is not constant.
: Steady-state RF voltage (phase modulation)
is constant.

## Slide 29
Normalized standard deviation
at
Time dependence of cavity voltage
:Average voltage
Beam loading compensation off crest
Phase difference [rad] | Input power [MW] | Beam loading current [A]
Phase difference [rad] | Input power [MW] | Beam loading current [A]

## Slide 30: ILCX2021 Accelerator Source Session
System integration of
ILC E-Driven Positron Source
M. Kuriki, S. Konno, Z. Liptak,
T. Takahashi, T. Omori,
J. Urakawa, H. Hayano, K. Yokoya

## Slide 31
Target Section
For the radiation shield, the target is surrounded by 2m thick boronized concrete blocks.
Used targets are stored in a cavern.
The target module consists of target, FC, collimator, and the first RF cavity. The module is mounted on a wagon with shield.
It is designed with copulations A. Miyamoto and P. Sievers.
Unit (m)

## Slide 32
L-band 1.27m APS
3/4λ
λ/2
3/4λ
1500.00
1500.00
1500.00
1500.00
115.4
173.1
173.1
6692.4
Capture Linac unit
L-band 1.27m APS
L-band 1.27m APS
L-band 1.27m APS
RF load
RF load
λ
230.8
BPM
BPM

## Slide 33: 2m L-band TW Accelerator
Accelerator for Positron booster
Shunt impedance and length are scaled with the same manner.
Accelerating voltage per tube is with 22.5 MW input.
Parameter | Value
Shunt impedance | 48.0 MW/m
Length | 2.00m
t (attenuation) | 0.261
tf | 1.28 ms
RF voltage
Beam loading voltage
Pulse
train
Cavity voltage
Beam loading current

## Slide 34: The whole system

## Slide 37: Summary of Summary
8 contributions only for positron source.
4 for Undulator and 4 for E-driven.
Progresson target, capture device, photon colimator for Undulator.
Progress on target, thermal analysis, beam loading compensation, and the system integration for E-Driven.
Positron R&D is one of the main issue in pre-lab. We source group are vigorous! (at least until the pre-lab. end).