## Slide 1: ILC 1.3 GHz CM. 2021
Design status on 10/28/21,
by Y. Orlov, behalf FNAL and KEK teams

## Slide 2: Outline
1.3 GHz cavity
SC magnet
Cavity string
Cold mass
Cryogenic piping compare
1.3 GHz CM
Transportation
Interconnection

## Slide 3: 1.3 GHz ILC cavity (short-short)
9-cell cavity, TESLA style
1247.4mm, flange to flange
Support lugs - LCLS-II
He vessel material: Ti Gr2
2-phase pipe material: SS316L
Ti-SS transition joins used:
- warm up nozzle
- 2 phase pipe connection
Ti-SS transition
SS
Ti Gr2
support lugs
Ti-SS transition
342
24

## Slide 4: 1.3 GHz cavity #1 (with tuner, magnetic shielding and GV)
LCLS-II style tuner will be used
  (cavity #1 – tuner with extended arms)
One-layer external magnetic shieled (LCLS-II style)

## Slide 5
Bellows and Magnetic shield
Mag. Shield inside helium tank as suggested in TDR (KEK)
This cross-sectional view is confidential? KEK got from the FNAL document.
(From Kirk presentation)

## Slide 6: 1.3GHz ILC Cavity with Mag shielding (for discussion)
External Mag. Shielding (LCLS II)
Internal Mag. Shielding (KEK)

## Slide 7: 1.3 GHz ILC magnet
ILC conduction cooled splittable quad, ~1 m
Magnet 2-phase pipe have extra volume for He
Optional: Magnet 2phase pipe from Al (Al-SS transition?)
342
24
250
1000
Al thermal straps
support rails

## Slide 8: From IPAC2021 paper

## Slide 9: 1.3 GHz cavity string-A
GV
GV
BP bellows with
Al gaskets
2 phase bellows
DS GV with spool

## Slide 10: 1.3 GHz cavity string-B
GV
GV
BP bellows with
Al gaskets
2 phase bellows
splittable SC magnet
magnet BP spool

## Slide 11: 1.3 GHz cold mass upper
70 K lower thermal
shield
Not shown
cavities/magnet
needle bearings
supports
Invar rod

## Slide 12: 1.3 GHz cold mass – ILC
quad can be replaced with
a 1.3 GHz cavity
70 K Insulation
70 K thermal shield
All cryogenic piping and
Cavities He Vessels are wrapped
With 10 layers of MLI
5K&70K thermal intercepts

## Slide 13: 1.3 GHz ILC CM-B
1.3 GHz ILC-2021, is the next generation of:
1.3 GHz T4CM + 1.3 GHz XFEL + 1.3 GHz LCLS-II

## Slide 14: 1.3 GHz ILC CM-B
8 tuner motor
access ports (LCLS-II)
magnet current leads box
(with HTC CL-KEK)
Vacuum vessel is identical for types “A” and “B”

## Slide 15: LCLS-II tuner access port

## Slide 16: KEK SC magnet CL
Akira Yamamoto, Hirotaka Shimizu, and Nobuhiro Kimura
in Cooperation with Vladiir Kashikhin, and
with acknowledgement to Toshiba Corporation
Date: 2021-8-12

## Slide 17: 1.3 GHz ILC CM-A, layout

## Slide 18: 1.3 GHz ILC CM-B, layout
Magnet instrumentation area
Cold: MC-MC
Warm: MC-MC

## Slide 19: 1.3GHz ILC CM-B, layout
12804
(CM slot)

## Slide 20: ILC CM line designation
Line A
Line C
Line E
Line GG
Line B
Line H
Line F
Line D

## Slide 21: ILC CM cryogenic piping sizes

## Slide 22: TESLA-style cryomodules compared - 1
Yuriy Orlov and Tom Peterson for the LCLS-II Team LCLS-II CM Assembly Meeting 17July 2014
(38.9)
(68.9)
(76.2)
(76.2)
(72.0)
(57.0)
(60.2)
(300)
(57.0)
BLUE for ILC 2021CM

## Slide 23: TESLA-style cryomodules compared - 2
Yuriy Orlov and Tom Peterson for the LCLS-II Team LCLS-II CM Assembly Meeting 17July 2014
NO,
but retain
intercepts
BLUE for ILC 2021 CM
1326.7
12804

## Slide 24: Typical 45’ container

## Slide 25: Transportation of 1.3 GHz CM
Inside volume of 45’ container
Transportation platforms
(proposal)

## Slide 26: Transportation of 1.3 CM
DESY transportation
feed cap
DESY transportation
end cap
(~7cm)
(~8cm)

## Slide 27: 1.3 GHz CM’s interconnection
HOM absorber
700 mm
8 mm
11 mm

## Slide 28: 1.3 GHz CM’s interconnection
CM2
CM1
interconnection bellows
HOM

## Slide 29
Backup slides

## Slide 30: ILC TDR Layout
Damping Rings
Polarised electron source
E+ source
Ring to Main Linac (RTML)
(including
bunch compressors)
e- Main Linac
e+ Main Linac
Parameters | Value
C.M. Energy | 500 GeV
Peak luminosity | 1.8 x1034 cm-2s-1
Beam Rep. rate | 5 Hz
Pulse duration | 0.73 ms
Average current | 5.8 mA (in pulse)
E gradient in SCRF acc. cavity | 31.5 MV/m +/-20% Q0 = 1E10

## Slide 31: 1.3 GHz ILC CM, Section 1

## Slide 32: 1.3 GHz ILC CM, Section 2

## Slide 33
Tuners
XFEL
LCLS-II
T4CM

## Slide 34
Magnet Packages with BPM
XFEL
LCLS-II
(BPM before Magnet)
T4CM

## Slide 35
1.3GHz cavities (9 elliptical cells)
XFEL
LCLS-II
T4CM
(Long-Short)
(Long-Short)
(Short-Short)
Ti Mini CF
Ti-SS Transition
He Vessel Bellows