Update on the Development of the Active Plasma Lens as an Alternative Optical Matching Device
M. Formela, N. Hamann,
K. Floettmann, G. Moortgat-Pick,
G. Loisch, S. Riemann
ILCX2021
2021-10-25

---
Table of Contents
Status-quo
Principle of an Active Plasma Lens
Advantages of a Plasma Lens
Optimization Results & Optimum Stability Test
Near Future Plans
Plasma Lens Experiments
Improved Particle Tracking
Back-up
ILCX2021

---
Status Quo

---
Principle of an Active Plasma Lens
ILCX2021

---
Advantages of a Plasma Lens
ILCX2021
	Current ILC Options
	Quarter Wave / Transformer (QWT)	Plasma Lens / (PL)
Dephasing	- helical	+ sinusoidal
Chromaticity	- high	+ low
Eddy current / in rotating target	+ manageable	++ spatially / confined field

---
Dephasing Advantage of the Plasma Lens
The azimuthal magnetic field of the plasma lens leads to a sinusoidal trajectory (helical for QWT), which results in an effectively shorter path and therefore smaller longitudinal spread, the so called dephasing.
ILCX2021
QWT
Plasma Lens
Longitudinal cut (14 mm)
 Dephasing

---
Optimization Results of
Tapered Active Plasma Lens as OMD
Simulations
with ASTRA
40.6% captured e+ within DR energy acceptance of .75% (14 mm long. Cut)
→ ~50% improvement over ILC’s current proposed OMD (QWT) design
Captured Yield Stability of the Opimum
		Captured Yield Deviation / for deviations in optimized parameter by
Parameter	Symbol	-10% offset	+10% offset
PL Length	zmax	-0.3% yield	-0.2% yield
Opening Radius	R0	-0.1% yield	-1.1% yield
Tapering Strength	g	-0.2% yield	-0.3% yield
Current strength	I0	-1.5% yield	+1.2% yield
PL-SWT distance	d	+0.2% yield	-0.2% yield
SWT Phase	φ0	-0.5% yield	-0.4% yield
ILCX2021
R(z) = R_0(1+gz)^{n/2}
Optimized Parameters at I0 = 3, 6 & 9 kA
	Symbol	Optimal / Value
PL Length	zmax	5.9 cm
Opening Radius	R0	3.8 mm
Tapering Order	n	1
Tapering Strength	g	300 m-1
PL-SWT distance	d	1 cm
SWT Phase	φ0	230°
Taper profile:

---
Near Future Plans

---
Dephasing Advantage of the Plasma Lens
Sources:	Loisch, Gregor, et al. "Jitter mitigation in low density discharge plasma cells for	wakefield accelerators." Journal of applied physics 125.6 (2019): 063301.
Preparatory Plasma Lens Experiments:
Determine max. current I0 & required voltage U
Measure plasma density ne
Via spectroscopy of spectral line broadening
Temporally & longitudinally resolved
transversal resolution to be investigated
Plasma Cell provided by PITZ, DESY Zeuthen
Previously used for plasma wakefield acceleration experiments

---
Optimisation Conditions
No Beam Self-interaction (neglected Coulomb interaction)
Only 1st SWT (neglect 2nd SWT and three TWT of pre-accelerator)
Idealised Plasma Lens (no beam-plasma interaction, idealised B-field, etc.)
Future improved Particle Tracking & Magnetohydrodynamic Simulations
Sources:	1) J.W. Wang. POSITRON INJECTOR ACCELERATOR AND RF SYSTEM FOR THE ILC*. 2007.
2) F Dietrich. Status of the undulator-based ILC positron source. 2019.
Optical
Matching
Device (OMD)
Target
*Plasma Lens optimizations
Only with 1st SWT
*

---
Summary
Theoretical advantages of PLs over conventional OMDs
in Dephasing, Chromaticity & Target eddy currents
PL with ~50% more e+ yield over ILC’s currently proposed OMD
Stability of e+ yield within ±2% for single parameter deviations of ±10%
grant from July ‘21 to June ‘24 to build prototype plasma lens
ILCX2021

---
Thank you for your attention!
LCWS2021

---
Back-up Slides

---
Motivation -
Plasma Lens for Optical Matching
Motivation:
To achieve a twothousandfold increase in luminosity from the SLC (3e30 cm-2s-1) to the proposed ILC (7500e30 cm-2s-1), it is necessary to push all technological boundaries. One area of improvement in particular is the particle number, which is primarily determined by the capture section and specifically by its optical matching device.
This is where the application of a plasma lens could potentially open up new possibilities
*
*Plasma Lens optimizations
Only with 1st SWT
Sources:	1) J.W. Wang. POSITRON INJECTOR ACCELERATOR AND RF SYSTEM FOR THE ILC*. 2007.
2) F Dietrich. Status of the undulator-based ILC positron source. 2019.
Optical
Matching
Device (OMD)
Target
(e+ distribution)

---
	Symbol	PITZ	Optimized / Value
PL Length	zmax	10 cm	5.9 cm
Aperture	2a	10 mm	7.6 - 33 cm
Discharge Current	I0	≤ 1 kA	3 – 9 kA
Discharge Voltage	U	≤ 3 kV	TBD
Plasma Density	ρPlasma	≤ 1016 cm-1	TBD
Current Pulse Duration	t	~ 1 µs	TBD
Current Pulse Frequency	f	1 – 10 Hz	TBD