## Slide 1: Overview on simulation implementation for the testbeam 2020
Alina – Tania Neagu
Mihai Potlog

## Slide 2: Outline
Testbeam setup:
  setup description, Lumical configuration,
  code check: geometry construction and overlaping
Data collection, .root file structure
Results
Notes: check the geometry for the studied cases impling geometry construction, checking overlaps and sensitive detector assignation;
evaluation of data retrievement in Sensitive Detector class with proper identification of geometries and correct retrieving of data;
overview the construct of ROOT analysis manager which handles the corresponding data output format

## Slide 3: Testbeam setup
LumiCal configuration:
15 sensor layers (S1 - S15) glued to tungsten absorbers (W1 – W15) ->config. A
Additional tungsten layer in front of the stack (W0) -> config. AA
Regular configuration:
Beam spot after the colimator ~5mm x 5mm
Two scintilator triggers operating in coincidence mode
5 telescope planes – 2 before and 3 after the magnet
Magnet switched OFF
LumiCal placed on movable table
Sensor components:
kapton fan-out
LumiCal sensor
high-voltage kapton
carbon fiber support
Sensor position:
only sectors R1 and R2 are equiped

## Slide 4: Testbeam setup: visualisation
Geometry construction for testbeam configurations
Lumical detector configuration A (15 sensors)
sectors R1 and R2
64 pads each
Lumical sensor components

## Slide 5
Geometry construction
Geometry construction for testbeam configurations
Derive own concrete class from G4VUserDetectorConstruction abstract base class
Implement the method Construct()
C
U
R
R
E
N
T
S
I
T
U
A
T
I
O
N
2. define shapes, logical volumes and position of the experimental hall
3. define shapes, logical volumes and position of the coverage of LumiCal – Al foil
1. construct all necessary materials

## Slide 6
Geometry construction
5. define shapes, logical volumes and placed the scintillators
4. define shapes, logical volumes
and position of the telescope
6. define shapes, logical volumes and placed the tungsten absorbers
C
U
R
R
E
N
T
S
I
T
U
A
T
I
O
N

## Slide 7
7. define shapes and logical volumes of silicon sensors with all their components starting with kapton fan-out
8. define shapes, logical volumes
and placed the silicon sensor
silicon sensors are constructed using G4PVReplica method to identify easily the pads
Geometry construction
C
U
R
R
E
N
T
S
I
T
U
A
T
I
O
N

## Slide 8
9. define assembly of an entire silicon sensor
placement of all 15 silicon sensors using MakeImprint
11. visualization of all
constructed shapes
10. define a region for sensors
in order to apply various
conditions on it
Instantiate sensitive detectors and set them to corresponding volumes
Geometry construction

## Slide 9
Overlap checking
Each one of the geometry element constructed had the option for the checking of the volume overlaps activated
silicon sensors assembly components
tungsten absorbers
Outcome of the overlap checking

## Slide 10
Geometry construction and overlap checking
Geometry construction:
rather simplist with some minor point of high interest;
geometry constructed having placed the first sensors in the (0,0,0) coordinates; all other geometries are placed with respect to this one;
telescope:
a G4Box shape;
positioned using Z axis coordinates taken from an array;
scintillators:
a G4Box shape;
each placed individually using regular G4PVPlacement class;
tungsten absorbers:
a G4Box shape;
each absorber has a different width;
construction of solid made inside a loop with the width for absorbers taken from an array;
sensors:
each layer constructed individually from kapton fan-out to carbon fiber support;
silicon sensor build using G4PVReplica which replicates the pads horizontally and the sectors vertically;
everything wrapped in an assembly;
the assembly is positioned several times using a loop and a geometry overlap checking.

## Slide 11
Data collection
at each step in a sensitive detector, the ProcessHit() method is invoked which create, fill and stores the Hit objects
Intialize() - create a hit collection at start of an event
Data are collected using Sensitive Detectors which has the goal of creating hits objects through the following virtual methods:
Initialize()
ProcessHits()
EndOfEvent()

## Slide 12
Processing hit information
Data are retrieved using EventAction:EndOfEventAction() class
get the index number of the hit collection - which is unique and don’t change during a run
retrieve the pointer to the hits collection with the GetHC() method using the collection index
loop through the entries of hits collection to access individual hits
store the output in analysis objects

## Slide 13
Output datafile
Data are collected using Sensitive Detectors which has the goal of creating hits objects through the following virtual metods:
Initialize()
ProcessHits()
EndOfEvent()
// Default settings
analysisManager->SetVerboseLevel(1);
analysisManager->SetFileName("fcal");
// Creating ntuples
if ( fEventAction ) {
analysisManager->CreateNtuple("LumicalTree", "Calorimeter data");
analysisManager->CreateNtupleIColumn("nHits"); // Id = 0
analysisManager->CreateNtupleIColumn("Plan", fEventAction->fCalPlan); // Id = 1
analysisManager->CreateNtupleIColumn("Sector", fEventAction->fCalZone); // Id = 2
analysisManager->CreateNtupleIColumn("Pad", fEventAction->fCalPad); // Id = 3
analysisManager->CreateNtupleDColumn("Energy", fEventAction->fCalEne); // Id = 4
analysisManager->CreateNtupleDColumn("pos_x", fEventAction->fCalX); // Id = 5
analysisManager->CreateNtupleDColumn("pos_y", fEventAction->fCalY); // Id = 6
analysisManager->CreateNtupleDColumn("pos_z", fEventAction->fCalZ); // Id = 7
analysisManager->CreateNtupleDColumn("px", fEventAction->fCalPx); // Id = 8
analysisManager->CreateNtupleDColumn("py", fEventAction->fCalPy); // Id = 9
analysisManager->CreateNtupleDColumn("pz", fEventAction->fCalPz); // Id = 10 2
stringstream nameformat;
G4String edname;
for(G4int k = 1; k < 16; k++){
G4String columname = "Edep";
nameformat << k;
columname += nameformat.str();
nameformat.str("");
edname = columname;
analysisManager->CreateNtupleDColumn(edname);
}
analysisManager->FinishNtuple();
Energy deposited in each plane
RunAction class
Create analysis manager, Creatie ntuples

## Slide 14: energy deposited spectrum from different X0 - config. AA
Results

## Slide 15
Results

## Slide 16: THANK YOU!

## Slide 17: Results

## Slide 18: Testbeam setup
layer | sensor | plate | Thickness [mm]
1 | - | Plansse 2 | 3.520
2 | 52 | Plansse 3 | 3.470
3 | 51 | MGS3 | 3.542
4 | 29 | Plansse 1 | 3.505
5 | 59 | Plansse 5 | 3.490
6 | 10 | MGS1 | 3.584
7 | 57 | MGS2 | 3.521
8 | Free | MGS5 | 3.645
9 | 53 | MGS6 | 3.470
10 | 60 | A2 | 3.55
11 | 64 | A8 | 3.588
12 | 42S | B24 | 3.543
13 | Old T2 | B23 | 3.543
14 | Old C3 | B12 | 3.55
15 | 61 | B17 | 3.55
16 | Old C4 | A5 | 3.538
17 | 58 | Plansse 4 | 3.474
Brand | Density | Chemical composition |  | 
 |  | W | Ni | Cu
Plansee | 18 | 95% | 3.5% (estimated) | 1.5% (estimated)
MGS | 17.7 | 93% | 5.25% | 1.75%
JINR | 18 | 95% | 3.5% (estimated) | 1.5% (estimated)

## Slide 19: Part II

## Slide 20
Suggestion 1: to apply the same bin for Edep 1 and Edep 2

## Slide 21: Suggestion 2: to simulate a configuration without the first 2 W absorber in order to studied the behavior of sensors 2 and 3
3
1
2
4
...
Conf AA
Conf aaaa

## Slide 22
Energy deposited in sensors
un-normalised

## Slide 23: Suggestion 3: to move beam in pad 27 (like in experimental data) to implement all 4 sectors to increase statistics at 50000 events

## Slide 24
energy deposited spectrum from different X0 - config. AA

## Slide 26: Suggestion 4: to plot energy deposited in each pad for each plane

## Slide 27
Still needed further investigation on energy deposition
Ghost hits at boundary mistaken as real hits;
Conclusions

## Slide 28: 3D representation of energy deposited in each plan for each sector/pad *
* For a configuration where energy deposited was collected in all 4 sectors