## Slide 1
2021/09/17
Toshiyuki OKUGI, KEK
IDT WG3 MDI meeting
Introduction of the BDS magnets for ILC

## Slide 2
Overview of BDS (Beam Delivery System)
BDS is the beamline after main linac.
BDS consists of
- beam diagnostic section.
- collimator system.
- final focus beam line.
- beam extraction line.

## Slide 3
Application to low energy (ECM=250GeV)
The field strength for ECM=250GeV is a half to ECM=500GeV.
When we only use a half of FD magnets,
the beta functions at FD magnets are decreased.
Therefore, the collimation depth can be increased.
IP
ECM=250GeV
QD0A
QD0B
QF1A
QF1B
ECM=500GeV
0.5
1.1m
0.5
1.1m
0.5
1.1m
Beta
ECM=250GeV
ECM=500GeV
Half length of FD was used.
Full length of FD was used.
The geometry optimizes the more difficult low-energy optics
and allows the higher-energy optics to deviate slightly from the optimum value.

## Slide 4
Cryomodule of Final Doublet and Extraction Quads
We will use the 2 set of cryomodules for ILC IP region.
Supported
with Detector
Supported to
Accelerator Tunnel
We can split the QD0 magnet
to be half length of magnets
(to be explained for low energy operation)

## Slide 5
ECM=250GeV
ECM=350GeV
ECM=500GeV
Horizontal
Profile
Vertical
Profile
ECM=250GeV
ECM=350GeV
ECM=500GeV
IP beam profile
ECM | Horizontal |  | Vertical |  | Relative Luminosity
 | design beam size | simulation (core) | design beam size | simulation (core) | 
250GeV | 0.729um | 0.755um | 7.66nm | 7.81nm | 94.7%
350GeV | 0.683um | 0.690um | 5.89nm | 5.97nm | 97.8%
500GeV | 0.474um | 0.482um | 5.86nm | 5.89nm | 97.8%
Simulation Results for ECM<500GeV optics ( no SR )

## Slide 6
( not include the dumpline )
 | Energy [GeV] | # of BEND | # of QUAD | # of SEXT | # of Steer | # of PS | # of Mover | # of BPM
Section A | 500 | 16 | 64 | 0 | 19 | 73 | 70 | 78
 | 1000 | 43 | 108 | 0 | 19 | 115 | 108 | 116
Section B | 500 | 63 | 33 | 7 | 55 | 46 | 40 | 101
 | 1000 | 176 | 41 | 7 | 55 | 56 | 48 | 112
Section A
to betatron collimator
Section B
from Energy Collimator
The number of components both for ECM=500GeV and ECM=1TeV
Application to high energy (ECM=1TeV)
The beam optics is designed to be expandable to ECM=1TeV in the same tunnel.
Beam optics up to 500 GeV can be used with electromagnets to support beam optics up to 1 TeV.
When ECM=1TeV, the Final Doublet strength must be twice as strong as when ECM=250-500GeV. What technology will be used for this purpose has not been decided at present.

## Slide 7
 | Horizontal |  |  | Vertical |  |  | Relative Luminosity
 | design | rms | core | design | rms | core | 
no SR | 0.481um | 0.481um | 0.481um | 2.99nm | 2.99nm | 2.99nm | 99.8%
with SR |  | 0.499um | 0.498um |  | 3.71nm | 3.15nm | 91.7%
<< no SR >>
Simulation Results for ECM=1TeV optics
<< with SR >>
Aberrations due to synchrotron radiation
Luminosity of more than 90% can be achieved for ECM=1TeV, even with the effect of synchrotron radiation on the beamline.

## Slide 8
Beta Function at SP2/SP4 = (X; 1000m / Y; 1000m)
Phase Advance (SP2/SP4) = (X; 0.5 pi / Y; 1.5 pi )
Phase Advance (SP4/ IP ) = (X; 5.5 pi / Y; 4.5 pi )
EtaX at SPEX = 0.158m
FD phase
collimation
IP phase
collimation
Energy
collimation
Arrangement of the Collimators
QF1
20 f
QD0
20 f
IP
28 f
QDEX1
30 f
Detector apertures
Source for background
Halo particles
SR form halo particles
Consideration of collimation depth
SP2/SP4 X ; 0.86mm
SP2/SP4 Y ; 0.98mm
SPEX X ; 1.60mm
( Dp/p = 1% )
30f
When the L* of QD0 is increased, the L* of QDEX1 in the extraction line must also be increased.
Since the collimation depth is limited mainly by the fact that SR from the Final Doublet hits QDEX1, the collimation depth becomes more severe when L* is increased.

## Slide 9
Horizontal limit
Shorter QD0 L*
Longer QD0 L*
Horizontal limit
The situation of QDEX1 limit
will be changed by the parameters
- the location of QDEX1.
- the aperture of QDEX1.
- the vertical aperture of collimator.
Synchrotron radiation around IP area
QF1
QD0
IP
QDEX1

## Slide 11
Apertures for Dumpline
ILC beam extraction line
Quadrupole magnets in extraction line
First two quadrupoles : SC magnets in FD package
Other quadrupoles : Large aperture NC magnets
Disrupted charged particles
Beamstrahlung photons
Power loss at extraction line (beam-beam effect)
E. Marin and Y. Nosochkov et al., LCWS 2013
Y. Nosochkov et al., LCWS/ILC 2007
The ILC extraction line uses large-diameter quadrupole magnets (maximum bore diameter 170 mm) to transport the beam with large beam spread by the beam-beam effect to the dump with minimal loss.
When the L* of QD0 is lengthened, the L* of the extraction quadrupole magnet QDEX1 is also lengthened, and the diameter of the quadrupole magnet in the entire extraction line should be increased more.
Therefore, the design of the entire extraction line needs to be redesigned.

## Slide 12
ILC extraction line beam diagnostics
Beam diagnostics for ILC beam extraction line
Cross section of Compton scattering
with different beam polarization

## Slide 13
IP beam size tuning
Sigma < 1um
presented by T.Tauchi (KEK) at AWLC2014
For small beam size
( smaller than 1 um)
The beam size will be optimized by monitoring the Luminosity monitor in actual ILC beam operation.
Sigma > 1um
For large beam size
( larger than 1 um)

## Slide 14
Backup

## Slide 15
Is it better to take the bending angle of the dipole magnet infinitely large?
The higher-order aberration derived energy spread becomes stronger.
The larger the emittance dilution due to synchrotron radiation become larger for the high energy beam.
There is an optimum value of bending angle for each beam energy.
I have considered the ILC final focus optics with long L* in the past.
Large L* optics for ILC
Toshiyuki OKUGI, KEK
2014/ 5/ 15
AWLC2014, Fermilab

## Slide 16
Long L* and Chromaticity
In order to squeeze the beam to the same size at the focus, it is necessary to squeeze the beam at the same divergence angle.
The beam size at the final focus magnet becomes larger.
The chromatic aberration at the focal point becomes larger.
When the L* is long, the chromatic aberration becomes larger, and a strong chromatic aberration compensation is needed.
The difference in particle trajectory is created by the difference in energy.
The strength of the sextupole magnet depends on the position of the particle passing through it.
The angle at which a particle injects a quadrupole magnet depends on its energy.
Chromaticity correction
Small difference in position
due to energy in sextupole
Large difference in position
due to energy in sextupole
Requires strong sextupoles
Spatial aberration becomes large
Enough to use weak sextupoles
Spatial aberrations are small.
This is especially effective in “the low energy region”, because the beam size passing through the magnet is large.

## Slide 17
Since the (2nd order and higher) geometrical aberration for large L* optics was large
the large L* optics is more difficult than the small L* optics, even if we set same chromaticity.
L*=7.0m optics based on ILC RDR optics (ECM=500GeV)
In order to reduce the beam size at SF6, SF5 and SD4,
the beta function at the section was reduced
(ATF2-like optimization).
1st step optimization
2nd step optimization
The strength of dipole magnet was increased to twice to increase the dispersion and reduce the strength of sextupoles.

## Slide 18
Bandwidth of sigmaX for E=250GeV
Bandwidth of sigmaY for E=250GeV
Luminosity Bandwidth for E=250GeV
Energy Dependence of Luminosity
Performances for the optics with strong bending magnet
The luminosity was increased to almost 97%, and the bandwidth increased.
But, the luminosity reduction for low energy was still large.
Optics was matched to ILC TDR parameters.
sp/p = 0.12%
sp/p = 0.12%
sp/p = 0.12%
sp/p = 0.12%
IP Beam Size at E=250GeV | sigmaX* | sigmaY*
w/o Synchrotron Radiation | 0.50um | 5.81nm
with Synchrotron Radiation | 0.50um | 5.95nm
Effect of SR
Even at ECM=500 GeV,
some effects of synchrotron radiation are appeared.
At AWLC2014, this proposal was rejected.
The reasons are
Energy extendability
Collimation depth
Aperture of the dumpline .

## Slide 19
The current ILC FF optics are designed to support energies of ECM=250GeV-1TeV with the same geometry.
However, the FF optics is not optimized for each energy, because the bending angle of the dipole magnet does not have an optimum angle for each energy.
In order to optimize for each energy, we need to choose optimal bending angle of dipole for each beam energy.
A layout to optimize for two energies, ECM=250GeV and 1TeV, was proposed in 2017.

## Slide 20
Horizontal beamline offset
is shifted by 1m at 2xB0.
Original beam optics
Beam optics with strong bending magnet
 | Collimator | FF beamline | Total
B = 1.0 x B0 | 0.0058% | 0.0017% | 0.0061%
B = 1.5 x B0 | 0.0059% | 0.0020% | 0.0062%
B = 2.0 x B0 | 0.0060% | 0.0024% | 0.0064%
 | Collimator | FF beamline | Total
B = 1.0 x B0 | 0.45% | 0.07% | 0.52%
B = 1.5 x B0 | 0.67% | 0.49% | 1.16%
B = 2.0 x B0 | 1.49% | 2.06% | 3.55%
Momentum Spread Growth by Synchrotron Radiation
Horizontal Emittance Growth by Synchrotron Radiation
Synchrotron radiation for BDS at ECM=500GeV
IP beam profile at ECM=250GeV
Even at ECM=500 GeV, the effect of SR is not so small (1 TeV is impossible).
Strong dipole for low energy

## Slide 21
Add horizontal bend at BDS entrance.
When we upgrade the energy to ECM=1TeV, we will align the IP position and angle of the two beamlines by adjusting the angle of this horizontal bend and the energy collimator.
This beam optics improves the performance of ECM=250 GeV, and has the expendability up to ECM=1 TeV.
This was proposed in 2017, but was rejected because of the slightly longer beamline (cost).
ECM=500GeV
ECM=1TeV
Upstream beamline
Entire beamline
Beam kick
at horizontal bend
Small kick angle
for energy collimator
Upstream beamline
Entire beamline
New beamline layout to allow ECM=250GeV to 1TeV

## Slide 22
X
Y
No Errors
No Errors
Geometrical Aberration
SR Aberration
Optimization of bending angle for ECM=1TeV
Original
Optimum
Optimum bending angle is 70% of original.
( balanced geometrical aberration and SR aberration )