## Slide 1
2021/09/29
Toshiyuki OKUGI, KEK
IDT WG2 DR/BDS/DUMP group meeting
Present ILC FF optics

## Slide 2
Basic ILC FFS optics design

## Slide 3
2 sextupoles are put to the following condition.
Only chromaticities are generated as total system.
Sext-1
Sext-2
Sext-1
Sext-2
Total
Chromaticity
Vertical
Chromaticity
Correction
Horizontal
Chromaticity
Correction
Final Doublet
Global Chromaticity Correction System
Linear collider FFS optics in 1990’s

## Slide 4
Final Focus Test Beam (FFTB)
FFTB is built in SLC research yard (SLAC) for the LC final focus test
with global chromticity correction system in 1990’s.
 | IP beam size
Design | 45 nm
Achieved | 70 nm
Shintake Monitor

## Slide 5
Sext-2
Sext-1
Sext-2
Sext-1
Total
Geonetrical aberration
was cancelled.
Chromaticity
2nd order dispersion
P. Raimondi and A. Seryi, PRL Vol. 86 3779 (2001)
 | X chromaticity | Y chrotaticity | 2nd order dispersion
Linear Optics | ○ | ○ | ○
X chromaticity corr. | ○ | △ (small) | ○
Y chromaticity corr. | △ (small) | ○ | ○
Local Chromaticity Correction System
When chroticity correction knobs (sextupoles) are changed.
=> 2nd order dispersion is changed. (linear optics and sextupoles are coupled.)
=> Liniear optics must be changed.

## Slide 6
Vertical Correction
Horizontal Correction
Local Chromaticity Correction
Global Chromaticity Correction
Horizontal Correction
Vertical Correction
The beamline length is shorter than that for the global chromaticity correction system
Orbit distortion through long beamline of off-momentum particle exists for global chromaticity correction beamline.
  Longer L*
  Smaller background by the halo particles
  Wider energy bandwidth
Advantage of local chromaticity correction optics
IP Energy Bandwidth
Beam Halo at IP
P. Raimondi and A. Seryi, PRL Vol. 86 3779 (2001)

## Slide 7
Present ILC Final Focus Optics
We adopted the modified Local Chromaticity Correction Optics.
3 parameters to be corrected
- X Chromaticity
- Y Chromaticity
- 2nd order Dispersion
2 sext. pair for correction
- SF6, SF5 (combination) and SF1
- SD4 and SD0
We can correct 2nd order aberration
- only with sextupole magnet.
- without linear optics change.
Different dispersion
Name | X | Y
QD10B | -131.9 | 757.6
QD10A | -168.7 | 673.4
QF9B | 437.4 | -377.5
SF6 | 0.0 | 0.0
QF9A | 460.6 | -295.4
QD8 | -45.0 | 379.0
QF7B | 0.2 | -1.2
QF7A | 0.2 | -1.2
QD6 | -45.0 | 379.0
QF5B | 460.9 | -295.6
SF5 | 155.6 | -112.9
QF5A | 437.6 | -377.8
QD4B | -162.6 | 650.6
SD4 | 1238.1 | -6089.7
QD4A | -126.0 | 736.6
QD2B | 0.0 | -3.9
QF3 | 5.8 | -7.5
QD2A | -13.7 | 0.1
SF1 | -9095.3 | 4954.9
QF1 | 4830.8 | -2934.4
SD0 | 2497.5 | -12835.6
QD0 | -1002.9 | 14564.7
Total | -266.5 | -236.9
Chromaticities of quad/sext in ILC FF beamline
The chromaticities are generated not only Final Doublet, but also other quadrupoles.
The chromaticities are corrected by sextupole magnets within the Final Focus Beamline.
The large chromaticities are generated by sextupole near by Final Doublet. ( Not perfect local correction )

## Slide 8
Octupoles were used only for tail folding in the present ILC FFS design.
When the octupoles will be used for the IP beam focusing,
  we should take care of the effect of the collimation depth and the detector background by the halo particles.

## Slide 9
Beam Optics of ILC & ATF2
- ILC final focus systemand ATF2 beamline are both based on the Local Chromaticity Correction.
1x1 optics
X&Y chromaticities are comparable to ILC FF.
10x1 optics
Since betax* is 10 times larger than 1x1 optics, X chromaticity is one order smaller than ILC .
ATF2 Beam Optics
ILC final Focus System
Same magnet arrangement
Same tuning concept
Comparable magnet tolerances
Tolerances of FD multipole field error
to IP vertical beam size

## Slide 10
L* of the present ILC FFS

## Slide 11
Push-pull scheme of the ILC detectors
QF1 package is common for both detectors, and located in the accelerator tunnel.
QD0 package is independent for each detector.
L* (3.5m and 4.5m) for each detector is different, and the beam optics are not optimized for the L*s in the TDR.

## Slide 12
Effect of (QD0 L*) to Luminosity
ECM = 250GeV
beta* (x/y) = 13mm / 0.41mm
(QD0 L*) = variable
(QF1 L*) = 9.5m
Results of m Tuning Simulation
Effect of (QF1 L*) to Luminosity
ECM = 250GeV
beta* (x/y) = 13mm / 0.41mm
(QD0 L*) = 4.1m
(QF1 L*) = variable
Results of m Tuning Simulation
Horizontal collimation depth
Optimum QD0/QF1 L*s were discussed in 2014-2015,
and the present L*s were fixed by taking account of the luminosity and collimation depth.
SiD and ILD use same L* optics.
Since QF1 magnet is common, the optimum of QD0 L* is also same.
Present ILC L*

## Slide 13
Beta Function at SP2/SP4 = (X; 1000m / Y; 1000m)
Phase Advance (SP2/SP4) = (X; 0.5 pi / Y; 1.5 pi )
Phase Advance (SP4/ IP ) = (X; 5.5 pi / Y; 4.5 pi )
EtaX at SPEX = 0.158m
FD phase
collimation
IP phase
collimation
Energy
collimation
Arrangement of the Collimators
QF1
20 f
QD0
20 f
IP
28 f
QDEX1
30 f
Detector apertures
Source for background
Halo particles
SR form halo particles
Consideration of collimation depth
SP2/SP4 X ; 0.86mm
SP2/SP4 Y ; 0.98mm
SPEX X ; 1.60mm
( Dp/p = 1% )
30f
When the L* of QD0 is increased, the L* of QDEX1 in the extraction line must also be increased.
Since the collimation depth is limited mainly by the fact that SR from the Final Doublet hits QDEX1, the collimation depth becomes more severe when L* is increased.

## Slide 14
Application to low energy (ECM=250GeV)
The field strength for ECM=250GeV is a half to ECM=500GeV.
When we only use a half of FD magnets,
the beta functions at FD magnets are decreased.
Therefore, the collimation depth can be increased.
IP
ECM=250GeV
QD0A
QD0B
QF1A
QF1B
ECM=500GeV
0.5
1.1m
0.5
1.1m
0.5
1.1m
Beta
ECM=250GeV
ECM=500GeV
Half length of FD was used.
Full length of FD was used.
The geometry optimizes the more difficult low-energy optics
and allows the higher-energy optics to deviate slightly from the optimum value.

## Slide 15
ECM=250GeV
ECM=350GeV
ECM=500GeV
Horizontal
Profile
Vertical
Profile
ECM=250GeV
ECM=350GeV
ECM=500GeV
IP beam profile
ECM | Horizontal |  | Vertical |  | Relative Luminosity
 | design beam size | simulation (core) | design beam size | simulation (core) | 
250GeV | 0.729um | 0.755um | 7.66nm | 7.81nm | 94.7%
350GeV | 0.683um | 0.690um | 5.89nm | 5.97nm | 97.8%
500GeV | 0.474um | 0.482um | 5.86nm | 5.89nm | 97.8%
Simulation Results for ECM<500GeV optics ( no SR )

## Slide 16
( not include the dumpline )
 | Energy [GeV] | # of BEND | # of QUAD | # of SEXT | # of Steer | # of PS | # of Mover | # of BPM
Section A | 500 | 16 | 64 | 0 | 19 | 73 | 70 | 78
 | 1000 | 43 | 108 | 0 | 19 | 115 | 108 | 116
Section B | 500 | 63 | 33 | 7 | 55 | 46 | 40 | 101
 | 1000 | 176 | 41 | 7 | 55 | 56 | 48 | 112
Section A
to betatron collimator
Section B
from Energy Collimator
The number of components both for ECM=500GeV and ECM=1TeV
Application to high energy (ECM=1TeV)
The beam optics is designed to be expandable to ECM=1TeV in the same tunnel.
Beam optics up to 500 GeV can be used with electromagnets to support beam optics up to 1 TeV.

## Slide 17
 | Horizontal |  |  | Vertical |  |  | Relative Luminosity
 | design | rms | core | design | rms | core | 
no SR | 0.481um | 0.481um | 0.481um | 2.99nm | 2.99nm | 2.99nm | 99.8%
with SR |  | 0.499um | 0.498um |  | 3.71nm | 3.15nm | 91.7%
<< no SR >>
Simulation Results for ECM=1TeV optics
<< with SR >>
Aberrations due to synchrotron radiation
Luminosity of more than 90% can be achieved for ECM=1TeV, even with the effect of synchrotron radiation on the beamline.

## Slide 18
Longer L*

## Slide 19
L* issue will be discussed
at WG3 MDI group mtg.
2021/03/16
The longer L* issue was discussed in LCWS2021.
IDT WG3 MDI group meeting

## Slide 20
QD0 can be supported from the BDS tunnel
  We can get rid of QD0 pillar if L*=6m
  QD0 may have to be retractable like QSC of SuperKEKB
  Much more stable than the support from the pillar on the platform
  Much better position repeatability after push-pull
    Pillar on the platform: ~0.5mm
    Support from BDS tunnel: few tens of um (SuperKEKB)
  Much faster machine tuning after push-pull
  Only one pair of QD0 is necessary (2 pairs for ILD and SiD are necessary for TDR design)
ILD needs some modification
  Cut the End-cap iron to make access to flanges at Z~6m possible, and/or remote vacuum connection (RVC) like SuperKEKB
  FCAL support has to be re-considered (telescopic support?)
  No need for split endcap
BeamCAL can be placed far from IP
  Weaker magnetic field at BCAL (and QD0 front surface) causes less back-scattering of pair background
  No need for AntiDID (?)
  Less cost, less construction period, and less risk
Possible benefit of longer L* for detectors
Discussion of the longer L* in WG3 MDI group
by Y. Sugimoto @IDT-WG3-MDI-Phys kickoff meeting

## Slide 21
Comment; L* and luminosity
The horizontal beam size was defined with beamstrahlung parameter
The vertical beta function is roughly optimized to the bunch length
to minimize the hour-glass effect as
Then, the luminosity can be expressed as
Luminosity
In order to increased the luminosity,
Make small vertical emittance
Make beamstrahlung parameter large.
⇒ make the balance of the luminosity
and energy spread for collision beam.
Beam energy reduction by beamstrahlung
For ILC 500GeV, the
L* is not directly related to the design luminosity in linear colliders.
However, it may effectively lead to a decrease the integrated luminosity for ILC
through various tolerances and the associated beam tuning etc.

## Slide 22
Some issues for large L* optics
In order to change the L*, it is necessary to change not only the arrangement of the magnets near the IP but also the entire FFS optics including the beamline length.
When increasing L*, the acceptable range of the optimum bending angle for the beam energy becomes smaller, which may limit the future energy extendability (see later).
We should reevaluate the effect of the collimation depth and detector background (may be worse than present optics).
We may reevaluate the beam extraction line optics.
However, since the accelerator is a tool for conducting physics experiments, I believe that it is necessary to change the L* if it is required by the consensus of physics.
I have heard that there is no consensus on the physics side that L* should be changed at this time, so the accelerator side is not about to start considering it, and this presentation is nothing more than information sharing.

## Slide 23
Horizontal limit
Shorter QD0 L*
Longer QD0 L*
Horizontal limit
The situation of QDEX1 limit
will be changed by the parameters
- the location of QDEX1.
- the aperture of QDEX1.
- the vertical aperture of collimator.
Synchrotron radiation around IP area
QF1
QD0
IP
QDEX1
When L* is increased, the effect of SR from the Final doublet on the SC magnet in the extraction line becomes larger and the collimation depth is reduced.

## Slide 24
Apertures for Dumpline
ILC beam extraction line
Quadrupole magnets in extraction line
First two quadrupoles : SC magnets in FD package
Other quadrupoles : Large aperture NC magnets
Disrupted charged particles
Beamstrahlung photons
Power loss at extraction line (beam-beam effect)
E. Marin and Y. Nosochkov et al., LCWS 2013
Y. Nosochkov et al., LCWS/ILC 2007
The ILC extraction line uses large-diameter quadrupole magnets (maximum bore diameter 170 mm) to transport the beam with large beam spread by the beam-beam effect to the dump with minimal loss.
When the L* of QD0 is lengthened, the L* of the extraction quadrupole magnet QDEX1 is also lengthened, and the diameter of the quadrupole magnet in the entire extraction line may be increased more.
Therefore, the design of the entire extraction line needs to be redesigned.

## Slide 25
I have considered the ILC final focus optics with long L* in the past.
Large L* optics for ILC
Toshiyuki OKUGI, KEK
2014/ 5/ 15
AWLC2014, Fermilab

## Slide 26
Long L* and Chromaticity
In order to squeeze the beam to the same size at the focus, it is necessary to squeeze the beam at the same divergence angle.
The beam size at the final focus magnet becomes larger.
The chromatic aberration at the focal point becomes larger.
When the L* is long, the chromatic aberration becomes larger, and a strong chromatic aberration compensation is needed.
The difference in particle trajectory is created by the difference in energy.
The strength of the sextupole magnet depends on the position of the particle passing through it.
The angle at which a particle injects a quadrupole magnet depends on its energy.
Chromaticity correction
Small difference in position
due to energy in sextupole
Large difference in position
due to energy in sextupole
Requires strong sextupoles
Spatial aberration becomes large
Enough to use weak sextupoles
Spatial aberrations are small.
This is especially effective in “the low energy region”, because the beam size passing through the magnet is large.

## Slide 27
Since the (2nd order and higher) geometrical aberration for large L* optics was large
the large L* optics is more difficult than the small L* optics, even if we set same chromaticity.
L*=7.0m optics based on ILC RDR optics (ECM=500GeV)
In order to reduce the beam size at SF6, SF5 and SD4,
the beta function at the section was reduced
(ATF2-like optimization).
1st step optimization
2nd step optimization
The strength of dipole magnet was increased to twice to increase the dispersion and reduce the strength of sextupoles.

## Slide 28
Bandwidth of sigmaX for E=250GeV
Bandwidth of sigmaY for E=250GeV
Luminosity Bandwidth for E=250GeV
Energy Dependence of Luminosity
Performances for the optics with strong bending magnet
The luminosity was increased to almost 97%, and the bandwidth increased.
But, the luminosity reduction for low energy was still large.
Optics was matched to ILC TDR parameters.
sp/p = 0.12%
sp/p = 0.12%
sp/p = 0.12%
sp/p = 0.12%
IP Beam Size at E=250GeV | sigmaX* | sigmaY*
w/o Synchrotron Radiation | 0.50um | 5.81nm
with Synchrotron Radiation | 0.50um | 5.95nm
Effect of SR
Even at ECM=500 GeV,
some effects of synchrotron radiation are appeared.
At AWLC2014, this proposal was rejected.
The reasons are
Energy extendability
Collimation depth
Aperture of the dumpline .

## Slide 30
The additional sextupoles were put to the original chromaticity correction optics. They also use octupoles for IP focusing.
Since CLIC is designed to have weaker nonlinear effects than ILC, such as smaller horizontal emittance and higher energy, it will be necessary to examine carefully when matching the parameters of ILC.
The effect on the detector background and collimation depth when using octupole magnets for beam adjustment needs to be carefully examined.
The aperture of the inner detector around the IP is assumed to be very wider than ILC.
L*=6m optics for CLIC 380GeV

## Slide 31
Other topics

## Slide 32
The current ILC FF optics are designed to support energies of ECM=250GeV-1TeV with the same geometry.
However, the FF optics is not optimized for each energy, because the bending angle of the dipole magnet does not have an optimum angle for each energy.
In order to optimize for each energy, we need to choose optimal bending angle of dipole for each beam energy.
A layout to optimize for two energies, ECM=250GeV and 1TeV, was proposed in 2017.

## Slide 33
Horizontal beamline offset
is shifted by 1m at 2xB0.
Original beam optics
Beam optics with strong bending magnet
 | Collimator | FF beamline | Total
B = 1.0 x B0 | 0.0058% | 0.0017% | 0.0061%
B = 1.5 x B0 | 0.0059% | 0.0020% | 0.0062%
B = 2.0 x B0 | 0.0060% | 0.0024% | 0.0064%
 | Collimator | FF beamline | Total
B = 1.0 x B0 | 0.45% | 0.07% | 0.52%
B = 1.5 x B0 | 0.67% | 0.49% | 1.16%
B = 2.0 x B0 | 1.49% | 2.06% | 3.55%
Momentum Spread Growth by Synchrotron Radiation
Horizontal Emittance Growth by Synchrotron Radiation
Synchrotron radiation for BDS at ECM=500GeV
IP beam profile at ECM=250GeV
Even at ECM=500 GeV, the effect of SR is not so small (1 TeV is impossible).
Strong dipole for low energy

## Slide 34
IP
PM-8
PM+8
3.2km
2.3km
Design of vertical bead at entrance of BDS
BDS tunnel is laser straight.
No vertical bend in optics deck
( 0.432mrad )
Simple vertical bend (+87.5m)
BDS beamline will be longer,
when we put the vertical bend.
The vertical bending section was designed in between MPS and skew quadrupole section.
The optics was designed to smoothly connected to FODO cell of skew quadrupole section.
The vertical emittance growth, generated by the bending system is less than 1%.

## Slide 35
Add horizontal bend at BDS entrance.
When we upgrade the energy to ECM=1TeV, we will align the IP position and angle of the two beamlines by adjusting the angle of this horizontal bend and the energy collimator.
This beam optics improves the performance of ECM=250 GeV, and has the expendability up to ECM=1 TeV.
This was proposed in 2017, but was rejected because of the slightly longer beamline (cost).
ECM=500GeV
ECM=1TeV
Upstream beamline
Entire beamline
Beam kick
at horizontal bend
Small kick angle
for energy collimator
Upstream beamline
Entire beamline
New beamline layout to allow ECM=250GeV to 1TeV

## Slide 36
X
Y
No Errors
No Errors
Geometrical Aberration
SR Aberration
Optimization of bending angle for ECM=1TeV
Original
Optimum
Optimum bending angle is 70% of original.
( balanced geometrical aberration and SR aberration )

## Slide 37
Summary
The current FF optics of the ILC is designed to cover ECM=250 GeV to 1 TeV with the same geometry. However, they are not optimized for all energies.
The present QD0/QF1 L* was determined by communicating with SiD and ILC groups in 2014-2015.
There are L*=6m optics for CLIC 380GeV. But, we have not yet evaluated the optics is fit to the ILC FF optics.
Long L* optics for ILC was proposed in 2014, but it was rejected for the following reasons.
  Energy extendability
  Collimation depth .
  Aperture of the dumpline
If we will consider for the adoption, a comprehensive design must be developed to meet these conditions (especially for 2 and 3, which have a significant impact on the entire accelerator system).
In order to optimize for each energy, we need to choose optimal bending angle of dipole for each beam energy. A layout to optimize for two energies, ECM=250GeV and 1TeV, was proposed in 2017.
When we prioritize the optimization of FFS at ECM=250GeV, we should consider it again (just my opinion).

## Slide 38
Backup

## Slide 39
ILC extraction line beam diagnostics
Beam diagnostics for ILC beam extraction line
Cross section of Compton scattering
with different beam polarization