LCIO RawCalorimeterHit discussion
AHCAL (SPIROC + KLauS) subsystem usage
Jiri Kvasnicka
16.11.2021

---
Stored information – SPIROC
- SPIROC designed for short spill (~1-16 ms) operation with
  acquisition, conversion and “slow” readout phase
- SPIROC packet:
  - ChipID (8bits)
  - List of BXIDs (16 bits each, 1~16 memory cells)
  - 36 * ADC (12 bits +gain bit +hit bit) * memory cells
  - 36 * TDC (12 bits +gain bit +hit bit) * memory cells
- DIF:
  - DIF_ID (16 bits)
  - ASIC readout chain, ASIC Index
- LDA:
  - Readout Cycle number
  - LDA number, Port number
- LDA separate stream:
  - Timestamps (start, stop, trigger)
  - Trigger number (counting or fetched from TLU)
aggregation

---
LCIO events
- Different event building (in Eudaq) → different LCIO:
  - Complete readout cycle,
  - same BXID,
  - triggered BXID
- Collections:
  - EUDAQDataLDATS
    - Timestamps (25 ns bins): Acq start (64 bits), stop (64 bits), triggers (64bits each)
  - EUDAQDataScCAL – array(s) of integers (32 bits)
    - i:CycleNr – cycle number
    - i:BunchXID – BXID (12 or 16 bits)
    - i:EvtNr – memory cell (essential for calibration)
    - i:ChipID – defined by slowcontrol for each SPIROC (8bits) + (DIF_ID << 8)
    - i:Nchannels – number of channels – used to get the following arrays
    - i:TDC14bit[NC]
    - i:ADC14bits[NC]
  - TempSensor, SlowControl, LEDinfo, HVAdjInfo, ASICStopData
DAQquality parameter of the collection – indicates a “good” and complete event

---
Stored information - KLauS
- Two operation mode: “spilled/pulsed” and continuous
- Up to 700 individual hits buffered stored – single channel only (unlike SPIROC, which fills complete SCA row with 36 channels)
- KLauS (DIF) readout packet:
  - Chip ID
  - Up to 700 KLauS hits
- KLauS hit information (6 bytes packets) from one ASIC
  - Channel ID – 36 channels
  - ADC – 12 bits, converted on the fly
  - TDC – digital clock counter from the start. 16++ bits (more for KLauS6)
  - Gain selection flags
- Data is readout via I2C – shared readout bus for all asics
- Spilled mode: hits accepted only during acquisition window, ASICs readout at the end
  - –> BXID is only a reconstructed information from TDC using a fixed offset to SPIROC’s BXID0
- Continuous mode: hits read out continuously
  - TDC counter is continuously counting (and overrunning)

---
Additional LCIO parameters
- Timestamp [ns] – unixtime, rounded to nearest second
- DaqErrorStatus
- TimestampBegin, TimestampEnd – meaning depends on event building
  - Start + stop of readout cycle, or
  - Start + stop of a BXID, or
  - Trigger timestamp
- TriggerNumber – when building triggered events