## Slide 1: WG2 SRF: WP3 Crab Cavities Design Review Workshop #3 – 21/10/22
Peter McIntosh
UKRI-STFC Daresbury Laboratory
1st November 2022

## Slide 2: Agenda for WP3 Design Review #3 (GMT)
Friday 21st October 2022 | Friday 21st October 2022 |  | 
13:30 | Introduction and Remit for the Workshop | Peter McIntosh (STFC) | 5 min
13:35 | Specification Review | Peter McIntosh (STFC) | 15 min
Cavity Design Updates |  |  | 
13:50 | Elliptical/Racetrack | Graeme Burt (Lancaster University) | 15 + 5 min
14:10 | RF Dipole (RFD) | Suba De Silva/Jean Delayen (ODU/JLab) | 15 + 5 min
14:30 | Double Quarter Wave (DQW) | Silvia Verdu Andres (CERN) | 15 + 5 min
14:50 | Wide Open Waveguide (WOW) | Binping Xiao (BNL) | 15 + 5 min
15:10 | Quasi-waveguide Multicell Resonator (QMiR) | Andrei Lunin (FNAL) | 15 + 5 min
15:30 | Next Stage CC Preparations | Peter McIntosh (STFC)/K Yamamoto (KEK)/A Yamamoto (KEK) | 30 min
16:00 | Meeting close |  | 

## Slide 3: Scope Design Review #3
Assess and compare CC EM designs, not likely finally optimised:
  Cavity,
  HOMs,
  Couplers,
  Multipacting,
  Tuning.
Clarifying next steps to ‘head towards’ a down-selection process:
  All EM design aspects complete, including pressure stability and fabrication assessment.
  Down-select 2 optimum CC designs for future prototype development (external review).
Final CC down-selection, post-prototype validation at ~18-months later.
As proposed at Design Review #1 – Dec 21

## Slide 4: Specifications Update (v14)
A Yamamoto/T Okugi – 19/7
Further clarify longitudinal impedance specification – Both Short/Long-range

## Slide 5: Elliptical/Racetrack 3.9 GHz G Burt (Lancaster U)
25 mm central beam-pipe, with 30 mm for end-cells to aid HOM damping.
Expect to achieve 9.7 MV/m at 80 mT with Rt/Q=132 Ohms.
250 GeV ILC requires 1 x 3-cell cavity @ 5 MV/m to achieve 0.615 MV.
1 TeV ILC requires 4 x 3 cells @ 5.5 MV/m to achieve 2.5 MV.
Multipactor limit identified @ 7.15 MV/m (narrowband) on minor axis iris.
Transverse Impedance
Trapped Mode extraction using on-cell waveguide extraction

## Slide 6: Elliptical/Racetrack 3.9 GHz G Burt (Lancaster U)
A 2-cell cavity has no trapped modes - on-cell damping is therefore not required – simpler to manufacture:
  Expect an increase in both LOM and SOM Qe.
Would change the ILC application expectations:
  250 GeV – 2 x 2-cell cavities @ 4.2 MV/m
  1 TeV – 5 x 2-cell cavities @ 6.5 MV/m

## Slide 7: RF Dipole 1.3 GHz S De Silva/J Delayen (Jlab/ODU)
Machined from Nb ingots, 2.5 mm thick walls - ~ 40 kg Nb material

## Slide 8: RF Dipole 1.3 GHz S De Silva/J Delayen (Jlab/ODU)
Impedance threshold/cavity:
Zx= 8.13 MΩ/m & Zy= 10.28 MΩ/m (6 cav).
Well damped HOMs (with margin).
For 1 TeV – cryomodule to fit within 3.8 m:
6 cavities for single CM.
Incl 2nd exhaust 20 mm beam pipe.
Total achievable – 8.1 MV (1.24 MV Vt per cavity).
~10% extra margin
Design concept follows JLab C100 cryomodule.

## Slide 9: Double Quarter Wave 1.3 GHz S Andres Verdu (BNL)
25 mm pole-separation, with 40 mm beam-pipe.
Both Tesla-type and waveguide HOM couplers being explored.
Qe = 1e7, with 130 Hz bandwidth and 300 W power requirement.
Various FPC options under study: Hook, Coax (cone and profiled).
ILC CC Specs v11 | 125 GeV, 10 Hz upgrade | 500 GeV
Frequency (GHz) | 1.3 | 1.3
Total (MV) | 1.86 | 7.4
Ib0 (mA) | 8.75 | 7.6
No. DQW cavities | 2 | 5
per cavity (MV) | 0.93 | 1.48
DQW (Ω, circuit) | 211 | 211
Max. offset (mm) | 0.5 | 0.5
Detuning (Hz) | 50 | 50
ILC CC Specs v11 | 125 GeV, 10 Hz upgrade | 500 GeV
 | 1.3 | 1.3
 | 1.86 | 7.4
Ib0 (mA) | 8.75 | 7.6
No. DQW cavities | 2 | 5
 | 0.93 | 1.48
 | 211 | 211
 | 0.5 | 0.5
 | 50 | 50

## Slide 10: Double Quarter Wave 1.3 GHz S Andres Verdu (BNL)
~3 orders magnitude HOM damping required.
Combination of both hook and waveguide HOM dampers anticipated.
Freq TE11 cutoff (25 mm diameter) = 7 GHz
Zx, Zy
THRESHOLD
X=hor.
Y=vert.
Promising results using single Tesla-type coupler.
CM easily fits within 3.8 m envelope.

## Slide 11: Wide Open Waveguide 1.3 GHz B Xiao (BNL)
25 mm pole-separation, with 100 mm beam-pipe.
HOM waveguides preferred to Beam Line Absorber – shorter structure.
SOM can also attenuate in waveguides.
First transverse HOM at ~1.8GHz, first longitudinal HOM at ~2.3GHz.
Property | Value
Operating frequency [GHz] | 1.300
1st longitudinal HOM [GHz] | 2.299
1st transverse HOM [GHz] | 1.765
Ep/Et with Et=Vt/(λ/2) | 3.24
Bp/Et [mT/(MV/m)] | 5.75
Bp/Ep [mT/(MV/m)] | 1.77
G [Ω] | 130.9
R/Q [Ω] | 454.3
RtRs [Ω2] | 59446

## Slide 12: Wide Open Waveguide 1.3 GHz B Xiao (BNL)
1.845 MV for 125 GeV case and 7.4 MV for 500 GeV required.
2 cavities for 125GeV (1.48MV/cavity) or 5 cavities for 500 GeV.
Considering to electrically short 1 WG to reduce the number of coax on each circular pipe from 3 to 2 (re: Jlab ERL-FEL scheme).
FPC Qe = 3 x 106, requires 850 W RF power.

## Slide 13
ILC Crab Cavity Aperture Limit: Ø25 mm
□ 54 mm
Ø25
SOM strongly coupled with WG-port, Qext < 5x103
HOM spectrum is sparse and loaded to a beam pipe
4 QMiR cavities can provide Vt ~ 4 MV for 1 TeV option
Freq | 2600 MHz
Vkick | 0.92 MV
(R/Q)t | 225 Ω
G-factor | 130
WSTORED | 0.24 J
Length | < 500 mm
HOM Transverse Impedance, Ω
Blue –horizontal, Red -vertical
Quasi-waveguide Multicell Resonator 2.6 GHz A Lunin/S Yakovlev (FNAL)
Two options are considered, a chain of 1x4 and 2x2 cavities
Simple stainless-steel inserts to damp HOMs
Ceramic BLA can be a backup if needed.

## Slide 14: Quasi-waveguide Multicell Resonator 2.6 GHz A Lunin/S Yakovlev (FNAL)
(R/Q)x < 8 Ω
(R/Q)y < 3 Ω
Dipole HOM
QL < 5E5
For max beam offset x0 < 1 mm and < 1 kHz (LFD, microphonics)
Beam OFF: ≈ 940 W, Optimal Coupling: QL ≈ 1x106
Beam ON & Microphonics: ≈ 1500 W
Required RF power from the generator (overhead 100%):
Pgen < 3 kW (FPC design is ongoing)
Option B
LFD < 1.5 kHz
dF/dP < 150 Hz
Expected frequency tuning range: ~ 2 MHz (1 MHz)

## Slide 15: Crab Cavity Parameters
Design teams to converge on consistent parameters

## Slide 16: Next Stage WP3 CC Preparations
For a future down-selection process:
Agree the criteria to develop for each of the CC designs:
  Cavity
  Couplers (input and HOM)
  Pressure stability and tuning
  Multipacting
  Fabrication (Sheet/Ingot/Mixed, Nb material required, readiness detail)
  Anything else (level of design detail expected (bare/dressed)
WP3 meeting proposed to review and agree criteria in Nov/Dec.
What’s left to complete for each of the design options currently?
What are the expected timescales to complete – try and agree/set today?
What alignment is needed with ILC IDT processes – timescales likely? (Spring 2023?)
Context for a proposed down-selection review:
  Terms of reference to be developed/agreed.
  Specialist membership – who defines/invites?
  IDT output anticipated and when?
(From WP3 Design Review #3 discussions)

## Slide 17: MANY THANKS Questions?