## Slide 1: ILC Racetrack Crab Design
Prof Graeme Burt, Lancaster University / Cockcroft Institute

## Slide 2: Re-optimizing the ILC crab
250 GeV ILC requires a 3-cell cavity @ 5 MV/m, or 2x2-cells at @4.2 MV/m
4 x 3 cells @5.5 MV/m or a 5x2 cells @6.5 MV/m at 1 TeV
Equator rounding radius
Iris rounding radius
Major radius
Minor radius

## Slide 3: 3 cell cavity
End cells initially had lower peak magnetic field
Larger beampipes were used on the end cells to aid damping (30 mm)
Slightly higher B field means that gradient is limited to 9.7 MV/m at 80 mT
Rt/Q=132 Ohms
E field
B field

## Slide 4: Multipactor
Multipactor band found at 7.15 MV/m on minor axis iris.
Required gradient is only 6.5 MV/m so this is acceptable
Appears very narrow band (not at 7 or 7.3 MV/m)

## Slide 5: Same order and lower order modes
Highest impedance SOM is the pi mode at 5.07 GHz, Rt/Q is only 50 Ohms/m due to frequency not being synchronous.
Highest impedance LOM is the pi/2 mode at 3.32 GHz, R/Q is only 134 Ohms
Trapped mode in the centre cell may be difficult to damp so may be a larger issue

## Slide 6: Mode spectrum
Chart: frequency (GHz)
| 3.2947454530215001 | 3.3277658063773998 | 3.3282601323800001 | 5.4963686737110997 | 5.5030095205866996 | 5.5233451905470003 | 7.5189353708204001 | 7.5242186758215999 | 7.6236508160097003 | 7.8620149393959 | 7.8622376449770002 | 7.9503114727013999 | 8.2496347573618998 | 8.2561764749975008 | 8.2827288922853999 | 8.2893219991227003 | 8.6986527158948999 | 9.1270278249775991 | 9.1274487276821006 | 9.1346555199794999 | 9.1905104769209007 | 9.4347461873236007 | 9.8060377017208999 | 9.8070122789745007 | 9.8470578197632008 | 10.284284067055999 | 10.31977977349 | 10.388045742558001 | 10.480868548935 | 10.544568147946
Rz/Q | 51.9097 | 27.1752 | 134.4311 | 0.63662 | 30.045 | 20.7315 | 1.2302 | 0.16051 | 0.63348 | 0.002649 | 0.34232 | 0.15678 | 2.0129 | 2.6571 | 0.090722 | 0.062851 | 0.0013648 | 0.084918 | 7.3541 | 0.03845 | 2.0581 | 0.016456 | 0.39973 | 0.01849 | 9.0625 | 1.7604 | 0.043365 | 1.2994 | 19.6128 | 0.2053
Rx/Q | 132.103 | 0.003744 | 0.12015 | 0.14218 | 9.3915 | 7.1132 | 2.3798 | 0.78922 | 0.45165 | 6.2465 | 8.8355 | 0.77229 | 0.005961 | 0.0054154 | 0.016224 | 1.7553 | 0.021771 | 0.74312 | 0.017951 | 0.92923 | 0.098568 | 0.73268 | 0.00092853 | 0.13586 | 0.089345 | 0.058574 | 0.082974 | 0.24725 | 0.0054949 | 0.091189
Ry/Q | 50.7726 | 39.3729 | 8.7964 | 3.0697 | 5.7587 | 0.72489 | 1.0137 | 0.20547 | 0.022409 | 1.5525 | 5.2843 | 1.5449 | 0.012274 | 0.0084011 | 0.50658 | 0.13459 | 0.21674 | 0.0057477 | 0.18365 | 0.010995 | 0.22932 | 0.53492 | 0.42315 | 0.0010742 | 0.001814 | 0.0060719 | 0.044789 | 0.032924 | 0.013768 | 0.00011027

## Slide 7: Waveguide damping
Waveguide damper does damp the pi and 0 modes well but doesn’t damp the pi/2 modes but these will be damped strongly by a coax damper in the beampipes.
Considering a waveguide section with a coax coupled to it to minimize size and heat leak.
Coax can be positioned to prevent coupling to the crabbing mode.
Good damping overall except one mode, unfortunately the highest impedance mode.

## Slide 8: Waveguide damper with coax antenna
Waveguide has a coax antenna positioned at the field null in the waveguide at 3.9 GHz but field maxima at 3 and 5 GHz to damp LOM and SOM
LOM Q is 25,000 and SOM Q is 3,500

## Slide 9: HOM coupler design
Modified version of old ILC HOM coupler, similar to ILC main linac coupler
Designed to have larger transmission at the LOM and SOM frequencies while filtering 3.9 GHz

## Slide 10: Impedance for waveguide damped 3 cell
The long. Impedance has no spec, the transverse impedance meets the spec except the other modes in the crabbing passband
The FPC may well damp these
ILC spec

## Slide 11: 2 cell cavity
A 2 cell cavity has no trapped mode so the on-cell waveguide damper is no longer required
LOM Q factor increases to 500,000 so depends what the spec is
SOM Q is 35-100 so not an issue.

## Slide 12: Lorentz force
Lorentz force is 4.6 kN/m^2 at 7 MV/m gradient which is fairly small
Equivalent to a 50 nm displacement
LF at 17 MV/m

## Slide 13: Conclusions
Multipactor limit is 7 MV/m so we have set the cavity gradient at <6.5 MV/m
Trapped LOM in the middle cell could be an issue with a 3 cell cavity, requiring on-cell damping. A waveguide with a coax antenna provides sufficient damping while rejecting the crabbing mode
To avoid an on-cell damper a 2 cell cavity can be used
Both designs meet the ILC specification except the 0 and pi/2 crabbing modes
The modes in the crabbing passband could be damped by the FPC which needs investigation.