## Slide 1: Sources Subgroup Summary IDT-WG2, Nov.29. 2022, K. Yokoya
Nov.21 33rd Regular meeting
  Joe Grames, Sabine Riemann, Spencer Gessner, Hitoshi Hayano, Andriy Ushakov, Sama Habet, Tsunehiko Omori, Yoshinori Enomoto, Amy Sy , Steffen Doebert , Mike Spata, Gudi Moortgat, Peter Sievers, Kaoru Yokoya
  Indico https://agenda.linearcollider.org/event/9874/
Talk
  “Novel Positron Source Development at SLAC”
    Spencer Gessner,
      New member of sources group
    File uploaded as Positron source concepts ILC IDT.pdf
Next meeting
  Presumably on Dec.12

## Slide 2: Positron PWFA
As a part of Spencer’s involvement on positron
PWFA for positron
  Only a small phase area for acceleration and focusing for positron
  Hollow plasma proposed to eliminate the transverse force
SLC positron target
FACET II Positrons
  Positron PWFA experiments at FACET in the past
    Non-linear regime, two bunch acceleration
  Hollow plasma created
S. Gessner et. al. Nat. Comm. 7, 11785 (2016)

## Slide 3: Liquid Xenon Target
Metal targets degrade over time
Liquid metal targets can be used but they are toxic (e.g., mercury)
Liquid xenon
  Non-toxic, high density
  Max. PEDD ~ 100 J/g (3x solid target)
  LXe temperature 161 K
  e+ yield cpmparable to solid target with the same radiation length
  Can be used for e-driven ILC positron source
    GEANT simulation: max. PEDD/train = 84 J/g
    Required flow rate 0.073 L/s
Issues
  Energy deposit in the beryllium at exit side
  Robustness and cost effectiveness

## Slide 4: Compact Positron Source
Compact positron sources for non-HEP applications
A Penning-Malmberg trap is used to accumulate and cool positrons from a radioactive source.
  The positrons are naturally polarized because they are produced by 𝛽-decays from the 22Na source
  A buffer gas to cool the positrons.
  The intrinsic emittance is proportional to positron temperature in the trap.
    Possible to reach 100 nm-scale emittance at room temperature.
  The beam is “magnetized” because the cooling occurs in a solenoid ﬁeld.
    Naturally gives ﬂat-beam emittance (Round-to-Flat Transformation, Brinkmann-Derbenev-Floettmann)
Issues
  Higher intensity (only107 e+/s from 22Na)
  Can polarized bremsstrahlung (PEPPo at JLABbe used?