## Slide 1: C3: What is to be done?
Emilio Nanni & Caterina Vernieri
IDT WG3 Update
6/8/2023

## Slide 2
Greetings from LCWS 2023!

## Slide 3: Outline
1. Brief Review of C3 Concept
2. Outstanding Technological Issues for the Accelerator
3. Demo Program
4. New Accelerator Results at LCWS
5. Comments Detectors from LCWS
7. Conclusion

## Slide 4: Acknowledgements
ILC Update
Additional Contributors
Mitchell Schneider
Charlotte Whener
Gordon Bowden
Andy Haase
Julian Merrick
Bob Conley
Radiabeam
Cici Hanna
More Details Here (Follow, Endorse, Collaborate):
https://indico.slac.stanford.edu/event/7155/

## Slide 5: C3 Cool Copper Collider
Snowmass
C3 is based on a new rf technology
  Dramatically improving efficiency and breakdown rate
Distributed power to each cavity from a common RF manifold
Operation at cryogenic temperatures (LN2 ~80-K)
Robust operations at high gradient: 120 MeV/m
Scalable to multi-TeV operation
High Gradient Operation at 150 MV/m
Cryogenic Operation at X-band
C3 Prototype One Meter Structure
High power Test at Radiabeam (C-band)

## Slide 6: Tunnel Layout for Main Linac 250/550 GeV CoM
ILC Update
Need to optimize tunnel layout – first study looked at 9.5 m inner diameter in order to match ILC costing model
Must minimize diameter to reduce cost and construction time
Surface site (cut/cover) provides interesting alternative – concerns with length of site for future upgrade
Usable Tunnel Width - 9.5 m
(Same tunnel width as ILC)
Cryomodule Unit - 9 m
(630 MeV/1 GeV )

## Slide 7: Accelerator Complex
Snowmass
8 km footprint for 250/550 GeV CoM ⟹ 70/120 MeV/m
7 km footprint at 155 MeV/m for 550 GeV CoM – present Fermilab site
Large portions of accelerator complex compatible between LC technologies
Beam delivery / IP modified from ILC (1.5 km for 550 GeV CoM)
Compatible w/ ILC-like detector
Damping rings and injectors to be optimized with CLIC as baseline
C3 Parameters
C3 - 8 km Footprint for 250/550 GeV

## Slide 8: Technical Timeline for 250/550 GeV CoM
ILC Update
Technically limited timeline developed through the Snowmass process
Energy upgrade in parallel to operation with installation of additional RF power sources
Notes: Run plan to match ILC at 250, we remain open to input -> Higher energy faster, push harder for luminosity

## Slide 9: Accelerator Design and Challenges
ILC Update
Cryomodule Concept
Vibration
Studies
Accelerator Design
Engineering and design of prototype cryomodule underway
Focused on challenges identified with community through Snowmass (all underway)
Gradient – Scaling up to meter scale cryogenic tests
Vibrations – Measurements with full thermal load
Alignment – Working towards raft prototype
Cryogenics – Two-phase flow simulations to full flow tests
Damping – Materials, design and simulation
Beam Loading and Stability - Thermionic beam test
Scalability – Cryomodules and integration
Notes: Stay a SLAC for LCWS for detailed information

## Slide 10: C3 Demonstration R&D Plan
ILC Update
C3 demonstration R&D needed to advance technology beyond CDR level
Minimum requirement for Demonstration R&D Plan:
Demonstrate operation of fully engineered and operational cryomodule
  Simultaneous operations of min. 3 cryomodules
Demonstrate operation during cryogenic flow equivalent to main linac at full liquid/gas flow rate
Operation with a multi-bunch photo injector - high charges bunches to induce wakes, tunable delay witness bunch to measure wakes
Demonstrate full operational gradient 120 MeV/m (and higher > 155 MeV/m) w/ single bunch
  Must understand margins for 120 - targeting power for (155 + margin) 170 MeV/m
  18X 50 MW C-band sources - off the shelf units
Fully damped-detuned accelerating structure
Work with industry to develop C-band source unit optimized for installation with main linac
This demonstration directly benefits development of compact FELs, beam dynamics, high brightness guns, etc.
The other elements needed for a linear collider - the sources, damping rings, and beam delivery system – more advanced from the ILC and CLIC – need C3 specific design
Our current baseline uses these directly; will look for further cost-optimizations for of C3

## Slide 11: The Complete C3 Demonstrator
ILC Update
Demonstrate fully engineered cryomodule
~50 m scale facility
3 GeV energy reach
Answer technical questions needed for CDR

## Slide 12: C3 Demonstration R&D Plan
ILC Update
F. Wang, NCRF W 17th May 8:30
J. Wu, BD Th 18th May 16:30
A. Krasnykh, BD W 17th May 11:20
Demo Plan
High Power RF Distribution
Demo Beam Dynamics

## Slide 13: Power Consumption and Sustainability
250 GeV CoM - Luminosity - 1.3x1034
Parameter | Units | Value
Reliquification Plant Cost | M$/MW | 18
Single Beam Power (125 GeV linac) | MW | 2
Total Beam Power | MW | 4
Total RF Power | MW | 18
Heat Load at Cryogenic Temperature | MW | 9
Electrical Power for RF | MW | 40
Cryoplant Electrical Power | MW | 60
Accelerator Complex Power | MW | ~50
Site Power | MW | ~150
Temperature (K) | 77
Beam Loading (%) | 45
Gradient (MeV/m) | 70
Flat Top Pulse Length (𝜇s) | 0.7
Cryogenic Load (MW) | 9
Main Linac Electrical Load (MW) | 100
Site Power (MW) | ~150
Linac Parameters
Sustainability - construction + operations CO2 emissions per % sensitivity on couplings
  Polarization and high energy to improve sensitivity
  Construction CO2 emissions → minimize excavation and concrete
  Operations → limit power, decarbonization of the grid and dedicated renewable sources
B. Bullard, S&A Th 18th May 10:30
Surface Tunnel
10 m
6.6 m
Notes: Sustainability lcws talk and paper

## Slide 14: RF Design to High Gradient and High Power Testing
ILC Update
High gradient testing at LANL
Single cell structures
Up to 8 MW per cavity (>240 MeV/m)
~190 MeV/m
Appl. Phys. Lett. 121, 254101 (2022); doi: 10.1063/5.0132706
High power testing at Radiabeam
Meter scale structures and components
~22 MW delivered in bunker -> 50 MW upgrade in progress
Additive Spiral Load (Inspired by CLIC)
One Meter Structure
Notes: Stay a SLAC for LCWS for detailed information

## Slide 15: Alignment and Vibrations
System level optimization essential for achieving performance
ILC Update
RF Structure Optimization
Main Linac Beam Dynamics
Vibration Analysis
Two-Phase Fluid Simulations
Precision Short and Long Range Alignment
3.55 mm iris radius
2.0=Emax/Eacc
1.23=Hcoup/Hwall
White (C3), Schulte (CLIC)
Alignment Parameters | Units | Value
Raft Components | μm | 5
Short Range (~10m) | μm | 30
Long Range (>200m) | μm | 1000
Structure Vert. Vibration | μm | 9
Quad Vert. Vibration | nm | 15
BPM Resolution | μm | 0.1
BPM-Quad Alignment | μm | 2
Electric Field
Magnetic Field
M. Shumail, Z. Li
K. Shoele
H. Van Der Graaf
Z. George, V. Borzenets
100 nm resolution
Approved effort to test cold
H. van der Graaf, CF W 17th May 14:30
Z. Li, NCRF W 17th May 10:30
G. White, Beam Dynamics W 17th May 10:30

## Slide 16: RF Power Requirements and Cryogenics
ILC Update
70 MeV/m 250 ns Flattop (extendible to 700 ns)
~1 microsecond rf pulse, ~30 MW/m
2.3X enhancement from cryo
No pulse compression
Ramp power to reduce reflected power
Flip phase at output to reduce thermals
<2.5 kW/m of structure for C3-250/550
15% cooling efficiency with LN
Gradient
Thermals
RF Power
M. Breidenbach, CF W 17th May 14:15

## Slide 17: Gaussian Detuning Provides Required 1st Band Dipole Suppression for Subsequent Bunch, Damping Also Needed
ILC Update
Dipole mode wakefields immediate concern for bunch train
4𝜎 Gaussian detuning of 80 cells for dipole mode (1st band) at 𝑓𝑐=9.5 GHz, w/ ∆𝑓/𝑓𝑐=5.6%
First subsequent bunch s = 1m, full train ~75 m in length
Damping needed to suppress re-coherence

## Slide 18: Distributed Coupling Structures Provide Natural Path to Implement Detuning and Damping of Higher Order Modes
ILC Update
Individual cell feeds necessitate adoption of split-block assembly
Perturbation due to joint does not couple to accelerating mode
Exploring gaps in quadrature to damp higher order mode
Detuned Cavity Designs
Quadrant Structure

## Slide 19: Implementation of Slot Damping
ILC Update
Need to extend to 40 GHz / Optimize coupling / Modes below 104 V/pC/mm/m
NiCr coated damping slots in development
Tapered Slot
Kick Factor
Vacuum Space Model
Kick Factor * Q
Two Cell Prototype
H. Xu, NCRF W 17th May 13:30
NiCr Tested at 80K

## Slide 20: Upgrade Options
Snowmass
Cryogenics Scale to multi-TeV
Parameter | Units | Baseline | High-Lumi
Energy CoM | GeV | 250 | 250
Gradient | MeV/m | 70 | 70
Beam Current | A | 0.2 | 1.6
Beam Power | MW | 2 | 16
Luminosity | x1034 | 1.3 | 10.4
Beam Loading |  | 45% | 87%
RF Power | MW/m | 30 | 125
Site Power | MW | ~150 | ~180
Caution: Requires serious investigation of beam dynamics - great topic for C3 Demonstration R&D
Luminosity
Energy
arXiv:1807.10195 (2018)
HTS Pulse Compressor
REBCO Coatings
Le Sage, CERN Collaborators
Qo ~ 400k
Beam power can be increased for additional luminosity
C3 has a relatively low current for 250 GeV CoM (0.19 A) - Could we push to match CLIC at 1.66 A? (8.5X increase?)
Pulse length and rep. rate are also options
Scalability studied to 3 TeV
Requires rf pulse compression for reasonable site power
Higher gradient option (155 MeV/m) in consideration
G. Le Sage, S&A Th 18th May 11:30

## Slide 21: Detector R&D topics
Some of the R&D topics emerged during LCWS
Precise timing
  For PID (10-50ps)
  For improved tracking (ns) with MAPS
  For Calorimetry PF
Highly integrated sensors MAPS for tracking and calorimetry
Different PID approaches
  i.e. gaseous compact RICH
Smart sensors/ASICs
Better and modern software frameworks
  Simulation and Reconstruction, leveraging LHC expertise

## Slide 22: ILC Update Program Related to C3
ILC Update
ID | Title | Date | Session | Track | Presenters | Email
3 | Distributed Coupling Linac for Efficient Acceleration of High Charge Electron Bunches | 17 May 2023, 11:00 | Accelerator: Normal Conducting RF | Normal Conducting RF | Ankur Dhar | adhar@slac.stanford.edu
4 | Physics with the XFEL Compton γγ Collider (XCC) Higgs Factory | 17 May 2023, 13:30 | Physics and Detectors: Track 1 | Track 1: Physics at e+e- colliders | Timothy Barklow | timb@slac.stanford.edu
6 | C3 | 15 May 2023, 10:30 | Joint Plenary | Joint | Caterina Vernieri | caterina@slac.stanford.edu
13 | A design of the C-band RF photoinjector cavity for testing photocathodes under extreme fields | 17 May 2023, 14:40 | Accelerator: Normal Conducting RF | Normal Conducting RF | Haoran Xu | haoranxu@lanl.gov
14 | Two-cell high-gradient C-band RF accelerator cavity for high power HOM absorber testing | 17 May 2023, 11:20 | Accelerator: Normal Conducting RF | Normal Conducting RF | Haoran Xu | haoranxu@lanl.gov
20 | C3 Main Linac Beam Dynamics | 17 May 2023, 10:30 | Accelerator: Beam Dynamics | Beam Dynamics | Glen White | whitegr@slac.stanford.edu
21 | C3 demonstration plan and applications | 17 May 2023, 08:30 | Accelerator: Normal Conducting RF | Normal Conducting RF | Faya Wang | fywang@slac.stanford.edu
28 | RF sources and power distribution for the C3-demo and beyong | 17 May 2023, 13:30 | Accelerator: Normal Conducting RF | Normal Conducting RF | Anatoly Krasnykh | krasnykh@slac.stanford.edu
30 | Cryogenic Design for C3 Main Linacs | 17 May 2023, 14:15 | Accelerator: Conventional Facilities | Conventional Facilities | Martin Breidenbach | mib@slac.stanford.edu
31 | A nanosecond pulse technology for injection/extraction systems | 17 May 2023, 16:10 | Accelerator: Beam Dynamics | Normal Conducting RF | Anatoly Krasnykh | krasnykh@slac.stanford.edu
41 | C-Band Distributed Coupling Structure Design and Wakefield Damping | 17 May 2023, 10:30 | Accelerator: Normal Conducting RF | Normal Conducting RF | Zenghai Li | lizh@slac.stanford.edu
46 | Pair Production and Hadron Photoproduction Backgrounds at C3 | 18 May 2023, 13:30 | Physics and Detectors: Track 2 | Track 2: Analysis and Reconstruction | Elias Mettner | emettner@wisc.edu
47 | Muon Backgrounds from Beam Interactions with the Accelerator Structure at C3 | 18 May 2023, 13:45 | Physics and Detectors: Track 2 | Track 2: Analysis and Reconstruction | Dimitris Ntounis | dntounis@stanford.edu
51 | High Temperature Superconducting RF cavity | 18 May 2023, 11:30 | Accelerator: Sustainability & Applications | Sustainability and Applications | Gregory Le Sage | lesage@slac.stanford.edu
52 | Sustainability studies for the Cool Copper Collider | 18 May 2023, 10:30 | Accelerator: Sustainability & Applications | Sustainability and Applications | Brendon Bullard | bbullard@slac.stanford.edu
55 | Rasnik as alignment system for linac submodules | 17 May 2023, 14:30 | Accelerator: Conventional Facilities | Conventional Facilities | Harry van der Graaf | vdgraaf@nikhef.nl
88 | Cool Copper Collider Demonstrator Beam Dynamics and Diagnostics | 18 May 2023, 15:30 | Accelerator: Beam Dynamics | Beam Dynamics | Juhao Wu | jhwu@slac.stanford.edu
111 | An Integrated Simulation Tool for Dark Current Radiation Effects using ACE3P and Geant4 | 17 May 2023, 16:00 | Accelerator: Normal Conducting RF | Normal Conducting RF | Lixin Ge | lge@slac.stanford.edu
120 | Application of CrYogenic Brightness-Optimized Radiofrequency Gun (CYBGORG) for Future Collider Studies | 17 May 2023, 14:20 | Accelerator: Normal Conducting RF | Normal Conducting RF | Gerard Lawler | gelawler@protonmail.com
207 | Wakefield Damping in a Distributed Coupling Accelerating Structure for CLIC | 17 May 2023, 16:30 | Accelerator: Normal Conducting RF | Normal Conducting RF | Evan Ericson | eje344@mail.usask.ca

## Slide 23: Conclusions
ILC Update
C3 provides a rapid route to precision Higgs physics with a compact 8 km footprint
  Higgs physics run by 2040
  US-hosted facility possible
C3 time structure is compatible with ILC-like detector design and optimizations ongoing
C3 upgrade to 550 GeV with only added rf sources
  Higgs self-coupling and expanded physics reach
C3 is scalable to multi-TeV
C3 Demo advances technology beyond CDR level
  5 year program, followed by completion of TDR and industrialization
  Three stages with quantitative metrics and milestones for decision points
  Direct and synergistic contributions to near-term collider concepts
More Details Here (Follow, Endorse, Collaborate):
https://indico.slac.stanford.edu/event/7155/

## Slide 24: Questions?

## Slide 25: Additional Material

## Slide 26: Synergies with Future Colliders
RF Accelerator Technology Essential for All Near-Term Collider Concepts
C3 Demo is positioned to contribute synergistically or directly to all near-term collider concepts
CLIC - components, damping, fabrication techniques
ILC - options for electron driven positron source based C3 technology
Muon Collider - high gradient cryogenic copper cavities in cooling channel, alternative linac for acceleration after cooling
AAC - C3 Demo utilized for staging, C3 facility multi-TeV energy upgrade reutilizing tunnel, 𝛾𝛾 colliders
FCC-ee - common electron and positron injector linac from 6 to 20 GeV
  reduce length 3.5X OR reduce rf power 3.5X
ILC Update
90% seeds < 8 um-rad with lattice errors
Planned test at Argonne
Tracking with Lucretia includes longitudinal and transverse wakes, chromatic effects etc
Error study is 100 seeds, 100 μm element offsets, 300 μrad element rolls (rms)
  No corrections applied

## Slide 27: Further Cavity Optimization Possible
ILC Update
Dipole
with symmetrization 100X reduction
V1-simple-stub
(not ideal cancellation)
V2-symm-stub
(good cancellation)
Single side coupling iris induces dipole and quad fields
Coupling hole symmetrization and racetrack shape incorporated to minimize dipole and quad fields
Dipole
Quad
Quad
w/o symmetrization
✅
dipole, quad calculated at 50MV/m
Zenghai Li

## Slide 28: Global Contributions
C3 Technical Timeline Only Possible with the Exceptional Progress of ILC and CLIC
Benefit from injector complex and beam delivery concepts
Continue to benefit from technological improvement by ILC and CLIC
ILC Update
Vibrant International Community for Future Colliders is Essential
High Efficiency RF Sources (CLIC)
I. Sarchev, CERN
Electron Driven Positron Source
Nanobeams for IP (ATF)
https://www-atf.kek.jp/atf/
Courtesy of Y. Enomoto

## Slide 29: Full Parameters
ILC Update

## Slide 30: Cryomodule Design and Alignment
ILC Update
Up to 1 GeV of acceleration per 9 m cryomodule; ~90% fill factor with eight 1 m structures
Main linac will require 5 micron structure alignment
Combination of mechanical and beam based alignment
Pre-alignment warm, cold alignment by wire, followed by beam based
Mechanical motor runs warm or cold – no motion during power failure
Piezo for active alignment
Investigating support and assembly design
Cryomodule Cross Section
Cryomodule

## Slide 31: Requirements for a High Energy e+e- Linear Collider
ILC Update
Using established collider designs to inform initial parameters
Quantifying impact of wakes requires detailed studies
Most important terms – aperture, bunch charge (and their scaling with frequency)
Target initial stage design at 250 GeV CoM
2 MW single beam power
Luminosity
Beam Power
https://clic-meeting.web.cern.ch/clic-meeting/clictable2010.html
NLC, ZDR Tbl. 1.3,8.3
Machine | CLIC | NLC | C3
Freq (GHz) | 12.0 | 11.4 | 5.7
a (mm) | 2.75 | 3.9 | 2.6
Charge (nC) | 0.6 | 1.4 | 1
Spacing (𝜆) | 6 | 16 | 30/20
# of bunches | 312 | 90 | 133/75

## Slide 32: Breakthrough in the Performance of RF Accelerators
ILC Update
RF power coupled to each cell – no on-axis coupling
Full system design requires modern virtual prototyping
Electric field magnitude produced when RF manifold feeds alternating cells equally
Optimization of cell for efficiency (shunt impedance)
Control peak surface electric and magnetic fields
Key to high gradient operation
Tantawi, Sami, et al. PRAB 23.9 (2020): 092001.

## Slide 33: Cryo-Copper: Enabling Efficient High-Gradient Operation
ILC Update
Cryogenic temperature elevates performance in gradient
Material strength is key factor
Impact of high fields for a high brightness injector may eliminate need for one damping ring
Operation at 77 K with liquid nitrogen is simple and practical
Large-scale production, large heat capacity, simple handling
Small impact on electrical efficiency
Cahill, A. D., et al. PRAB 21.10 (2018): 102002.
Cryogenic temperature elevates performance in gradient
Increased material strength is key factor
Increase electrical conductivity reduces pulsed heating in the material

## Slide 34: Beam Format and Detector Design Requirements
ILC Update
ILC timing structure: Fraction of a percent duty cycle
Power pulsing possible, significantly reduce heat load
  Factor of 50-100 power saving for FE analog power
Tracking detectors don’t need active cooling
  Significantly reduction for the material budget
Triggerless readout is the baseline
C3 time structure is compatible with ILC-like detector overall design and ongoing optimizations
1 ms long bunch trains at 5 Hz
2820 bunches per train
308ns spacing
ILC timing structure
C3 timing structure

## Slide 35: Why 550 GeV?
ILC Update
We propose 250 GeV with a relatively inexpensive upgrade to 550 GeV
An orthogonal dataset at 550 GeV to cross-check a deviation from the SM predictions observed at 250 GeV
From 500 to 550 GeV a factor 2 improvement to the top-Yukawa coupling
O(20%) precision on the Higgs self-coupling would allow to exclude/demonstrate at 5𝜎 models of electroweak baryogenesis

## Slide 36: One note on polarization
ILC Update
There are extensive comparisons between the FCC-ee plan and the C3/ILC runs that show they are rather compatible to study the Higgs Boson
When analyzing Higgs couplings with SMEFT, 2 ab-1 of polarized running is essentially equivalent to 5 ab-1 of unpolarized running.
  Electron polarization is essential for this. But, there is almost no difference in the expectation with and without positron polarization.
  Positron polarization allows more cross-checks of systematic errors. We may wish to add it later.
  Positron polarization brings a large advantage in multi-TeV running, where the most important cross sections are from e-Le+R
arXiv:1708.08912
arXiv:1801.02840

## Slide 37: Implementation of Slot Damping
ILC Update
Need to extend to 40 GHz / Optimize coupling / Modes below 104 V/pC/mm/m
NiCr coated damping slots in development
Tapered Slot
Kick Factor
Vacuum Space Model
Kick Factor * Q
Damping Slot Prototype

## Slide 38: Accelerator Complex
ILC Update
8 km footprint for 250/550 GeV CoM ⟹ 70/120 MeV/m
7 km footprint at 155 MeV/m for 550 GeV CoM – present Fermilab site
Large portions of accelerator complex compatible between LC technologies
Beam delivery / IP modified from ILC (1.5 km for 550 GeV CoM)
Compatible w/ ILC-like detector
Damping rings and injectors to be optimized with CLIC as baseline
C3 - 8 km Footprint for 250/550 GeV
G. White, Beam Dynamics W 17th May 10:30
A. Krasnykh, Beam Dynamics W 17th May 16:10
DR Kickers
Alignment and DFS Studies

## Slide 39: Table of Parameters
ILC Update